## Slide 1: Performance Evaluation of Edge-Based Smoothed Finite Element Method for 4-node Tetrahedral Meshes on Electrodeposition Simulation
Kai KITAMURA(1), Yuki ONISHI(1), Takeshi KASHIYAMA(2),
Kenji AMAYA(1)
(1) Tokyo Institute of Technology (Japan)
(2) SUZUKI MOTOR CORPORATION (Japan)

## Slide 2: What is electrodeposition (ED) ?
Most widely-used basecoat methods for car bodies.
Making coating film by applying direct electric current in a paint pool.
Relatively good at making uniform film thickness but not satisfactory uniform in actual production lines.
ED simulator is necessary for the optimization of carbody design and coating conditions in actual lines.
+
-
Cathode
Anode
Paint
＋
＋
http://n-link.nissan.co.jp/NOM/PLANT/

## Slide 3: Photos of ED process line
1. dipping and deposition process
2. water rinse process
3. baking process
We focus on this process.

## Slide 4: Mechanism of Electrodeposition
Positively charged paint ions are attracted to the cathode.
Paint ions gradually lose their electrical charge and are aggregated into paint particles.
Some of the paint particles diffuse and dissolve.
-
+
+
-
Paint Ions
Carbody
（Cathode)
-
-
+
Deposition
Aggregated into paint particles
When the particle gets big enough
Voltage is applied
Coating
Film
Electrophoresis

## Slide 5: What is ED Simulation ?
ED simulation provides film thickness, surface potential, surface current density and so on.
Film Thickness
Surface Potential
Surface Current Density
You can see that the paint film starts to be deposited from the outside surface.

## Slide 6: How to Develop an ED Simulator
Experiments at lab in various coating conditions.
Identification of ED boundary model and its parameters.
Implementation to a FE code.
One-Plate Test
ED simulation for actual lines
Plate
Paint
On the analogy of solid mechanics,
Step 1: material tests with MTS, Step 2: identification of elastoplastic model.
DELIGHT web page, https://delightcfd.com

## Slide 7: Issues in Meshing (1)
✗ It is difficult to discretize complex shapes such as car bodies with hexahedral meshes.
→ We have to use tetrahedral meshes in ED simulation.
However…
Only surface
mesh is shown.

✗
Accuracy of the standard FEM-T4 is insufficient in complex shapes.

## Slide 8: Issues in Meshing (2)
✗ 10-node tetrahedral (T10) mesh without kink generally requires more large number of nodes than T4 mesh.
T4 T10 without kink
For the same shape representation, T10 mesh without kink leads to massive increase in DOF.
Carbody
Carbody
hole
hole

## Slide 9: Issues in Meshing (2) Cont.
✗ 10-node tetrahedral (T10) mesh with kink causes severe accuracy loss.
T4 T10 with kink
T10 mesh with kink does not increase DOF but induces severe accuracy loss.
Carbody
Carbody
hole
hole
Kinked T10

## Slide 10: Motivation
Hexahedral elements: ✗ It is difficult to discretize complex shapes.
T10 elements without kink: ✗ It leads to massive increase in DOF.
T10 elements with kink: ✗ It causes severe accuracy loss.
→ We want to realize high accuracy analysis with T4 mesh.
ES-FEM-T4 could be a solution to these issues.

## Slide 11: Objective
Table of body contents:
Outline of ED Simulation
Formulation of ES-FEM for ED Simulation
Analysis Results
Development of ED simulator using ES-FEM-T4 and its performance evaluation by comparing with FEM-T4.

## Slide 12: Outline of ED Simulation

## Slide 13: Fundamental Equations
Governing equation
The electrostatic Laplace equation in the paint pool domain.
Boundary conditions (BCs)
Insulation BC
Anodic (Electrode surface) BC
Cathodic (Carbody surface) BC
ED boundary models are identified with experimental data at a laboratory.
Solving the Laplace equation for potential, the current density distribution on a carbody is determined and then the film thickness distribution is time-evolutionally calculated.
+
-
Cathode
Anode
Paint
＋
＋

## Slide 14: How to Identify ED Boundary Models
1. Conduct a lab experiment called one-plate tests.
Plot
Data fitting
2. Obtain Scatter diagram. e.g.) .
3. Generate approximated surface for each ED Boundary Model.

## Slide 15: Formulation of ES-FEM for ED Simulation

## Slide 16: Outline of ES-FEM
What is ES-FEM-T4?
A kind of strain smoothing method.
Using element edges as Gauss points.
Robust against element skew.
Super-linear mesh convergence rate with T4 mesh.
ES-FEM can suppress the accuracy loss by smoothing.
Standard FEM ES-FEM
Integration domain
Element
Node
FEM assembles each element’s value.
ES-FEM assembles each edge’s value.
Integration domain is different !!

## Slide 17: Analysis Results

## Slide 18: 4-Plate BOX Simulation
Outline
Imitating a bag-like structure such as side sill in a carbody.
Accuracy on the innermost surface (leftmost plate surface) is the most important; i.e., “maximize the minimum”.
Film thickness is calculated with 4 different mesh seed sizes and compared between FEM-T4 and ES-FEM-T4.
Film Thickness
(http://plaza.rakuten.co.jp/heroc)
Side Sill
4-P BOX

## Slide 19: 4-Plate BOX Simulation
Overview of Meshes
3.2 mm Mesh Seed Size (31k T4 elem.)
0.8 mm Mesh Seed Size (169k T4 elem.)
1.6 mm Mesh Seed Size (65k T4 elem.)
0.4 mm Mesh Seed Size (716k T4 elem.)
Only the surface meshes are shown.

## Slide 20: 4-Plate BOX Simulation
Film Thickness on G-Plate (innermost surface)
Mesh seed size
FEM results (dashed lines) have large errors due to mesh coarseness. Meanwhile, ES-FEM (solid lines) results have no such errors.

## Slide 21: 4-Plate BOX Simulation
Comparison of Convergence Rate on G-Plate
FEM-T4 shows a linear convergence. Meanwhile, ES-FEM-T4 almost shows a quadratic convergence.
ES-FEM-T4 has much better mesh convergence rate than FEM-T4.
The result of ES-FEM with the minimum mesh seed size (0.4 mm) is used as the reference.

## Slide 22: Carbody Simulation
Outline
A half carbody is fixed in a box pool.
The side wall is treated as an anode surface.
270 V
0 30 180 (s)
Applied Voltage

## Slide 23: Carbody Simulation
Overview of Surface Mesh with 10M Elems.
Compare the time-developed film thickness between FEM-T4 and ES-FEM-T4 with 3 different size meshes.
Each mesh has 10M, 16M and 50M T4 elements.

## Slide 24: Carbody Simulation
Overview of Surface Mesh with 16M Elems.
Compare the time-developed film thickness between FEM-T4 and ES-FEM-T4 with 3 different size meshes.
Each mesh has 10M, 16M and 50M T4 elements.

## Slide 25: Carbody Simulation
Overview of Surface Mesh with 50M Elems.
Compare the time-developed film thickness between FEM-T4 and ES-FEM-T4 with 3 different size meshes.
Each mesh has 10M, 16M and 50M T4 elements.

## Slide 26: Carbody Simulation
Zoom in View around a Hole on Carbody
Compare the time-developed film thickness between FEM-T4 and ES-FEM-T4 with 3 different size meshes.
Each mesh has 10M, 16M and 50M T4 elements.
10M
16M
50M

## Slide 27: Carbody Simulation
Overview results of Film Thickness Distribution
Outer View
Inner View
The results of ES-FEM with 50M elements. (Reference results)

## Slide 28: Carbody Simulation
Film Thickness Distribution with 10M Elems. Mesh
(Clipped View on Side Sill)
FEM-T4
ES-FEM-T4
FEM-T4 requires 50M elements to obtain the converged solution. Meanwhile, ES-FEM-T4 requires only 16M elements.

## Slide 29: Carbody Simulation
Film Thickness Distribution with 16M Elems. Mesh
(Clipped View on Side Sill)
FEM-T4
ES-FEM-T4
FEM-T4 requires 50M elements to obtain the converged solution. Meanwhile, ES-FEM-T4 requires only 16M elements.

## Slide 30: Carbody Simulation
Film Thickness Distribution with 50M Elems. Mesh
(Clipped View on Side Sill)
FEM-T4
ES-FEM-T4
FEM-T4 requires 50M elements to obtain the converged solution. Meanwhile, ES-FEM-T4 requires only 16M elements.

## Slide 31: Carbody Simulation
Film Thickness Distribution with 50M Elems. Mesh
(Clipped View on Side Sill)
FEM-T4
ES-FEM-T4
FEM-T4 requires 50M elements to obtain the converged solution. Meanwhile, ES-FEM-T4 requires only 16M elements.

## Slide 32: Carbody Simulation
Comparison of Time-histories of Film Thickness
FEM-T4 with 50M elems. and ES-FEM-T4 with 10M elems. show almost the same results.

## Slide 33: Comparison of Computational Costs
Calculation Time
on a PC with Intel i9-9960X using 8 cores
 | Mesh / Elements | FEM-T4 | ES-FEM-T4
4-P BOX | 3.2 mm | 0.3 min | 0.5 min
 | 1.6 mm | 0.5 min | 0.9 min
 | 0.8 mm | 1.2 min | 2.4 min
 | 0.4 mm | 6.3 min | 12.2 min
Carbody | 10M Elements | 1.5 h | 3.0 h
 | 16M Elements | 2.4 h | 4.7 h
 | 50M Elements | 6.9 h | 15.4 h
Same Accuracy
Same Accuracy
There is no big difference in calculation time although the accuracy of ES-FEM-T4 is much better.

## Slide 34: Summary

## Slide 35: Summary
Conclusion
ES-FEM-T4 was applied to actual ED simulations.
High accuracy of ES-FEM-T4 because of its super-linear (almost quadratic) mesh convergence rate was confirmed in comparison to the poor accuracy of FEM-T4.
Future Works
Validation of the ED models on the actual manufacturing lines.
Calculation speed-up with distributed memory parallelization.
Thank you for your kind attention.