## Slide 1: SelectiveCS-FEM-T10: Selective cell-based smoothed finite element methods with 10-node tetrahedral elements
Yuki ONISHI Tokyo Institute of Technology, Japan

## Slide 2: What is S-FEM?
Smoothed finite element method (S-FEM) is a relatively new FE formulation proposed by Prof. G. R. Liu in 2006.
S-FEM is one of the strain smoothing techniques.
There are several types of classical S-FEMs depending on the domains of strain smoothing.
For example in 2D triangular mesh:
Standard FEM
Edge-based S-FEM (ES-FEM)
Node-based S-FEM (NS-FEM)

## Slide 3: How popular is S-FEM?
Number of journal papers written in English whose title contains “smoothed finite element”:
(inquired at Google Scholar)
The attraction of S-FEM is expanding continuously.

## Slide 4: Applications of S-FEMs in Our Lab
Solid mechanics
Static Implicit Dynamic Explicit Viscous Implicit
Electrostatic

## Slide 5: Motivation
What we want to do:
Solve hyper large deformation analyses accurately and stably.
Treat complex geometries with tetrahedral meshes.
Consider nearly incompressible materials .
Support contact problems.
Handle auto re-meshing.
Rubber
Plastic/Glass
Metal

## Slide 6: Issues
Conventional tetrahedral (T4/T10) FE formulations still have issues in accuracy or stability especially in nearly incompressible cases.
2nd or higher order elements: ✗ Volumetric locking. Accuracy loss in large strain due to intermediate nodes.
B-bar method, F-bar method, Selective reduced integration: ✗ Not applicable to tetrahedral element directly.
F-bar-Patch method: ✗ Difficulty in building good-quality patches.
u/p mixed (hybrid) method: (e.g., ABAQUS/Standard C3D4H and C3D10MH) ✗ Pressure checkerboarding, Early convergence failure etc..
F-bar type smoothed FEM (F-barES-FEM-T4):  Accurate & stable ✗ Hard to implement in FEM codes.

## Slide 7: Issues (cont.)
E.g.) Compression of neo-Hookean hyperelastic body with
1st order hybrid T4 (C3D4H)
 No volumetric locking
✗ Pressure checkerboarding
✗ Shear & corner locking
2nd order modified hybrid T10 (C3D10MH)
 No shear/volumetric locking ✗ Early convergence failure
✗ Low interpolation accuracy
# of Nodes is almost the same.
Pressure
Pressure

## Slide 8: Issues (cont.)
E.g.) Compression of neo-Hookean hyperelastic body with
Same mesh as C3D4H case.
Pressure
Although F-barES-FEM-T4 is accurate and stable, ✗ it cannot be implemented in general-purpose FE software due to the adoption of ES-FEM.
Also, it cosumes larger memory & CPU costs.
Another approach adopting CS-FEM with T10 element would be effective.
F-barES-FEM-T4  No shear/volumetric locking
 No corner locking  No pressure checkerboarding
 No increase in DOF

## Slide 9: Objective
To develop an S-FEM formulation using T10 mesh (SelectiveCS-FEM-T10) for severe large deformation analyses.
Table of Body Contents
Quick introduction of F-barES-FEM-T4 Why not T4 but T10?
Formulation of SelectiveCS-FEM-T10
Demonstrations of SelectiveCS-FEM-T10
Summary

## Slide 10
Quick Introduction of F-barES-FEM-T4 Why not T4 but T10?

## Slide 11: Brief of Edge-based S-FEM (ES-FEM)
Calculate at each element as usual.
Distribute to the connecting edges with area weight and build .
Calculate etc. in each edge smoothing domain.
As if putting an integration point on each edge center
ES-FEM can avoid shear locking. However, it cannot be implemented in ordinary FE codes due to the strain smoothing across multiple elements...

## Slide 12: Brief of Node-based S-FEM (NS-FEM)
Calculate at each element as usual.
Distribute to the connecting nodes with area weight and build .
Calculate etc. in each node smoothing domain.
As if putting an integration point on each node
✗ Spurious low-energy mode (or hour-glass mode)
Less pressure checkerboarding
No shear locking
No volumetric locking

## Slide 13: Concept of F-barES-FEM
Outlline
is given by ES-FEM.
is given by cyclically applied NS-FEM.
is calculated in the manner of F-bar method:
.
Concept: combining ES-FEM and NS-FEM using F-bar method

## Slide 14: Formulation of F-barES-FEM (1 of 2)
ES-FEM
Deformation gradient of each edge () is derived as
in the manner of F-bar method.

## Slide 15: Formulation of F-barES-FEM (2 of 2)
Each part of is calculated as
(1)
Isovolumetric part
Smoothing the value of adjacent elements.
(same manner as ES-FEM)
(1)Calculating node’s value by smoothing
the value of adjacent elements
(2)Calculating elements’ value by smoothing
the value of adjacent nodes
(3)Repeating (1) and (2) a few times
(2)
Volumetric part

## Slide 16: Advantages of F-barES-FEM
Like a ES-FEM
1. Shear locking free
Like a NS-FEM
2. Little pressure oscillation
3. Volumetric locking free with the aid of F-bar method
Isovolumetric part
Volumetric part
This formulation is designed to have 3 advantages.

## Slide 17: Compression of Rubber Block
Outline
Arruda-Boyce hyperelastic material ().
Applying pressure on ¼ of the top face.
Result of F-barES-FEM-T4 is compared to ABAQUS C3D4H with the same unstructured T4 mesh.
Load
Static Implicit

## Slide 18: Compression of Rubber Block
Pressure dist.
ABAQUS C3D4H
Early stage Middle stage Later stage
Static Implicit
F-bar ES-FEM- T4(3)
Smooth pressure distributions are obtained.

## Slide 19: Stretch of Filler-containing Rubber with 2D Remesing
Several hard circular fillers are distributed in a square soft matrix rubber (neo-Hookean hyperelastic with ).
of the filler is 100 times larger than of the matrix.
Left side is constrained and right side is displaced.
Valid Mises stress dist. is obtained after many time remeshings.
Static Implicit

## Slide 20: Shear-tensioning of Elasto-plastic cylinder with 3D Remeshing
Valid plastic strain dist. is obtained after many time remeshings.
Aluminium cylinder subjected to enforced disp..
Pure shear at the initial stage, but stretch dominates at the later stage.
Necking occurs in the end.
Final stretch at the neck is more than 7000%.
Static Implicit

## Slide 21: Characteristics of F-barES-FEM-T4
No increase in DOF. (No Lagrange multiplier. No static condensation.)
Locking- & checkerboarding-free with T4 mesh.
✗ Higher costs in memory and CPU time due to wider bandwidth of .
In case of standard unstructured T4 meshes:
✗ Difficulty in implementation to existing FE codes due to the smoothing across elements.
Method | Approx. Bandwidth
Standard FEM-T4 | 40
F-barES-FEM-T4(1) | 390
Critical Issue!!

## Slide 22: Why Not T4 But T10?
For example in tire analyses:
Material constitutive models,
Structural elements,
Cohesive elements,
Contact functionality and so on.
Therefore, choosing S-FEM-T4 leads us to the long and winding road…
If we cannot implement F-barES-FEM-T4 to existing FE codes, then we have to code everything in our in-house code for practical use.
We gave up T4 and chose T10 for solid mechanics analyses.
MSC Software web page

## Slide 23
Formulation of SelectiveCS-FEM-T10

## Slide 24: Concept of SelectiveCS-FEM-T10
Our new approach using T10 mesh.
Adopting CS-FEM having no smoothing across multiple elements, SelectiveCS-FEM-T10 becomes an independent finite element.
We can implement it as an element of existing FE code.
Same memory & CPU costs as the T10 elements.

## Slide 25: Brief of Cell-based S-FEM (CS-FEM)
Subdivide each element into some sub-element.
Calculate at each sub-element.
Calculate etc. in each sub-element.
Implementable as an independent finite element.
Locking can be avoided with SRI etc..
As if putting an integration point on each sub-element

## Slide 26: Flowchart of SelectiveCS-FEM-T10
Explanation in 2D (6-node triangular element) for simplicity
ES-FEM
SRI
(1) Subdivision without dummy nodes
(3) Vol. strain smoothing with all sub-elements
(2) Dev. strain smoothing at edges
(4)
Overall mean

## Slide 27: (1) Subdivision into T4 Sub-elements
Introduce no dummy node (i.e., asymmetric element).
Subdivide a T10 element into eight T4 sub-elements and calculate their B-matrices and strains.
The shape function should not be quadratic in large deformation analyses.

## Slide 28: (2) Deviatoric Strain Smoothing
Perform strain smoothing in the manner of ES-FEM (i.e., average dev. strains of sub-elements at edges).
Evaluate deviatoric strain and stress at edges.
From 8 sub-elements to 25 edges
T4 sub-elements cause shear locking and thus
strain smoothing is necessary.

## Slide 29: (3) Volumetric Strain Smoothing
Treat the overall mean vol. strain of all sub-elements as the uniform element vol. strain (i.e., same approach as SRI elements).
The spatial order of vol. strain should be lower than that of dev. strain to avoid volumetric locking.

## Slide 30: (4) Combining with SRI Method
Apply SRI method to combine the Dev. & Vol. parts and obtain and .
Deviatoric
Volumetric
Internal force
Stiffness
SRI

## Slide 31
Demonstration of SelectiveCS-FEM-T10

## Slide 32: Bending of Hyperelastic Cantilever
Outline
Neo-Hookean hyperelastic material
Initial Poisson’s ratio:
Compared to ABAQUS C3D10MH (modified hybrid T10 element) with the same mesh.
Dead Load
Static Implicit

## Slide 33: Bending of Hyperelastic Cantilever
Comparison of the deflection disp. at the final state
No volumetric locking is observed.
ABAQUS C3D10MH
Selective CS-FEM-T10
Static Implicit

## Slide 34: Bending of Hyperelastic Cantilever
Comparison of the pressure dist. at the final state
Almost the same pressure distributions with no checkerboarding.
ABAQUS C3D10MH
Selective CS-FEM-T10
Static Implicit

## Slide 35: Bending of Hyperelastic Cantilever
Comparison of the Mises stress dist. at the final state
ABAQUS C3D10MH
Selective CS-FEM-T10
Almost the same Mises stress distributions.
Static Implicit
ABAQUS C3D10MH
Selective CS-FEM-T10

## Slide 36: Barreling of Hyperelastic Cylinder
Outline
Enforce axial displacement on the top face.
Neo-Hookean body with ．
Compare results with ABAQUS T10 hybrid elements (C3D10H, C3D10MH, C3D10HS) using the same mesh.
Static Implicit

## Slide 37: Barreling of Hyperelastic Cylinder
Animation of Mises stress (ABAQUS C3D10MH)
Convergence failure at 24% compression
Unnaturally oscillating distributions are obtained around the rim.
Static Implicit

## Slide 38: Barreling of Hyperelastic Cylinder
Animation of Mises stress (Selective CS-FEM-T10)
Convergence failure at 43% compression
Smooth distributions
are obtained except around the rim.
The present element is more robust than ABAQUS C3D10MH
Static Implicit

## Slide 39: Barreling of Hyperelastic Cylinder
Comparison of Mises stress at 24% comp.
Selective CS-FEM-T10
ABAQUS C3D10MH
ABAQUS C3D10HS
ABAQUS C3D10H
All results are similar to each other except around the rim having stress singularity.
Static Implicit

## Slide 40: Barreling of Hyperelastic Cylinder
Comparison of pressure at 24% comp.
Selective CS-FEM-T10
ABAQUS C3D10MH
ABAQUS C3D10HS
ABAQUS C3D10H
All results are similar to each other except around the rim having stress singularity.
Static Implicit

## Slide 41: Barreling of Hyperelastic Cylinder
Comparison of nodal reaction force at 24% comp.
Selective CS-FEM-T10
ABAQUS C3D10MH
ABAQUS C3D10HS
ABAQUS C3D10H
ABAQUS C3D10H and C3D10HS suffer from nodal force oscillation.
Static Implicit

## Slide 42: Compression of Hyperelastic Block
Outline
Arruda-Boyce hyperelastic material ().
Applying pressure on ¼ of the top face.
Compared to ABAQUS C3D10MH with the same unstructured T10 mesh.
Load
Static Implicit

## Slide 43: Compression of Hyperelastic Block
Animation of pressure dist. (ABAQUS C3D10MH)
Convergence failure at 0.7 GPa pressure
Static Implicit

## Slide 44: Compression of Hyperelastic Block
Animation of Mises stress dist. (ABAQUS C3D10MH)
Convergence failure at 0.7 GPa pressure
Static Implicit

## Slide 45: Compression of Hyperelastic Block
Animation of pressure dist. (Selective CS-FEM-T10)
Convergence failure at 1.3 GPa pressure
The present element is more robust than ABAQUS C3D10MH
Static Implicit

## Slide 46: Compression of Hyperelastic Block
Animation of Mises stress dist. (Selective CS-FEM-T10)
The present element presents Mises stress oscillation.
Static Implicit

## Slide 47: Compression of Hyperelastic Block
Misess stress dist. at 0.7 GPa pressre
ABAQUS C3D10MH SelectiveCS-FEM-T10
Less smoothed Mises stress is observed in SelectiveCS-FEM-T10. Further improvement is still required.
Static Implicit

## Slide 48: Characteristics of SelectiveCS-FEM-T10
Benefits
  Accurate (no locking, no checkerboarding, no force oscillation).
  Robust (long-lasting in large deformation).
  No increase in DOF (No static condensation).
  Same memory & CPU costs as the other T10 elements.
  Implementable to commercial FE codes (e.g., ABAQUS UEL).
Drawbacks
✗ Mises stress oscillation in same extreme analyses.
✗ No longer a T4 formulation.
SelectiveCS-FEM-T10 is competitive with the best ABAQUS T10 element, C3D10MH.

## Slide 49
Summary

## Slide 50: Summary
One-sentence summary
SelectiveCS-FEM-T10 is already good enough for practical use as compared to ABAQUS Tet elements.
Take-home message
Please consider implementing SelectiveCS-FEM-T10 to your in-house code. It’s supremely useful & easy to code!!
Thank you for your kind attention!

## Slide 51: Appendix

## Slide 52: Differences between Old and New
The new formulation has NO dummy node at the center of an element.
  Fewer sub-elements and edges.
  Asymmetric element.
The new formulation has No ES-FEM-1 after ES-FEM.
  Strain & stress evaluation at edges.
  No strain smoothing at frame edges.
Its reason has not revealed yet.
Intuitively, the lack of element symmetry and frame edge smoothing is not good for accuracy and stability; however, the new formulation is better in fact.

## Slide 53: Collapse Analysis of Viscoelastic Bunny
Outline
Applying gravity to the Stanford Bunny and let it collapsed by its self-weight.
Soft viscoelastic material .
Contact is NOT considered.
Comparing F-barES-FEM-T4(2) and ABAQUS C3D4H.
Viscous Implicit
# of nodes: 24136
# of elems: 126231

## Slide 54
Animation of Deformation
Because contact is not considered, the body penetrates the feet and finally becomes upside downside. The analysis lasts till the necking.
Viscous Implicit

## Slide 55: Collapse Analysis of Viscoelastic Bunny
Mises stress dist. when C3D4H get a convergence failure
ABAQUS C3D4H shows a stiffer result due to shear locking.
The result of F-barES-FEM-T4 would be better.
F-barES-FEM-T4(2)
ABAQUS C3D4H
Viscous Implicit

## Slide 56: Impact of Rubber Bunny
Outline
A bunny made of rubber (Neo-Hookean) is crushed to a rigid wall.
Compared with ABAQUS/Explicit C3D4 using a same T4 mesh.
Note that neither Hex mesh nor hybrid elements is not available in this problem.
Initial velocity
10 m/s
(uniform)
Rigid Wall
Contact condition
free-slip, free-separation
Dynamic Explicit
Rubber body

## Slide 57: Impact of Rubber Bunny
Animation of Pressure Dist.
Dynamic Explicit
ABAQUS/Explicit C3D4 ✗ Pressure Checkerboarding
✗ Shear Locking
SymF-barES- FEM-T4(1)
 Smooth pressure
 No Locking

## Slide 58: Impact of Rubber Bunny
Sign of Pressure at Initial Phase
The proposed S-FEM captures the pressure wave in a complex body successfully!!
SymF-barES-FEM-T4(1)
ABAQUS/Explicit C3D4
(Standard T4 element)
Dynamic Explicit
✗ Pressure Checkerboarding
✔ Pressure Wave

## Slide 59: Issues (cont.)
E.g.) Compression of neo-Hookean hyperelastic body with
SelectiveCS-FEM-T10 (Old Ver.)
 No shar/voluemetric locking
 Little corner locking  Little pressure checkerboarding  Same cost & userbility as T10 elements.
Same mesh as C3D10MH case.
As other S-FEMs, SelectiveCS-FEM-T10 has many varieties in the formulation.
The proposed method last year was not an optimal formulation yet.

## Slide 60: Shear-tensioning of Elasto-plastic Bar
P. 60
Outline
Blue face is perfectly constrained.
Red face is constrained in plane and pressed down.
Compared to ABAQUS C3D4H with the same unstructured T4 mesh.
Elasto-plastic material:
Hencky elasticity with and .
Isotropic von Mises yield criterion with and (constant).
1.2 k nodes & 4.8 k elems.
Static Implicit

## Slide 61: Shear-tensioning of Elasto-plastic Bar
Result of F-bar ES-FEM(2) (Equiv. plastic strain)
Static Implicit
Extreme large deformation with smooth strain dist. is successfully achieved.

## Slide 62: Shear-tensioning of Elasto-plastic Bar
P. 62
Equivalent plastic strain dist. in middle states
F-barES-FEM-T4(2)
ABAQUS C3D4H
There is minor oscillation.
Smooth distribution.
Static Implicit

## Slide 63: Shear-tensioning of Elasto-plastic Bar
P. 63
Pressure dist. in middle states
F-barES-FEM-T4(2)
ABAQUS C3D4H
Smooth distribution.
There is major oscillation.
Static Implicit