## Slide 1: A Brief Introduction to Smoothed Finite Element Method (S-FEM)
Yuki ONISHI (Tokyo Institute of Technology)

## Slide 2: Quick Review of S-FEM

## Slide 3: What is S-FEM?
Smoothed finite element method (S-FEM) is a relatively new FE formulation proposed in 2006.
S-FEM is one of the gradient (strain) smoothing techniques.
There are many kinds of S-FEMs depending on the scheme of smoothing.
There are a few classical S-FEMs depending on the smoothing domain.
For example, in a 2D triangular mesh:
Standard FEM
Edge-based S-FEM (ES-FEM)
Node-based S-FEM (NS-FEM)
Each colored area shows the domain for gradient smoothing.

## Slide 4: e.g.) Brief of ES-FEM
Let us consider a mesh with only two 3-node triangular cells.
Calculate at each cell as usual.
Distribute each to the connecting edge with an area weight and build .
Calculate strain , Cauchy stress () and nodal internal force in each edge smoothing domain with .
As if putting a Gauss point on each edge center
etc.
Let me explain in 2D for simplicity

## Slide 5: What are the major benefits of S-FEM?
Super-linear mesh convergence rate with T4 mesh. (Almost same rate as 2nd-order elements with T4 mesh.)
Shear locking free with ES-FEM-T4. (Good accuracy with T4 mesh in solid mechanics.)
Volumetric locking free with NS-FEM-T4. (Key technique for rubber-like nearly incompressible solid.)
Little accuracy loss with skewed meshes. (No problem with complex geometry or severe deformation.)
No increase in DOF. (Purely displacement-based formulation. )
Easy to code. (keeping away from mixed variational formulations.)
S-FEM is a powerful method suitable for practical industrial applications.
T4: 4-node Tetrahedra
T4

## Slide 6: How popular is S-FEM?
Number of journal papers whose title contains “smoothed finite element”:
The attraction of S-FEM is expanding continuously.
Two active researchers in Germany:
Prof. Günther Meschke in Ruhr University Bochum
Denisa Martonová in Friedrich-Alexander-Universität
inquired at Google Scholar

## Slide 7: Applications of S-FEM-T4 in Our Lab
Large deformation solid mechanics (still in academic research)
Dynamic Explicit Static Implicit Viscous Implicit
Electrostatic (already in commercial use)
Carbody Electro Deposition
Today, I’ll focus on static implicit analyses and introduce the latest studies on S-FEM-T4 briefly.

## Slide 8: Motivation & Objective of Our Latest Study

## Slide 9: Motivation
What we want to do:
Solve severe large deformation analyses accurately and robustly.
Treat complex geometries with tetrahedral meshes.
Consider nearly incompressible materials .
Support contact problems.
Handle auto re-meshing.
Rubber
Plastic/Glass
Metal

## Slide 10: Issues in Conventional FE (ABAQUS）
e.g.) Barreling of Rubber Cylinder Neo-Hookean hyperelastic body with
ABQUS C3D4H  No volumetric locking.
✗ Pressure checkerboarding.
✗ Shear locking & Corner locking.
ABAQUS C3D10MH
 No shear/volumetric locking.
✗ Short lasting (weak to severe deformation). ✗ Low interpolation accuracy.
Almost the same # of nodes.
Pressure
Pressure
4 node tet (T4)
10 node tet (T10)
T4
T10

## Slide 11: Our Approach using S-FEM
e.g.) Barreling of Rubber Cylinder Neo-Hookean hyperelastic body with
F-barES-FEM-T4 (2017)
 No shear/volumetric locking.
 Less pressure checkerboarding.  Less corner locking. Long lasting.
 No oscillation in deviatoric stress. ✗ Long CPU time. Incompatible w/ FE.
SelectiveCS-FEM-T10 (2021)
 No shear/volumetric locking.
 Less pressure checkerboarding.  Less corner locking. Long lasting. ✗ Major oscillation in deviatoric stress.  Same CPU time. Compatible w/ FE.
4 node tet (T4)
10 node tet (T10)
T4
T10
More than 10 times slower than FEM-T4, but no good idea for speed-up…
Cannot suppress
stress oscillation, but no good idea for accuracy improvement…
Pressure
Pressure

## Slide 12: Birth of a New-generation S-FEM, EC-SSE, in 2022
Comparison of Mises stress dist. in cantilever bending analyses in 2D
T. Jinsong et al., Euro. J. Mech. /A, v95, 2022.
Step-like stress dist. (poor).
Shear locking.
Edge Center-based Strain Smoothing Element
Detailed Later
Linear stress dist. (very good) using the same T3 mesh. So close to analytical solution.
No shear locking.
EC-SSE is an excellent formulation for compressible solids; but when , EC-SSE has volumetric locking and pressure checkerboarding. Therefore, EC-SSE is NOT directly applicable to nearly incompressible solids.
T3
Poisson’s Ratio:
This breakthrough should be called
“S-FEM 2.0”.

## Slide 13: Objective
Objective
Strategy
Use the selective reduced integration (SRI)
Use EC-SSE for the deviatoric part,
Use NS-FEM for the volumetric part, and
Combine them with SRI.
Develop a new S-FEM formulation to extend EC-SSE to nearly incompressible large deformation analysis
EC-SSE-SRI

## Slide 14: Method Introduction to ES-FEM, NS-FEM，EC-SSE，and EC-SSE-SRI

## Slide 15: Brief of ES-FEM
Let us consider a mesh with only two 3-node triangular cells.
Calculate at each cell as usual.
Distribute each to the connecting edge with an area weight and build .
Calculate deformation gradient , Cauchy stress () and nodal internal force in each edge smoothing domain with .
As if putting a Gauss point on each edge center
etc.
Strain distribution is piecewise constant in each smoothing domain.
No shear locking.
Cannot avoid volumetric locking & pressure checkerboarding.
Let me explain in 2D for simplicity

## Slide 16: Brief of NS-FEM
Let us consider a mesh with only four 3-node triangular cells.
Calculate at each cell as usual.
Distribute each to the connecting node with an area weight and build .
Calculate deformation gradient , Cauchy stress () and nodal internal force in each nodal smoothing domain with .
As if putting a Gauss point on each node center
etc.
No shar/volumetric locking. Less pressure checkerboarding
Cannot avoid spurious low-energy modes.
Let me explain in 2D for simplicity
Strain distribution is piecewise constant in each smoothing domain.

## Slide 17: Brief of EC-SSE
Make s in the same procedure as ES-FEM.
Consider each is the value at the center of each edge, and assume is linearly distributed in each cell.
Make three s in each cell as the extrapolation of the three s.
Calculate , and using each in the same manner as the 2nd -order element.
No shear locking with T3/T4 mesh.
Fast mesh convergence rate in strain/stress as an 2nd –order element.
Strain distribution is piecewise-linear in each cell and is continuing at every edge center.
Conducting strain smoothing twice, the strain/stress are evaluated at each Gauss point.
Let me explain in 2D for simplicity
Cannot avoid volumetric locking and pressure checkerboarding

## Slide 18: Brief of EC-SSE-SRI (Our Latest Method)
Apply the selective reduced integration (SRI) to EC-SSE to handle rubber-like solids
(1) Calculate at each Gauss point with EC-SSE
(3) Calculate at each node with NS-FEM
(5) Assemble
(2) Calculate at each Gauss point and its contribution to
(4) Calculate at each node and its contribution to
Selective Reduced Integration (SRI)
Let me explain in 2D for simplicity
Deviatoric strain distribution is piecewise-linear in each cell and is continuing at each edge center.
No shear/volumetric locking. Less pressure checkerboarding.
Deviatoric Part
Volumetric Part

## Slide 19: Brief of EC-SSE-SRI-T4 (in 3D)
[Deviatoric Part]
Make s in the same procedure as ES-FEM.
Make s by re-smoothing three s per face.
Consider each is the value at the center of each face, and assume is linearly distributed in each cell.
Make four s in each cell as the extrapolation of the four s.
Calculate , and using each , like the 2nd -order element.
[Volumetric Part]
Make s in the same procedure as NS-FEM.
Calculate , and using each .
[SRI]
Make .
Let me explain with text only

## Slide 20: Result & Discussion Demonstration of EC-SSE-SRI-T4 in 3D and Evaluation of CPU Cost

## Slide 21: Bending of Rubber Cantilever
Outline
10 x 1 x 1 m cantilever.
Dead load applied to the tip node.
Neo-Hookean hyperelastic material, .
A large deflection analysis with m at the final state.
Compared the results of ABAQUS C3D4 and EC-SSE-SRI-T4.
Dead Load
Static Implicit

## Slide 22: Bending of Rubber Cantilever
Results of ABAQUS C3D4 (Final State)
Discontinuous distribution.
Volumetric locking. (-15% error in deflection)
Severe pressure checkerboarding.
Static Implicit
***WARNING: THE INITIAL BULK MODULUS OF 9.93333E+10 EXCEEDS 25 TIMES THE
INITIAL SHEAR MODULUS OF 2.00000E+09 (SO THE INITIAL POISSONS
RATIO 0.49000 EXCEEDS 0.48) FOR THE HYPERELASTIC MATERIAL NAMED
MATERIAL-1. HOWEVER, A HYBRID TYPE ELEMENT IS NOT USED. THIS MAY
CAUSE CONVERGENCE PROBLEMS.
ABAQUS dat file:

## Slide 23: Bending of Rubber Cantilever
Results of EC-SSE -SRI-T4 (Final State)
Smooth distribution.
No locking.
Little oscillation, but no checkerboarding.
Static Implicit

## Slide 24: Pressuring of Rubber Block
Outline
1 x 1 x 1 m block.
Arruda-Boyce hyperelastic material, GPa, .
Applying pressure on ¼ of the top face with lateral confinement.
Evaluated the result of EC-SSE-SRI-T4.
Load
Static Implicit

## Slide 25: Pressuring of Rubber Block
Results of EC-SSE-SRI-T4
No big issue in stress distributions
Sufficient large deformation robustness
Static Implicit

## Slide 26: Barreling of Rubber Cylinder
Outline
1 m cylinder in radius and height.
Neo-Hookean hyperelastic material, .
Applying enforced compression displacement on the top face with lateral confinement.
Evaluated the result of EC-SSE-SRI-T4.
Static Implicit

## Slide 27: Barreling of Rubber Cylinder
Results of EC-SSE-SRI-T4
No problem in Mises stress.
Minor oscillation in pressure.
Convergence failure at 37% compression.
Static Implicit
Within acceptable range, I think.
acceptably robust in large deformation

## Slide 28: Tensioning of Rubber-Filler Composite
Outline
0.5 x 0.5 x 0.5 m cube (1/8 model)
Rubber: Neo-Hookean hyperelastic material
Iron Filler: Neo-Hookean hyperelastic material
Applying enforced tensioning displacement on the top face with lateral confinement.
Evaluated the result of EC-SSE-SRI-T4.
Static Implicit

## Slide 29: Tensioning of Rubber-Filler Composite
Results of EC-SSE -SRI-T4
Minor pressure oscillation only in rubber part.
No issue in Mises stress.
Convergence failure at 221% stretch sufficiently robust in large deformation
Static Implicit
Within acceptable range, I think.

## Slide 30: Discussion on CPU Time of EC-SSE-SRI-T4
Since the most of CPU time for implicit analyses is spent solving the stiffness equation (i.e., ), the size of matrix () directly affects the CPU time.
EC-SSE-SRI-T4 is a purely displacement-based FE formulation; thus, the matrix size () is exactly identical to that of FEM-T4.
EC-SSE-SRI-T4 conducts strain smoothing across FE cells; thus, the matrix bandwidth of is x6.7 wider than that of FEM-T4.
Therefore, as for calculation speed, EC-SSE-SRI-T4 is about x6.7 slower than FEM-T4.
Formulation | Bandwidth of | v.s. FEM-T4 Ratio
FEM-T4 | 14 nodes x 3 DOF | 1
FEM-T10 | 28 nodes x 3DOF | 2.0
ES-FEM-T4 | 45 nodes x 3 DOF | 3.2
NS-FEM-T4 | 60 nodes x 3 DOF | 4.3
EC-SSE-T4, EC-SSE-T4-SRI | 94 nodes x 3DOF | 6.7
Formulation |  | v.s. FEM-T4 Ratio
FEM-T4 | 14 nodes x 3 DOF | 1
FEM-T10 | 28 nodes x 3DOF | 2.0
ES-FEM-T4 | 45 nodes x 3 DOF | 3.2
NS-FEM-T4 | 60 nodes x 3 DOF | 4.3
EC-SSE-T4, EC-SSE-T4-SRI | 94 nodes x 3DOF | 6.7

## Slide 31: Discussion on CPU Time of EC-SSE-SRI-T4
Meanwhile, we should remind that
  FEM-T4 cannot avoid volumetric locking and pressure checkerboarding,
  FEM-T10 cannot have large deformation robustness (short-lasting),
  no matter how fine the mesh is.
Therefore, I believe, EC-SSE-T4-SRI is practically acceptable and worth using, even though the CPU time is 6.7 times longer than FEM-T4. What do you think?

## Slide 32: Summary

## Slide 33: Summary
Smoothed finite element methods (S-FEMs) with T4 mesh are quite useful for practical complex geometry problems in various applications, including large deformation analyses.
EC-SSE-T4 is excellent for compressible solids, and is opening the door of “S-FEM 2.0”.
EC-SSE-SRI-T4 is recommended for nearly incompressible solids.
The EC-SSE family would be the standard T4 formulation in the near future.
Take home message:
Why not S-FEM? It is supremely useful and easy to code!
Thank you for your kind attention!

## Slide 34: Appendix

## Slide 35: Why not T10 but T4?
It is because T10 mesh is NOT good for the representation of complex geometries.
For example, surface mesh around a small hole looks like…
Also, the presence of mid-nodes leads to early convergence failure in large deformation.
Then, T4 is preferable.
solid
Hole
T10 mesh w/ kink
✗ leads to severe
accuracy loss.
solid
Hole
T10 mesh w/o kink
✗ leads to a massive
increase in DOF.
solid
Hole
T4 mesh
is excellent with ES-FEM
using minimal # of meshes.
T10
T4