## Slide 1: Performance Evaluation of the Selective Smoothed Finite Element Method with Deviatoric/Hydrostatic Split
Yuki ONISHI, Kenji AMAYA Tokyo Institute of Technology (Japan)

## Slide 2: Motivation & Background
Motivation
  We want to analyze severely large deformation problems in solids accurately and stably! (Target: automobile tire, thermal nanoimprint, etc.)
Background
  Finite elements are distorted in a short time, thereby resulting in convergence failure.
Mesh rezoning method (h-adaptive mesh-to-mesh solution mapping) is indispensable.
Mold
Polymer

## Slide 3: Our First Result in Advance
What we want to do:
Static
Implicit
Large deformation
Mesh rezoning

## Slide 4: Issues
The biggest issue in large deformation mesh rezoning
It is impossible to remesh arbitrary deformed 2D or 3D domains with quadrilateral or hexahedral elements.
However, the standard (constant strain) triangular or tetrahedral elements induce shear and volumetric locking easily, which leads to inaccurate results.
We have to use triangular or tetrahedral elements...
YES
NO

## Slide 5: Conventional Methods
Higher order elements: ✗ Not volumetric locking free; Not effective in large deformation due to intermediate nodes.
EAS elements: ✗ Unstable.
B-bar, F-bar and selective integration elements: ✗ Not applicable to triangular/tetrahedral mesh.
F-bar patch elements: ✗ Difficult to construct good patches
u/p hybrid (mixed) elements prime candidate ✗ No sufficient formulation for triangular/tetrahedral mesh is presented so far. (There are almost acceptable hybrid elements such as C3D4H or C3D10H of ABAQUS.)
Selective smoothed finite elements: ? Unknown potential. Performance evaluation is necessary.

## Slide 6: Objective
Performance evaluation of the selective S-FEMs
for large deformation problems
Table of Body Contents
Part 1: Brief Introduction to the Formulation of the Selective S-FEMs with Dev/Hyd Split
Part 2: Results of Performance Evaluation
Part 3: Demonstration with Mesh Rezoning
Summary

## Slide 7
Part 1:
Brief Introduction to the Formulation of the Selective S-FEMs with Dev/Hyd Split

## Slide 8: Review of Selective ES/NS-FEM
Separate stress into " part" and " part", where and are the Lame's parameters.
F, T etc and {f int} are calculated on both smoothed domains.
Only applicable to elastic constitutive models.
Substituting "face"
for
"edge"
gives
FS/NS-FEM
for 3D

## Slide 9: Modified Selective ES/NS-FEM
Separate stress into "deviatoric part" and "hydrostatic part" instead of " part" and " part".
F, T etc and {f int} are calculated on both smoothed domains.
Applicable to any kind of material constitutive models.
Substituting "face"
for
"edge"
gives
FS/NS-FEM
for 3D

## Slide 10: 3 Types of Selective S-FEMs
Method | Deviatoric Part | Hydrostatic Part
2D ES/NS-FEM-T3 | ES-FEM | NS-FEM
3D ES/NS-FEM-T4 | ES-FEM | NS-FEM
3D FS/NS-FEM-T4 | FS-FEM | NS-FEM
No increase in DOF!!
Displacement vector is only the unknown.

## Slide 11
Part 2:
Results of Performance Evaluation
focused on the analysis for hyperelastic materials without mesh rezoning

## Slide 12: Verification ~ Bending of Cantilever ~
Outline (Bending of Cantilever)
Neo-Hookean hyperelastic material, with a constant (=1 GPa) and various s.
Compared to ABAQUS with various elements.

## Slide 13: Verification ~ Bending of Cantilever ~
Results with (=0.499999)
The amount of vertical deflection
is about
6.5 m.

## Slide 14: Verification ~ Bending of Cantilever ~
Comparison of Deflection Displacements

## Slide 15: Verification ~ Bending of Cantilever ~
Comparison to 2nd-order Hybrid Hex Element (C3D20H)
Selective S-FEM is locking-free
in large deflection analysis!!

## Slide 16: Verification ~ Bending of Cantilever ~
Sign of Pressure at Nodes (=0.499999)
Selective S-FEMs suffer from pressure oscillation…
Selective FS/NS-FEM-T4
Selective ES/NS-FEM-T4

## Slide 17: Verification ~ Bending of Cantilever ~
Sign of Pressure at Nodes (=0.499999)
NS-FEM already suffers from minor pressure oscillation.
The oscillation is magnified a little in Selective S-FEMs.
NS-FEM-T4

## Slide 18: Verification ~ Bending of Cantilever ~
Internal Energy and External Work (=0.499999)
Conservation of energy is exactly satisfied.
No energy divergence but pure pressure oscillation.

## Slide 19: Verification ~ Bending of Cantilever ~
Mesh Size Convergence Rate (Error of Displacement at the Tip)
Linear convergence as same as the standard 1st-order FEM.

## Slide 20: Verification ~ Bending of Cantilever ~
Convergence behavior in Newton-Raphson Loop
(In the 1st timestep)
Convergence rate slightly depends on Poisson’s ratio. (Probably due to the loss/cancellation of digits in floating-point calculation.)

## Slide 21: Verification ~Partial Compression of Block ~
Outline
Arruda-Boyce hyperelastic material with .
Compared to ABAQUS with various elements.
on ¼ of top face

## Slide 22: Verification ~Partial Compression of Block ~
Result of Selective FS/NS- FEM-T4

## Slide 23: Verification ~Partial Compression of Block ~
Vertical Displacements vs. Applied Pressure
Constant strain element (C3D4) locks quickly.
Other elements including selective S-FEMs do not lock.
Selective S-FEMs are locking-free in large strain analysis!!

## Slide 24: Verification ~Partial Compression of Block ~
Sign of Pressure
Pressure oscillation is present as well.
Selective FS/NS-FEM-T4
Selective ES/NS-FEM-T4

## Slide 25: Verification ~Partial Compression of Block ~
Mises Stress
Selective S-FEMs cannot prevent locking of corner elements.
Selective FS/NS-FEM-T4
Selective ES/NS-FEM-T4

## Slide 26: Verification ~ Compression of 1/8 Cylinder ~
Outline
Neo-Hookean hyper elastic material with .
Compared to C3D4H of ABAQUS with exactly the same mesh.
(50% axial compression)

## Slide 27: Verification ~ Compression of 1/8 Cylinder ~
Result of Selective FS/NS- FEM-T4

## Slide 28: Verification ~ Compression of 1/8 Cylinder ~
Comparison to ABAQUS
Deformation is almost the same each other.
Pressure oscillation is about double in our result.
Locking of corner/edge elements is observed.
C3D4H
of ABAQUS/Standard
Selective
ES/NS-FEM-T4

## Slide 29: Verification ~ Compression of 1/8 Cylinder ~
Comparison to ABAQUS
Deformation is almost the same each other.
Pressure oscillation is about double in our result.
Locking of corner/edge elements is observed.
C3D4H
of ABAQUS/Standard
Selective
FS/NS-FEM-T4

## Slide 30: 3 Issues in Selective S-FEMs
Selective S-FEMs with dev/hyd split cannot handle material constitutive models with dev/vol coupling terms.
Selective S-FEMs cannot prevent pressure oscillation in the analysis with almost incompressible materials.
Selective S-FEMs cannot provide sufficient smoothing effect to elements at corners.

## Slide 31
Part 3:
Demonstration with Mesh Rezoning

## Slide 32: Demo ~ Twist & Stretch of Rubber Cuboid ~
Static, 1 m x 2 m x 4 m
Neo-Hookean hyperelastic body of and ()
Twist up to 360 deg. Stretch up to 100% nominal strain Twist back Shrink back
Our selective FS/NS-FEM with tetrahedral elements
Global mesh rezoning every 90 deg. and 50% stretch/shrink

## Slide 33: Demo ~ Twist & Stretch of Rubber Cuboid ~
Our selective FS/NS-FEM with mesh rezoning
Our selective FS/NS-FEM without mesh rezoning

## Slide 34: Demo ~ Twist & Stretch of Rubber Cuboid ~
Residual Displacement
It
spring backed
almost perfectly.

## Slide 35: Demo ~ Shearing & Necking of Plastic Rod ~
Outline
Static, 3D
Hencky's elasto-plastic material, , with von Mises yield criterion and isotropic hardening. Young's Modulus: 1 GPa, Poisson's Ratio: 0.3, Yield Stress: 1 MPa, Hardening Coeff.: 0.5 MPa.

## Slide 36: Demo ~ Shearing & Necking of Plastic Rod ~
After 2.8 m disp.,
mesh rezoning error occurred.
The final nominal stretch is >7000% at the neck.
Result with Selective FS/NS- FEM-T4

## Slide 37: Demo ~ Shearing & Necking of Plastic Rod ~
Result of Similar Analysis in 2D with Selective ES/NS- FEM-T3

## Slide 38: Demo ~Tension of Filler Particle Composite~
Outline
2D, plane-strain, static
Neo-Hookean Hyperelastic
  Filler: hard rubber（）
  Matrix: soft rubber（）

## Slide 39: Demo ~Tension of Filler Particle Composite~
Result of Selective ES/NS-FEM-T4
The deformation seems to be valid.
After 180% stretch, analysis stopped due to mesh rezoning error.

## Slide 40
Summary

## Slide 41: Characteristics of S-FEMs & C3D4H
 | Shear Locking | Volumetric Locking | Zero Energy Mode | No Increase in DOF | Pressure Oscillation & Locking at Corner | Dev/Vol Coupled Material
Standard FEM-T4 | ✗ | ✗ |  | - | ✗ | 
ES-FEM-T4 & FS-FEM-T4 |  | ✗ |  |  | ✗ | ✗
NS-FEM-T4 |  |  | ✗ |  | ✗ | ✗
Selective FS/NS-FEM-T4 & ES/NS-FEM-T4 |  |  |  |  | ✗ | ✗
ABAQUS C3D4H |  |  |  | ✗ | ✗ | 
Issues in Future
Benefit

## Slide 42: Summary and Future Work
Summary
  A new implicit static mesh rezoning method for severely large deformation analysis was proposed.
  It adopts our modified selective S-FEM, which separates stress into deviatoric part and hydrostatic part.
  Its performance was evaluated and then 3 issues were revealed.
Future Work
  Resolve the 3 issues
  Apply to contact forming, crack propagation, etc.
  Explicit dynamic formulation
  Local mesh rezoning
Thank you for your kind attention.
I appreciate your question in slow and easy English!!