## Slide 1: Performance Evaluation of Various Smoothed Finite Element Methods with Tetrahedral Elements in Large Deformation Dynamic Analysis
Ryoya IIDA, Yuki ONISHI, Kenji AMAYA
Tokyo Institute of Technology, Japan

## Slide 2: Goal and Requirements
(1)Being applied to 4-noded Tet (T4) elements
(2)Stability even in Nearly incompressible materials
(3)Being directly applied to Explicit Dynamics
Goal
To analyze large deformation dynamic problems
for rubber-like materials
For such analysis, these 3 properties are required.

## Slide 3: Requirements (1 of 3): T4 elements
Arbitrary shapes cannot be meshed
into good-quality Hex elements automatically.
Intermediate nodes cause bad-accuracy
in Large deformation problem.
First-order Tet elements (T4) are preferred for such analysis.
✗
✔

## Slide 4: Requirements (2 of 3): Stability for rubber-like materials
In FE analysis for rubber-like materials,
Pressure oscillation & Locking easily arise.
Reference solution
Standard T4 elements
✗pressure oscillation
✗shear & volumetric locking
Poisson’s ratio: 0.499

## Slide 5: Requirements (3 of 3): Explicit dynamics
2 types of time integration scheme
Implicit is suitable for long-term problems
Explicit is suitable for short-term problems
u/p hybrid formulations cannot be easily applied to explicit dynamics.
General methods of explicit dynamics
for rubber like materials have not been established !
The advantage of S-FEM is to be directly applied to explicit dynamics

## Slide 6: Objective
Objective
To evaluate the performance of competitive S-FEMs
Selective ES/NS-FEM
F-barES-FEM
in explicit dynamics for nearly incompressible materials.
Table of Body Contents
Methods: Quick introduction of S-FEMs
Results & Discussion: A few verification analyses
Summary

## Slide 7: Methods
Selective ES/NS-FEM F-barES-FEM

## Slide 8: Quick review of S-FEM
Integration area
Element
Node
Smoothed-FEM (S-FEM)
ES-FEM sums up each Edge values.
✔ High accuracy in isovolumetric part
without shear locking
Standard FEM
Nodal forces are calculated
by summing up of
each elements’
NS-FEM sums up each Node values.
✔ High accuracy in volumetric part
with little pressure oscillation

## Slide 9: Selective ES/NS-FEM (1 of 2)
Cauchy stress tensor is derived as

## Slide 10: Selective ES/NS-FEM (2 of 2)
Like a ES-FEM
1. Shear locking free
Like a NS-FEM
2. Little pressure oscillation
3. Volumetric locking free
Deviatoric part
Hydrostatic-pressure part
This formulation is designed to have 3 advantages.

## Slide 11: F-barES-FEM (1 of 3)
ES-FEM
Deformation gradient of each edge, is derived as

## Slide 12: F-barES-FEM (2 of 3)
Each part of is calculated as
(1)
Isovolumetric part
Smoothing the value of adjacent elements.
↓
The same manner as
ES-FEM
(1)Calculating node’s value by smoothing
the value of adjacent elements
(2)Calculating elements’ value by smoothing
the value of adjacent nodes
(3)Repeating (1) and (2) a few times
(2)
Volumetric part

## Slide 13: F-barES-FEM (3 of 3)
Like a ES-FEM
1. Shear locking free
Like a NS-FEM
2. Little pressure oscillation
3. Volumetric locking free with the aid of F-bar method
Isovolumetric part
Volumetric part
This formulation is designed to have 3 advantages.

## Slide 14: Characteristics of S-FEMs
Deformation
Stress
Displacement
Internal force
F-barES-FEM decomposes this part.
✗ Stiffiness matrix becomes asymmetric
Selective ES/NS-FEM decomposes this part
✗ Constitutive models are restricted
Both of S-FEMs have disadvantages…

## Slide 15: Equation to solve
Equation of Motion
,
Internal force vector is calculated as
Selective ES/NS-FEM
F-barES-FEM
-matrix of ES-FEM
Stress derived from
Defenition of in the same fashion as F-bar method
Dev. parts are
derived from ES-FEM
Hyd. parts are
derived from NS-FEM

## Slide 16: Result & Discussion

## Slide 17: Bending of a cantilever
Dynamic explicit analysis.
Neo-Hookean material Initial Young’s modulus: 6.0 MPa, Initial Poisson’s ratio: 0.499, Density: 10000 kg/m3.
Compare the results of S-FEMs with Selective H8 (ABAQUS/Explicit C3D8) elements.

## Slide 18: Result of Standard T4 elements
ABAQUS/Explicit
C3D8
(Reference)
Standard T4 element
×pressure oscillation
×locking
The result of standard T4 elements is useless…
at s

## Slide 19: Time history of deformed shapes
ABAQUS/Explicit
C3D8
Reference
All of S-FEMs are locking free.
F-barES-FEM shows good result in earlier stage
but gets worse in later stage.
Selective ES/NS-FEM and NS-FEM cannot suppress pressure oscillation…
Selective ES/NS-FEM
F-barES-FEM
(2)
NS-FEM

## Slide 20: Deformed shapes and pressure distributions
Selective ES/NS-FEM and NS-FEM cannot suppress pressure oscillation due to the insufficient smoothing.
at s
ABAQUS/Explicit C3D8
(Reference)
Selective
ES/NS-FEM
NS-FEM

## Slide 21: Deformed shapes and pressure distributions
ABAQUS/Explicit C3D8
(Selective H8 element)
Reference
at s
F-barES-FEM(2) is comparable to Selective H8 element!
F-barES-FEM(2)

## Slide 22: Time history of displacement
NS-FEM shows slightly soft result.
Selective ES/NS-FEM and F-barES-FEM agree with the reference.
NS-FEM
Reference
Selective ES/NS-FEM
F-barES-FEM

## Slide 23: Time history of total energy
F-barES-FEM causes energy divergences in earlier stage…
Increasing the number of smoothings suppresses the speed of divergence.

## Slide 24: Natural Modes of ¼ Cylinder
Outline
Iron part: , Elastic, No cyclic smoothing.
Rubber part: , Elastic, 1 or 2 cycles of smoothing.
Compare S-FEMs with ABAQUS C3D4 and C3D8.
Fixed
In Plane Slide
In Plane Slide
Rubber Part
Iron Part

## Slide 25: Natural frequencies of each mode
P. 25
1
NS-FEM
Reference
Selective ES/NS-FEM
F-barES-FEM
NS-FEM shows bad results due to spurious low-energy modes.
Selective ES/NS-FEM and F-barES-FEM agree with the reference.

## Slide 26: 1st mode shapes
1st mode shapes also agree with the reference solutions.
ABAQUS C3D8
(Reference)
F-barES-FEM(2)
Selective ES/NS-FEM
NS-FEM

## Slide 27: 11th mode shapes
NS-FEM shows spurious low-energy mode!
ABAQUS C3D8
(Reference)
F-barES-FEM(2)
Selective ES/NS-FEM
NS-FEM
spurious low-energy mode

## Slide 28: Distributions of natural frequencies of F-barES-FEM
Some natural frequencies have small imaginary part…
Imag.
Part
Increasing the number of smoothings makes
the frequencies close to real numbers.

## Slide 29: Cause of energy divergence
Due to the adoption of F-bar method, the stiffness matrix becomes asymmetric.
Equation of Motion:
Asymmetric stiffness matrix gives rise to imaginary part of natural frequencies and instability in dynamic problem.
As shown before, increasing the number of smoothings suppress the energy divergence speed.
asymmetric
F-barES-FEM is restricted to short-term analysis (such as impact analysis) with a sufficient number of smoothings.

## Slide 30: Swinging of Bunny Ears
Outline
Iron ears: , Neo-Hookean, No cyclic smoothing.
Rubber body: , Neo-Hookean, 1 cycle of smoothing.
Compared to ABAQUS/Explicit C3D4. No Hex mesh available!
Iron Ears
Rubber Body
Fixed
Initial Velocity of Iron Ears

## Slide 31: Time histories of deformed shapes
Only F-barES-FEM seems to be representing not pressure oscillations but pressure waves.
Selective ES/NS-FEM
F-barES-FEM
NS-FEM
ABAQUS/Explicit C3D4
✔ Pressure waves
✗ Pressure oscillation
✗Pressure oscillation
✗suspension in
an early stage
✗Pressure oscillation

## Slide 32: Deformed shapes and sign of pressure
F-barES-FEM represents pressure waves correctly!
✔ Pressure waves
In an early stage
✗ Pressure oscillations
Selective ES/NS-FEM
F-barES-FEM

## Slide 33: Deformed shapes and pressure distributions
NS-FEM
NS-FEM shows strange shapes in large deformed part
✗strange shapes

## Slide 34: Summary

## Slide 35: Summary
Characteristics of S-FEMs are summarized like them.
Selective ES/NS-FEM
Dynamic: with little pressure oscillation, temporary stable.
Modal : high accuracy
Constitutive equations are restricted.
F-barES-FEM
Dynamic: with no pressure oscillation, temporary unstable.
Modal : high accuracy, imaginary part of natural frequencies.
It is restricted to short-term analysis.
Thank you for your kind attention.

## Slide 36
Appendix

## Slide 37: B-barES-FEM
F-barES-FEM
B-barES-FEM
derived from ES-FEM
derived from

## Slide 38: Cantilever Bending Analysis
Small deformation static analysis
Compare B-barES-FEM with ABAQUS C3D20H

## Slide 39: Pressure distributions
ABAQUS C3D20H
Reference
B-barES-FEM(1)
Reference

## Slide 40: Pressure distributions
ABAQUS C3D20H
Reference
B-barES-FEM(2)
Reference

## Slide 41: Pressure distributions
ABAQUS C3D20H
Reference
B-barES-FEM(3)
Reference

## Slide 42: Pressure distributions
ABAQUS C3D20H
Reference
B-barES-FEM(4)
Reference

## Slide 43: Propagation of 1D pressure wave
Outline
Small deformation analysis.
Linear elastic material, Young’s modulus: 200 GPa, Poisson’s ratio: 0.0, Density: 8000 kg/m3.
Results of F-barES-FEM(0), (1), (2), and (3) are compared to the analysical solution.

## Slide 44: Propagation of 1D pressure wave
Results

## Slide 45: Velocity Verlet Method
Algorithm
Calculate the next displacement as
.
Calculate the next acceleration as
.
Calculate the next velocity as
Characteristics
2nd order symplectic scheme in time.
Less energy divergence.

## Slide 46: Cause of energy divergence
Due to the adoption of F-bar method, the stiffness matrix becomes asymmetric and thus the dynamic system turns to unstable.
Equation of natural vibration, , derives an eigen equation, , which has asymmetric left-hand side matrix.
Some of eigen frequencies could be complex numbers.
When an angular frequency （）, the time variation of the th mode is
Divergent term!

## Slide 47: Deformed shapes and sign of pressure
ABAQUS/Explicit C3D4
(Standard T4 element)
✗ Pressure oscillation in iron ears
A rubber parts is a “bad apple” when Standard T4 elements are used.
In a later stage
✔ No pressure oscillation in iron ears
It should be noted that a presence of rubber spoils over all accuracy of the analysis with Standard T4 elements.
F-barES-FEM