## Slide 1: F-bar aided edge-based smoothed finite element methods with 4-node tetrahedral elements for static large deformation hyperelastic and elastoplastic problems
Yuki ONISHI, Ryoya IIDA, Kenji AMAYA Tokyo Institute of Technology, Japan

## Slide 2: Motivation
Motivation
  We want to accurately and stably analyze severe large deformation of solids in any shape with finite elements.
Issues
  Only tetra mesh is available for arbitrary body shape.
  The standard 1st / 2nd order tetrahedral element are poor especially when incompressibility is present. Also, all the other u/p hybrid tetrahedral elements (e.g., C3D4H, C3D10MH in ABAQUS) have some issues:
    pressure oscillation,
    early convergence failure, etc.
  Researches on FE formulations for 1st order tetra (T4) are still active especially for rubber-like or elasto-plastic materials.

## Slide 3: An Example for Rubber-like Material
Material: neo-Hookean hyperelastic,
1st order hybrid T4 (C3D4H)
 No shear/volumetric locking
✗ Pressure oscillation
✗ Corner locking
2nd order modified hybrid T10 (C3D10MH)
 No shear/volumetric locking
✗ Low interpolation accuracy ✗ Early convergence failure
# of Nodes is almost the same.
Pressure
Pressure

## Slide 4: An Example for Rubber-like Material
Material: neo-Hookean hyperelastic,
Selective ES/NS-FEM-T4
 No shear/volumetric locking
✗ Pressure oscillation ✗ Corner locking
Selective ES/NS-FEM-T4 is not bad as ABAQUS C3D4H. Yet, it still has major issues…
# of Nodes is exactly the same as the C3D4H case.

## Slide 5: Objective
Propose a new type of S-FEM, F-barES-FEM-T4, to resolve the pressure oscillation and the corner locking issues in hyperelastic and elastoplastic materials.
Table of Body Contents
Methods: Quick introduction of F-barES-FEM-T4
Results: A few example analyses
Summary

## Slide 6
Methods
Quick introduction of F-barES-FEM-T4 (F-barES-FEM-T3 in 2D is explained for simplicity.)

## Slide 7: Quick Review of Node-based S-FEM (NS-FEM)
Algorithm:
Calculate the deformation gradient at each element, , as usual.
Distribute s to the connecting nodes with area weights to make at each node.
Use s to calculate the stress, nodal force and so on.
NS-FEM avoids shear & volumetric locking in T3/T4 elements and also alleviates pressure oscillation. Yet, it suffers from spurious low-energy modes, corner locking and minor pressure oscillation….
For triangular (T3) or tetrahedral (T4) elements.

## Slide 8: Quick Review of Edge-based S-FEM (ES-FEM)
Algorithm:
Calculate the deformation gradient at each element, , as usual.
Distribute s to the connecting edges with area weights to make at each edge.
Use s to calculate the stress, nodal force and so on.
ES-FEM avoids shear locking in T3/T4 elements. Yet, it suffers from volumetric locking, corner locking, and major pressure oscillation…
For triangular (T3) or tetrahedral (T4) elements.

## Slide 9: Quick Introduction of F-barES-FEM
Concept: combine ES-FEM and NS-FEM using F-bar method
Outlline
is given by ES-FEM.
is given by cyclically applied NS-FEM.
is calculated in the manner of F-bar method:
.

## Slide 10: Outline of F-barES-FEM
Brief Formulation
Calculateas usual.
Smooth at nodes and get.
Smooth at elements and get.
Repeat 2. and 3. as necessary ( times).
Smooth at edges to make .
Combine and of ES-FEM as
.
Cyclic Smoothing of
Hereafter, F-barES-FEM-T4 with cycles of smoothing is called “F-barES-FEM-T4()”.
( layers of ~)
A kind of low-pass filter for

## Slide 11: Additional Point of F-barES-FEM
Typical Flow of FE Solver
Selective ES/NS-FEM splits into and and merges and into .
F-barES-FEM builds and separately and combines and into .
F-barES-FEM can handle any kind of material constitutive model.
Deformation Gradient
Cauchy Stress
Internal Force
constitutive model
domain integration
deformation evaluation
Displace-ment

## Slide 12
Results
A few example analyses

## Slide 13: Compression of Rubber Block
Outline
Arruda-Boyce hyperelastic material ().
Applying pressure on ¼ of the top face.
Compared to ABAQUS C3D4H with the same unstructured T4 mesh.
Load

## Slide 14: Compression of Rubber Block
Pressure Distribution
ABAQUS C3D4H
F-bar ES-FEM-
T4(2)
Early stage Middle stage Later stage

## Slide 15: Compression of Rubber Block
Pressure Distribution
Early stage Middle stage Later stage
F-bar ES-FEM- T4(3)
F-bar ES-FEM- T4(4)
F-barES-FEM-T4 resolves the pressure oscillation issue!

## Slide 16: Barreling of 1/8 Rubber Cylinder
Outline
Neo-Hookean hyperelastic material ().
Enforced displacement is applied to the top surface.
Compared to ABAQUS C3D4H with the same unstructured T4 mesh.

## Slide 17: Barreling of 1/8 Rubber Cylinder
Result of F-bar ES-FEM(2) (Pressure)
50% nominal compression
Almost smooth
pressure
distribution is obtained
except just around the rim.

## Slide 18: Barreling of 1/8 Rubber Cylinder
Pressure Distribution
ABAQUS C3D4H
F-bar ES-FEM-
T4(3)
F-bar ES-FEM-
T4(4)
F-bar ES-FEM- T4(2)
F-barES-FEM-T4 with a sufficient cyclic smoothing resolves the corner locking issue!
Strange deformation (corner locking) around the rim

## Slide 19: Shearing & Tensioning of Elasto-Plastic Bar
P. 19
Outline
Blue face is perfectly constrained.
Red face is constrained in plane and pressed down.
Compared to ABAQUS C3D4H with the same unstructured T4 mesh.
Elasto-plastic material:
Hencky elasticity with and .
Isotropic von Mises yield criterion with and (constant).
1.2 k nodes & 4.8 k elems.

## Slide 20: Shearing & Tensioning of Elasto-Plastic Bar
Result of F-bar ES-FEM (Equiv. Plastic Strain)

## Slide 21: Shearing & Tensioning of Elasto-Plastic Bar
P. 21
Equivalent Plastic Strain
F-barES-FEM-T4
ABAQUS C3D4H
There is minor oscillation.
Smooth distribution.

## Slide 22: Shearing & Tensioning of Elasto-Plastic Bar
P. 22
Equivalent Plastic Strain
F-barES-FEM-T4
ABAQUS C3D4H
Accuracy of equivalent plastic strain seems no much different.

## Slide 23: Shearing & Tensioning of Elasto-Plastic Bar
P. 23
Pressure
F-barES-FEM-T4
ABAQUS C3D4H
Smooth distribution.
There is major oscillation.

## Slide 24: Shearing & Tensioning of Elasto-Plastic Bar
P. 24
Pressure
F-barES-FEM-T4 is pressure oscillation free in elastoplastic analysis.
F-barES-FEM-T4
ABAQUS C3D4H

## Slide 25: Twist of Rubber/Aluminium Composite Plate
Outline
Bottom face is perfectly constrained.
Top face is constrained in the plane and twisted 360 deg. around the vertical axis.
Calculated by F-barES-FEM-T4 only. (Just a demo.)
Multiple s at edges on the material interface.
3 k nodes & 14 k elems.
[Aluminium]
Hencky elasticity: ， .
Isotropic von Mises plasticity: ， (const.),
[Rubber]
Neo-Hook Hyperelasticity: ,

## Slide 26: Twist of Rubber/Aluminium Composite Plate
Seems valid.
Result of F-bar ES-FEM-T4 Equivalent Plastic Strain

## Slide 27: Twist of Rubber/Aluminium Composite Plate
No pressure oscillation.
Result of F-bar ES-FEM-T4 Pressure

## Slide 28: Twist of Rubber/Aluminium Composite Plate
Discontinuous .
No strain smoothing across material interfaces.
Result of
F-bar ES-FEM-T4 Deformation Gradient

## Slide 29
Summary

## Slide 30: Benefits and Drawbacks of F-barES-FEM-T4
Benefits
  Locking-free with 1st order tetra meshes.
  No difficulty in severe strain or contact analysis.
  No increase in DOF.
  Purely displacement-based formulation.
  No restriction of material constitutive model. Pressure dependent models are acceptable.
  Less corner locking and pressure oscillation.
Drawbacks
✗ The more cyclic smoothing necessitates the more CPU time due to the wider bandwidth.
More accurate than Selective ES/NS-FEM!
Slower than Selective ES/NS-FEM…

## Slide 31: FYI
If you are interested in F-barES-FEM-T4, please refer to the following paper:
“F-bar aided edge-based smoothed finite element method using tetrahedral elements for finite deformation analysis of nearly incompressible solids, International Journal for Numerical Methods in Engineering (IJNME), Jul. 2016.
Thank you for your kind attention!