## Slide 1: A stabilization method of F-barES-FEM-T4 for dynamic explicit analysis of nearly incompressible solids
Ryoya IIDA, Yuki ONISHI, Kenji AMAYA
Tokyo Institute of Technology, Japan

## Slide 2: Background
Our group has proposed new FEM formulation named F-bar aided edge-based smoothed finite element method with tetrahedral elements (F-barES-FEM-T4).
ABAQUS C3D4H
✗ pressure oscillation
F-barES-FEM-T4(3)
# of cyclic smoothings
Our method shows excellent accuracy in static problems!

## Slide 3: Drawbacks in explicit dynamics
Highly accurate results are restricted to short-term analysis.
F-barES-FEM-T4 causes energy divergence.
time
ABAQUS/Explicit
C3D8
Reference
F-barES-FEM
-T4(2)
Cantilever bending analysis

## Slide 4: Cause of energy divergence
Due to the adoption of F-bar method, the stiffness matrix becomes asymmetric.
Equation of Motion:
Asymmetric stiffness matrix gives rise to imaginary part of natural frequencies and thus causes energy divergence (instability) in dynamic problem.
asymmetric
To realize long-term analysis,
stiffness matrix must be symmetrized.

## Slide 5: Objective
Objective
To stabilize F-barES-FEM-T4 in explicit dynamics
for nearly incompressible materials.
Table of Body Contents
Methods: Quick introductions of F-barES-FEM-T4 and stabilized method
Results & Discussion: A few verification analyses
Summary

## Slide 6: Methods
Notes: Then we will explain our proposed method

## Slide 7: Procedure of F-barES-FEM (1 of 2)
ES-FEM
Deformation gradient of each edge, is derived as

## Slide 8: Procedure of F-barES-FEM (2 of 2)
Each part of is calculated as
(1)
Isovolumetric part
Smoothing the value of adjacent elements.
↓
The same manner as
ES-FEM
(1)Calculating node’s value by smoothing
the value of adjacent elements
(2)Calculating elements’ value by smoothing
the value of adjacent nodes
(3)Repeating (1) and (2) a few times
(2)
Volumetric part

## Slide 9: Advantages of F-barES-FEM
Like a ES-FEM
1. Shear locking free
Like a NS-FEM
2. Little pressure oscillation
3. Volumetric locking free with the aid of F-bar method
Isovolumetric part
Volumetric part
This formulation is designed to have 3 advantages.

## Slide 10: Construction of internal force vector
Internal force vector of F-barES-FEM-T4 is calculated as followings:
Combination of , and causes asymmetric stiffness matrix and thus causes energy divergence.
-matrix of ES-FEM
Stress derived from
Defenition of in the same fashion as F-bar method
of ES-FEM

## Slide 11: Proposed method: SymF-barES-FEM-T4
We modify the internal force vector in order to realize stabilization as followings:
-matrix
Derived from
Stress
derived from
volume
derived as
F-barES-FEM-T4
SymF-barES-FEM-T4
Proposed
We named this formulation SymF-barES-FEM-T4.

## Slide 12: Concept of SymF-barES-FEM-T4
The replacement to means to symmetrize stiffness matrix as standard FEM.
The replacement to is natural extension of volume term and introduced empirically.
-matrix
Derived from
Stress
derived from
volume
derived as
SymF-barES-FEM-T4
Proposed

## Slide 13: Result & Discussion

## Slide 14: #1 Bending of a cantilever
Dynamic explicit analysis.
Neo-Hookean material Initial Young’s modulus: 6.0 MPa, Initial Poisson’s ratio: 0.49, Density: 920 kg/m3.
Compare the results of SymF-barES-FEM-T4, F-barES-FEM-T4 and Selective H8 (ABAQUS/Explicit C3D8) elements.

## Slide 15: Inability of standard T4 element
ABAQUS/Explicit C3D4
Standard T4 element
✗Pressure oscillation and locking
Standard T4 element is useless!
at s (pressure distribution)
ABAQUS/Explicit C3D8
(Selective H8 element)
Reference

## Slide 16: Time history of deformed shapes
SymF-barES-FEM-T4(2)
(Proposed method)
✔ Less pressure oscillation
✔ No locking
✔ No energy divergence
ABAQUS/Explicit C3D8
(Selective H8 element)
Reference
F-barES-FEM-T4(2)
✔ No pressure oscillation
✔ No locking
✗ Energy divergence

## Slide 17: Time history of total energy
SymF-barES-FEM-T4 can suppress energy divergence!
SymF-barES-FEM-T4
(Proposed)
F-barES-FEM-T4
150,000 time steps

## Slide 18: Deformed shapes and pressure distributions
at s
Proposed method can give acceptable pressure distribution.
F-barES-FEM-T4(2)
✔ No pressure oscillation
✔ No locking
✗ Energy divergence
ABAQUS/Explicit C3D8
(Selective H8 element)
Reference
SymF-barES-FEM-T4(2)
(Proposed method)
✔ Less pressure oscillation
✔ No locking
✔ No energy divergence

## Slide 19: Time history of displacement
Proposed method shows good result without locking.
The accuracy of displacement does not depend on the number of cyclic smoothings as well as F-baES-FEM-T4.
Standard T4
Proposed &
Reference

## Slide 20: #2 Cantilever twisting analysis
Dynamic explicit analysis.
Twisting initial velocity fields:
Neo-Hookean material
Initial Young’s modulus: 17.0 MPa, Initial Poisson’s ratio: 0.49, Density: 1100 kg/m3.
Compare the results of
SymF-barES-FEM-T4, F-barES-FEM-T4,
and Selective H8

## Slide 21: Time history of deformed shapes
F-barES-FEM-T4(2)
✔ No pressure oscillation
✔ No locking
✗ Energy divergence
ABAQUS/Explicit C3D8
(Selective H8 element)
Reference
SymF-barES-FEM-T4(2)
(Proposed method)
✔ Less pressure oscillation
✔ No locking
✔ No energy divergence

## Slide 22: Time history of total energy
SymF-barES-FEM-T4 can suppress energy divergence!
F-barES-FEM-T4
SymF-barES-FEM-T4
(Proposed)
60,000 time steps

## Slide 23: Effect of cyclic smoothings
F-barES-FEM-T4
SymF-barES-FEM-T4
(Proposed method)
#cyclic
smoothings
1
2
3
1
2
3
The increase in cyclic smoothings no longer improves distribution
unlike F-barES-FEM-T4

## Slide 24: Time history of displacement
Standard T4
Proposed
Proposed methods can show as good result as F-barES-FEM-T4

## Slide 25: #3 Swinging of Bunny Ears
Outline
Iron ears: , Neo-Hookean, No cyclic smoothing.
Rubber body: , Neo-Hookean, 1 cycle of smoothing.
Compared to ABAQUS/Explicit C3D4. No Hex mesh available!
Iron Ears
Rubber Body
Fixed
Initial Velocity of Iron Ears

## Slide 26: Time histories of deformed shapes
SymF-barES-FEM-T4(1)
(Proposed method)
ABAQUS/Explicit C3D4
(Standard T4 element)
✗ Pressure oscillation
✗ Locking
✔ No energy divergence
✔ Less pressure oscillation ✔ No locking
✔ No energy divergence
F-barES-FEM-T4(1)
✔ No pressure oscillation
✔ No locking
✗ Energy divergence

## Slide 27: Deformed shapes and sign of pressure
Our method represents pressure waves appropriately!
SymF-barES-FEM-T4(1)
(Proposed method)
✔ Pressure waves
ABAQUS/Explicit C3D4
(Standard T4 element)
In an early stage
✗ Pressure oscillations
F-barES-FEM-T4(1)

## Slide 28: Summary

## Slide 29: Summary
SymF-barES-FEM-T4 was proposed in order to realize accurate and stable dynamic explicit analysis.
Proposed method realizes ✔ Less pressure oscillation ✔ No locking ✔ No energy divergence
Further improvement for perfect suppression of pressure oscillation is our future work.
Thank you for your kind attention.
Notes: まとめです
今後は接触を考慮した問題への拡張を中心に、研究を進めていくつもりです。