## Slide 1: Selective cell-based smoothed finite element method using 10-node tetrahedral elements for large deformation of nearly incompressible solids
Yuki ONISHI Tokyo Institute of Technology, Japan

## Slide 2: Motivation
What we want to do:
Solve hyper large deformation analyses accurately and stably.
Treat complex geometries with tetrahedral meshes.
Consider nearly incompressible materials .
Support contact problems.
Handle auto re-meshing.
Rubber
Plastic/Glass
Metal

## Slide 3: Issues
Conventional tetrahedral (T4/T10) FE formulations still have issues in accuracy or stability especially in nearly incompressible cases.
2nd or higher order elements: ✗ Volumetric locking. Accuracy loss in large strain due to intermediate nodes.
B-bar method, F-bar method, Selective reduced integration: ✗ Not applicable to tetrahedral element directly.
F-bar-Patch method: ✗ Difficulty in building good-quality patches.
u/p mixed (hybrid) method: (e.g., ABAQUS/Standard C3D4H and C3D10MH) ✗ Pressure checkerboarding, Early convergence failure etc..
F-bar type smoothed FEM (F-barES-FEM-T4):  Accurate & stable ✗ Hard to implement in FEM codes.

## Slide 4: Issues (cont.)
E.g.) Compression of neo-Hookean hyperelastic body with
1st order hybrid T4 (C3D4H)
 No volumetric locking
✗ Pressure checkerboarding
✗ Shear & corner locking
2nd order modified hybrid T10 (C3D10MH)
 No shear/volumetric locking ✗ Early convergence failure
✗ Low interpolation accuracy
# of Nodes is almost the same.
Pressure
Pressure

## Slide 5: Issues (cont.)
E.g.) Compression of neo-Hookean hyperelastic body with
F-barES-FEM-T4  No shear/volumetric locking
 No corner locking  No pressure checkerboarding
Same mesh as C3D4H case.
Pressure
Although F-barES-FEM-T4 is accurate and stable, ✗ it cannot be implemented in general-purpose FE software due to the adoption of ES-FEM.
Another approach adopting CS-FEM with T10 element would be effective.

## Slide 6: Objective
To propose an accurate and stable CS-FEM-T10, “SelectiveCS-FEM-T10”, and to implement it into general-purpose FE software.
Table of Body Contents
Formulation of SelectiveCS-FEM-T10
Demonstrations of SelectiveCS-FEM-T10
Implementation of SelectiveCS-FEM-T10 into ABAQUS
Summary

## Slide 7
Formulation of SelectiveCS-FEM-T10

## Slide 8: Brief Review of Edge-based S-FEM (ES-FEM)
Calculate at each element as usual.
Distribute to the connecting edges with area weight and build .
Calculate etc. in each edge smoothing domain.
As if putting an integration point on each edge center
ES-FEM can avoid shear locking. However, it cannot be implemented in ordinary FE codes due to the strain smoothing across multiple elements...

## Slide 9: (1) Subdivision into T4 Sub-elements
Put a dummy node (10) at the mean location of 6 mid-nodes.
Subdivide a T10 element into twelve T4 sub-elements and calculate their B-matrices and strains.
The shape function should not be quadratic in large deformation analyses.
Same as J.T.Ostien’s method. (IJNME, v107, 2016)

## Slide 10: (2) Deviatoric Strain Smoothing
Perform strain smoothing in the manner of ES-FEM (i.e., average dev. strains of sub-elements at edges). Then…
T4 sub-elements cause shear locking and thus
strain smoothing is necessary.
From 12 sub-elements to 30 edges

## Slide 11: (2) Deviatoric Strain Smoothing (cont.)
Perform one more strain smoothing in the reverse direction (i.e., average dev. strains of edges at sub-elements), which is so to speak (ES-FEM)-1.
ES-FEM does not smooth the strain at frame edges. Thus one more smoothing is necessary.
From 30 edges to 12 sub-elements

## Slide 12: (3) Volumetric Strain Smoothing
Treat the overall mean vol. strain of all sub-elements as the uniform element vol. strain (i.e., same approach as SRI elements).
The spatial order of vol. strain should be lower than that of dev. strain to avoid volumetric locking.

## Slide 13: (4) Combining with SRI Method
Apply SRI method to combine the Dev. & Vol. parts and obtain and .
Deviatoric
Volumetric
Internal force
Stiffness

## Slide 14: Flowchart of SelectiveCS-FEM
Explanation in 2D (6-node triangular element) for simplicity
(1) Subdivision with a dummy node
(2) Dev. strain smoothing with edges and sub-elements
(3) Vol. strain smoothing with all sub-elements
(4)
ES-FEM
(ES-FEM)-1
Overall mean
SRI

## Slide 15
Demonstration of SelectiveCS-FEM-T10

## Slide 16: Barreling of Hyperelastic Cylinder
Outline
Enforce axial displacement on the top face.
Neo-Hookean body with ．
Compare results with ABAQUS T10 hybrid elements (C3D10H, C3D10MH, C3D10HS) using the same mesh.

## Slide 17: Barreling of Hyperelastic Cylinder
Animation of Mises stress (ABAQUS C3D10MH)
Convergence failure at 24% compression
Unnaturally oscillating distributions are obtained around the rim.

## Slide 18: Barreling of Hyperelastic Cylinder
Animation of Mises stress (Selective CS-FEM-T10)
Convergence failure at 47% compression
Smooth distributions
are obtained except around the rim.
The present element is more stable than ABAQUS C3D10MH

## Slide 19: Barreling of Hyperelastic Cylinder
Comparison of Mises stress at 24% comp.
Selective CS-FEM-T10
ABAQUS C3D10MH
ABAQUS C3D10HS
ABAQUS C3D10H
All results are similar to each other except around the rim having stress singularity.

## Slide 20: Barreling of Hyperelastic Cylinder
Comparison of pressure at 24% comp.
Selective CS-FEM-T10
ABAQUS C3D10MH
ABAQUS C3D10HS
ABAQUS C3D10H
All results are similar to each other except around the rim having stress singularity.

## Slide 21: Barreling of Hyperelastic Cylinder
Comparison of nodal reaction force at 24% comp.
Selective CS-FEM-T10
ABAQUS C3D10MH
ABAQUS C3D10HS
ABAQUS C3D10H
ABAQUS C3D10H and C3D10HS suffer from nodal force oscillation.

## Slide 22: Barreling of Hyperelastic Cylinder
Comparison of pressure at 47% comp.
SelectiveCS-FEM-T10
ABAQUS C3D8
The present element has competitive accuracy and stability as much as H8-SRI element.
# of nodes are about 60k in both.
Conv. failure
at 50% comp.

## Slide 23
Implementation of SelectiveCS-FEM-T10 into ABAQUS

## Slide 24: Brief of ABAQUS UEL
ABAQUS has functionality of “user-defined element” (simply called “UEL”).
UEL is usually written in Fortran77, but in fact it can be written in Fortran90.
Coding a subroutine named “UEL” and compiling it, one can execute ABAQUS using one’s own element:
% abaqus job=test user=my_uel.o
Analysis results can be visualized on ABAQUS Viewer by defining overlap elements with zero stiffness in the “inp” file.

## Slide 25: Results of ABAQUS UEL
Comparison of Mises stress (24% comp.)
Selective CS-FEM-T10 of in-house code
Selective CS-FEM-T10 of ABAQUS UEL
Well agreed with in-house code.
Small difference comes form the difference of mapping calculation.

## Slide 26: Results of ABAQUS UEL
Comparison of pressure (24% comp.)
Selective CS-FEM-T10 of in-house code
Selective CS-FEM-T10 of ABAQUS UEL
Well agreed with in-house code.
Small difference comes form the difference of mapping calculation.

## Slide 27: Issues in ABAQUS UEL
We have to define the overlap elements
  to visualize the results with ABAQUS Viewer.
  to define element-based surface for pressure loading, contact pair definition etc..
The overlap elements cause convergence failure in large deformation analysis. i.e., the cylinder barreling analysis stops at 24% compression when the overset elements are defined.
Native implementation is essential for the full use of SelectiveCS-FEM-T10, unfortunately…

## Slide 28
Summary

## Slide 29: Summary of SelectiveCS-FEM-T10
Benefits
  Locking-free.
  No pressure checkerboarding.
  No nodal force oscillation.
  No increase in DOF.
  Long lasting in large deformation.
  Same CPU cost as the standard T10 elements.
Drawbacks
✗ No longer a T4 formulation.
Take-home message
Please consider implementing SelectiveCS-FEM-T10 to your in-house code. It’s supremely useful & easy to code!!
Thank you for your kind attention!