## Slide 1: An Optimal Multiple Smoothing Scheme of Selective Cell-based Smoothed Finite Element Methods with 10-node Tetrahedral Elements for Large Deformation of Nearly Incompressible Solids
Yuki ONISHI Tokyo Institute of Technology, Japan

## Slide 2: Motivation
What we want to do:
Solve hyper large deformation analyses accurately and stably.
Treat complex geometries with tetrahedral meshes.
Consider nearly incompressible materials .
Support contact problems.
Handle auto re-meshing.
Rubber
Plastic/Glass
Metal

## Slide 3: Issues
Conventional tetrahedral (T4/T10) FE formulations still have issues in accuracy or stability especially in nearly incompressible cases.
2nd or higher order elements: ✗ Volumetric locking. Accuracy loss in large strain due to intermediate nodes.
B-bar method, F-bar method, Selective reduced integration: ✗ Not applicable to tetrahedral element directly.
F-bar-Patch method: ✗ Difficulty in building good-quality patches.
u/p mixed (hybrid) method: (e.g., ABAQUS/Standard C3D4H and C3D10MH) ✗ Pressure checkerboarding, Early convergence failure etc..
F-bar type smoothed FEM (F-barES-FEM-T4):  Accurate & stable ✗ Hard to implement in FEM codes.

## Slide 4: Issues (cont.)
E.g.) Compression of neo-Hookean hyperelastic body with
1st order hybrid T4 (C3D4H)
 No volumetric locking
✗ Pressure checkerboarding
✗ Shear & corner locking
2nd order modified hybrid T10 (C3D10MH)
 No shear/volumetric locking ✗ Early convergence failure
✗ Low interpolation accuracy
# of Nodes is almost the same.
Pressure
Pressure

## Slide 5: Issues (cont.)
E.g.) Compression of neo-Hookean hyperelastic body with
Same mesh as C3D4H case.
Pressure
Although F-barES-FEM-T4 is accurate and stable, ✗ it cannot be implemented in general-purpose FE software due to the adoption of ES-FEM.
Also, it cosumes larger memory & CPU costs.
Another approach adopting CS-FEM with T10 element would be effective.
F-barES-FEM-T4  No shear/volumetric locking
 No corner locking  No pressure checkerboarding
 No increase in DOF

## Slide 6: Issues (cont.)
E.g.) Compression of neo-Hookean hyperelastic body with
SelectiveCS-FEM-T10 (Old Ver.)
 No shar/voluemetric locking
 Little corner locking  Little pressure checkerboarding  Same cost & userbility as T10 elements.
Same mesh as C3D10MH case.
As other S-FEMs, SelectiveCS-FEM-T10 has many varieties in the formulation.
The proposed method last year was not an optimal formulation yet.

## Slide 7: Objective
To find out an optimal formulation of SelectiveCS-FEM-T10
Table of Body Contents
Quick Introduction of ES-FEM, CS-FEM, and Old SelectiveES-FEM-T10
Formulation of New SelectiveCS-FEM-T10
Demonstrations of New SelectiveCS-FEM-T10
Summary

## Slide 8
Quick Introduction of ES-FEM, CS-FEM, and Old SelectiveCS-FEM-T10

## Slide 9: Brief Review of Edge-based S-FEM (ES-FEM)
Calculate at each element as usual.
Distribute to the connecting edges with area weight and build .
Calculate etc. in each edge smoothing domain.
As if putting an integration point on each edge center
ES-FEM can avoid shear locking. However, it cannot be implemented in ordinary FE codes due to the strain smoothing across multiple elements...

## Slide 10: Brief Review of Cell-based S-FEM (CS-FEM)
Subdivide each element into some sub-element.
Calculate at each sub-element.
Calculate etc. in each sub-element.
Implementable as an independent finite element.
Locking can be avoided with SRI etc..
As if putting an integration point on each sub-element

## Slide 11: Flowchart of Old SelectiveCS-FEM-T10
Explanation in 2D (6-node triangular element) for simplicity
(1) Subdivision with a dummy node
(2) Dev. strain smoothing with edges and sub-elements
(3) Vol. strain smoothing with all sub-elements
(4)
ES-FEM
ES-FEM-1
Overall mean
SRI

## Slide 12
Formulation of New SelectiveCS-FEM-T10

## Slide 13: Flowchart of New SelectiveCS-FEM-T10
Explanation in 2D (6-node triangular element) for simplicity
ES-FEM
SRI
(1) Subdivision without dummy nodes
(3) Vol. strain smoothing with all sub-elements
(2) Dev. strain smoothing at edges
(4)
No ES-FEM-1
Overall mean

## Slide 14: (1) Subdivision into T4 Sub-elements
Introduce no dummy node (i.e., asymmetric element).
Subdivide a T10 element into eight T4 sub-elements and calculate their B-matrices and strains.
The shape function should not be quadratic in large deformation analyses.

## Slide 15: (2) Deviatoric Strain Smoothing
Perform strain smoothing in the manner of ES-FEM (i.e., average dev. strains of sub-elements at edges).
Evaluate deviatoric strain and stress at edges.
From 8 sub-elements to 25 edges
T4 sub-elements cause shear locking and thus
strain smoothing is necessary.

## Slide 16: (3) Volumetric Strain Smoothing
Treat the overall mean vol. strain of all sub-elements as the uniform element vol. strain (i.e., same approach as SRI elements).
The spatial order of vol. strain should be lower than that of dev. strain to avoid volumetric locking.

## Slide 17: (4) Combining with SRI Method
Apply SRI method to combine the Dev. & Vol. parts and obtain and .
Deviatoric
Volumetric
Internal force
Stiffness
SRI

## Slide 18: Differences between Old and New
The new formulation has NO dummy node at the center of an element.
  Fewer sub-elements and edges.
  Asymmetric element.
The new formulation has No ES-FEM-1 after ES-FEM.
  Strain & stress evaluation at edges.
  No strain smoothing at frame edges.
Its reason has not revealed yet.
Intuitively, the lack of element symmetry and frame edge smoothing is not good for accuracy and stability; however, the new formulation is better in fact.

## Slide 19
Demonstration of New SelectiveCS-FEM-T10

## Slide 20: Bending of Hyperelastic Cantilever
Outline
Neo-Hookean hyperelastic material
Initial Poisson’s ratio:
Compared to ABAQUS C3D10MH (modified hybrid T10 element) with the same mesh.
Dead Load

## Slide 21: Bending of Hyperelastic Cantilever
Comparison of the deflection disp. at the final state
No volumetric locking is observed.
ABAQUS C3D10MH
New Selective CS-FEM-T10

## Slide 22: Bending of Hyperelastic Cantilever
Comparison of the pressure dist. at the final state
Almost the same pressure distributions with no checkerboarding.
ABAQUS C3D10MH
New Selective CS-FEM-T10

## Slide 23: Barreling of Hyperelastic Cylinder
Outline
Enforce axial displacement on the top face.
Neo-Hookean body with ．
Compare results with ABAQUS T10 hybrid elements (C3D10H, C3D10MH, C3D10HS) using the same mesh.

## Slide 24: Barreling of Hyperelastic Cylinder
Animation of Mises stress (ABAQUS C3D10MH)
Convergence failure at 24% compression
Unnaturally oscillating distributions are obtained around the rim.

## Slide 25: Barreling of Hyperelastic Cylinder
Animation of Mises stress (New Selective CS-FEM-T10)
Convergence failure at 43% compression
Smooth distributions
are obtained except around the rim.
The present element is more robust than ABAQUS C3D10MH

## Slide 26: Barreling of Hyperelastic Cylinder
Comparison of Mises stress at 24% comp.
New Selective CS-FEM-T10
ABAQUS C3D10MH
ABAQUS C3D10HS
ABAQUS C3D10H
All results are similar to each other except around the rim having stress singularity.

## Slide 27: Barreling of Hyperelastic Cylinder
Comparison of pressure at 24% comp.
New Selective CS-FEM-T10
ABAQUS C3D10MH
ABAQUS C3D10HS
ABAQUS C3D10H
All results are similar to each other except around the rim having stress singularity.

## Slide 28: Barreling of Hyperelastic Cylinder
Comparison of nodal reaction force at 24% comp.
New Selective CS-FEM-T10
ABAQUS C3D10MH
ABAQUS C3D10HS
ABAQUS C3D10H
ABAQUS C3D10H and C3D10HS suffer from nodal force oscillation.

## Slide 29: Compression of Hyperelastic Block
Outline
Arruda-Boyce hyperelastic material ().
Applying pressure on ¼ of the top face.
Compared to ABAQUS C3D10MH with the same unstructured T10 mesh.
Load

## Slide 30: Compression of Hyperelastic Block
Animation of pressure dist. (ABAQUS C3D10MH)
Convergence failure at 0.71 GPa pressure

## Slide 31: Compression of Hyperelastic Block
Animation of pressure dist. (New Selective CS-FEM-T10)
Convergence failure at 1.35 GPa pressure
The present element is more robust than ABAQUS C3D10MH

## Slide 32: Compression of Hyperelastic Block
Misess stress dist. at 0.7 GPa pressre
ABAQUS C3D10MH New SelectiveCS-FEM-T10
Less smoothed Mises stress is observed in New SelectiveCS-FEM-T10. Further improvement is still required.

## Slide 33
Summary

## Slide 34: Summary of SelectiveCS-FEM-T10
Benefits
  Accurate (no locking, no checkerboarding, no force oscillation).
  Robust (long-lasting in large deformation).
  No increase in DOF (No static condensation).
  Same memory & CPU costs as the other T10 elements.
  Implementable to commercial FE codes.
Drawbacks
✗ No longer a T4 formulation.
Take-home message
Please consider implementing SelectiveCS-FEM-T10 to your in-house code. It’s supremely useful & easy to code!!
Thank you for your kind attention!
Very close to practical use!!