## Slide 1: Smoothed Finite Element Methods: Recent Academic/Practical Progress
Yuki ONISHI Tokyo Institute of Technology, Japan

## Slide 2: Motivation of My S-FEM Researches
Our group is mainly interested in practical research topics for industrial applications.
Manufactured products usually have complex body shapes, which are difficult to be discretized with Hex meshes in FEA.
Tet meshes are easy to generate, but the analyses with conventional Tet elements are inaccurate.
We have started researching on smoothed FEM (S-FEM) with Tet meshes.
Only surface
mesh is shown.
Provided by SUZUKI Motor Co.

## Slide 3: What is S-FEM?
Smoothed finite element method (S-FEM) is a relatively new FE formulation proposed by Prof. G. R. Liu in 2006.
S-FEM is one of the strain smoothing techniques.
There are several types of classical S-FEMs depending on the domains of strain smoothing.
For example in 2D triangular mesh:
Standard FEM
Edge-based S-FEM (ES-FEM)
Node-based S-FEM (NS-FEM)

## Slide 4: What is S-FEM?
Number of journal papers written in English whose title contains “smoothed finite element”:
(inquired at Google Scholar)
The attraction of S-FEM is expanding continuously.

## Slide 5: Today’s Agendas
Part 1: Academic Progress of S-FEM in Large Deformation Analysis of Solids.
Part 2: Practical Progress of S-FEM in Electrodeposition Process Simulation of Auto Car Bodies.

## Slide 6
Part 1: Academic Progress of S-FEM in Large Deformation Analysis of Solids

## Slide 7: Motivation
What we want to do:
Solve hyper large deformation analyses accurately and stably.
Treat complex geometries with tetrahedral meshes.
Consider nearly incompressible materials .
Support contact problems.
Handle auto re-meshing.
Rubber
Plastic
Metal

## Slide 8: Issues
Conventional tetrahedral (T4/T10) FE formulations still have issues in accuracy or stability especially in nearly incompressible cases.
2nd or higher order elements: ✗ Volumetric locking. Accuracy loss in large strain due to intermediate nodes.
Enhanced assumed strain method (EAS): ✗ Spurious low-energy modes.
B-bar method, F-bar method, Selective reduced integration: ✗ Not applicable to tetrahedral element directly.
F-bar-Patch method: ✗ Difficulty in building good-quality patches.
u/p mixed (hybrid) method: (e.g., ABAQUS/Standard C3D4H and C3D10MH) ✗ Pressure checkerboarding etc..

## Slide 9: Issues (cont.)
E.g.) Compression of neo-Hookean hyperelastic body with
1st order hybrid T4 (C3D4H)
 No shear/volumetric locking
✗ Pressure checkerboarding
✗ Corner locking
2nd order modified hybrid T10 (C3D10MH)
 No shear/volumetric locking ✗ Early convergence failure
✗ Low interpolation accuracy
# of Nodes is almost the same.
Pressure
Pressure

## Slide 10: A Recent Solution: S-FEM
E.g.) Compression of neo-Hookean hyperelastic body with
F-barES-FEM-T4 (One of the latest S-FEM)  No shear/volumetric locking
 No corner locking  No pressure checkerboarding
 No increase in DOF (i.e., No static condensation)
Same mesh as C3D4H case.
Pressure

## Slide 11
Formulation of F-barES-FEM-T4

## Slide 12: Quick Intro. of Edge-based S-FEM (ES-FEM)
Calculate at each element as usual.
Distribute to the connecting edges with area weight and build .
Calculate etc. in each edge smoothing domain.
As if putting an integration point on each edge center
✗ Volumetric locking ✗ Pressure checkerboarding
No shear locking
No spurious modes

## Slide 13: Quick Intro. of Node-based S-FEM (NS-FEM)
Calculate at each element as usual.
Distribute to the connecting nodes with area weight and build .
Calculate etc. in each node smoothing domain.
As if putting an integration point on each node
✗ Spurious low-energy mode (or hour-glass mode)
Less pressure checkerboarding
No shear locking
No volumetric locking

## Slide 14: Concept of F-barES-FEM
Outlline
is given by ES-FEM.
is given by cyclically applied NS-FEM.
is calculated in the manner of F-bar method:
.
Concept: combining ES-FEM and NS-FEM using F-bar method

## Slide 15: Formulation of F-barES-FEM (1 of 2)
Deformation gradient of each edge () is derived as
in the manner of F-bar method.
ES-FEM

## Slide 16: Formulation of F-barES-FEM (2 of 2)
Each part of is calculated as
(1)
Isovolumetric part
Smoothing the value of adjacent elements.
(same manner as ES-FEM)
(1)Calculating node’s value by smoothing
the value of adjacent elements
(2)Calculating elements’ value by smoothing
the value of adjacent nodes
(3)Repeating (1) and (2) a few times
(2)
Volumetric part

## Slide 17: Advantages of F-barES-FEM
Like a ES-FEM
1. Shear locking free
Like a NS-FEM
2. Little pressure oscillation
3. Volumetric locking free with the aid of F-bar method
Isovolumetric part
Volumetric part
This formulation is designed to have 3 advantages.

## Slide 18
Demonstrations of F-barES-FEM-T4

## Slide 19: Compression of Rubber Block
Outline
Arruda-Boyce hyperelastic material ().
Applying pressure on ¼ of the top face.
Compared to ABAQUS C3D4H with the same unstructured T4 mesh.
Load
Static Implicit

## Slide 20: Compression of Rubber Block
Pressure dist.
ABAQUS C3D4H
Early stage Middle stage Later stage
Static Implicit
F-bar ES-FEM- T4(3)
Smooth pressure distributions are obtained.

## Slide 21: Shear-tensioning of Elasto-plastic Bar
P. 21
Outline
Blue face is perfectly constrained.
Red face is constrained in plane and pressed down.
Compared to ABAQUS C3D4H with the same unstructured T4 mesh.
Elasto-plastic material:
Hencky elasticity with and .
Isotropic von Mises yield criterion with and (constant).
1.2 k nodes & 4.8 k elems.
Static Implicit

## Slide 22: Shear-tensioning of Elasto-plastic Bar
Result of F-bar ES-FEM(2) (Equiv. plastic strain)
Static Implicit
Extreme large deformation with smooth strain dist. is successfully achieved.

## Slide 23: Shear-tensioning of Elasto-plastic Bar
P. 23
Equivalent plastic strain dist. in middle states
F-barES-FEM-T4(2)
ABAQUS C3D4H
There is minor oscillation.
Smooth distribution.
Static Implicit

## Slide 24: Shear-tensioning of Elasto-plastic Bar
P. 24
Pressure dist. in middle states
F-barES-FEM-T4(2)
ABAQUS C3D4H
Smooth distribution.
There is major oscillation.
Static Implicit

## Slide 25: Collapse Analysis of Viscoelastic Bunny
Outline
Applying gravity to the Stanford Bunny and let it collapsed by its self-weight.
Soft viscoelastic material .
Contact is NOT considered.
Comparing F-barES-FEM-T4(2) and ABAQUS C3D4H.
Viscous Implicit
# of nodes: 24136
# of elems: 126231

## Slide 26
Animation of Deformation
Because contact is not considered, the body penetrates the feet and finally becomes upside downside. The analysis lasts till the necking.
Viscous Implicit

## Slide 27: Collapse Analysis of Viscoelastic Bunny
Mises stress dist. when C3D4H get a convergence failure
ABAQUS C3D4H shows a stiffer result due to shear locking.
The result of F-barES-FEM-T4 would be better.
F-barES-FEM-T4(2)
ABAQUS C3D4H
Viscous Implicit

## Slide 28: Impact of Rubber Bunny
Outline
A bunny made of rubber (Neo-Hookean) is crushed to a rigid wall.
Compared with ABAQUS/Explicit C3D4 using a same T4 mesh.
Note that neither Hex mesh nor hybrid elements is not available in this problem.
Initial velocity
10 m/s
(uniform)
Rigid Wall
Contact condition
free-slip, free-separation
Dynamic Explicit
Rubber body

## Slide 29: Impact of Rubber Bunny
Animation of Pressure Dist.
Dynamic Explicit
ABAQUS/Explicit C3D4 ✗ Pressure Checkerboarding
✗ Shear Locking
SymF-barES- FEM-T4(1)
 Smooth pressure
 No Locking

## Slide 30: Impact of Rubber Bunny
Sign of Pressure at Initial Phase
The proposed S-FEM captures the pressure wave in a complex body successfully!!
SymF-barES-FEM-T4(1)
ABAQUS/Explicit C3D4
(Standard T4 element)
Dynamic Explicit
✗ Pressure Checkerboarding
✔ Pressure Wave

## Slide 31: Stretch of Filler-containing Rubber with Remesing
Several hard circular fillers are distributed in a square soft matrix rubber (neo-Hookean hyperelastic with ).
of the filler is 100 times larger than of the matrix.
Left side is constrained and right side is displaced.
Valid Mises stress dist. is obtained after many time remeshings.
Static Implicit

## Slide 32: Shear-tensioning of Elasto-plastic cylinder with Remeshing
Valid plastic strain dist. is obtained after many time remeshings.
Aluminium cylinder subjected to enforced disp..
Pure shear at the initial stage, but stretch dominates at the later stage.
Necking occurs in the end.
Final stretch at the neck is more than 7000%.
Static Implicit

## Slide 33: Characteristics of F-barES-FEM-T4
No increase in DOF. (No Lagrange multiplier. No static condensation.)
Locking- & checkerboarding-free with T4 mesh.
✗ Higher costs in memory and CPU time due to wider bandwidth of .
In case of standard unstructured T4 meshes:
Method | Approx. Bandwidth | Approx. Ratio
Standard FEM-T4 | 40 | 1
F-barES-FEM-T4(1) | 390 | x10
F-barES-FEM-T4(2) | 860 | x20
Another approach should be addressed for full industrial applications.

## Slide 34: Concept of SelectiveCS-FEM-T10
Our new another approach using T10 mesh.
Same memory & CPU costs as the T10 elements.
Details of SelectiveCS-FEM-T10 will be presented soon (10:40~) in the S-FEM MS at Room D today!!

## Slide 35
Part 2: Practical Progress of S-FEM in Electrodeposition Process Simulation of Auto Car Bodies

## Slide 36: What is Electrodeposition (ED) ?
Most widely-used basecoat methods for car bodies.
Making coated film by applying direct electric current (up to 300 V) in a paint pool.
Relatively good at making uniform film thickness but not satisfactory uniform in actual production lines.
ED simulator is necessary for the optimization of carbody design and coating conditions in actual lines.
+
-
Cathode
Anode
Paint
＋
＋
http://n-link.nissan.co.jp/NOM/PLANT/
Notes: What is electrodeposition.
Electrodeposition is the most widely-used ~~.
Coated film is made by applying direct electric current in a paint pool like this picture.
A carbody is cathode, while a paint pool is anode.
It is relatively good at making ~~.
So, ED simulator is necessary for ~~.

## Slide 37: Photos of ED Process Line
1. dipping and deposition process
2. water rinse process
3. baking process
We focus on this process.

## Slide 38: What is ED Simulation ?
ED simulation calculates film thickness derived from surface
potential and current density with moving boundaries.
Film Thickness
Surface Potential
Surface Current Density
Notes: This is an example of ED simulation results.
ED simulation ~~.
You can see that the paint film starts to be deposited from the outside surface.

## Slide 39: Issues in Meshing (1)
✗ It is difficult to discretize complex shapes such as car bodies with hexahedral meshes.
→ We have to use tetrahedral meshes in ED simulation.
However…

✗
Accuracy of the standard FEM-T4 is insufficient in complex shapes.
Only surface mesh is shown. Many holes exist on body plates
Notes: There are some issues in meshing.
First of all, it is difficult to represent complex shape ~~.
So, we have to ~~.
However, the accuracy of ~~.

## Slide 40: Issues in Meshing (2)
✗ 10-node tetrahedral (T10) mesh without kink generally requires more large number of nodes than T4 mesh.
T4 T10 without kink
For the same shape representation, T10 mesh without kink leads to massive increase in DOF.
Carbody
Carbody
hole
hole
Notes: This slide explains the issues about T10 mesh without kink.
Let’s say this gray part represents the surface of a carbody,
and this white circle represents a hole on the carbody.
If we mesh this parts using T4 and T10 without kink respectively,
the meshes would be like this.
As you can see, for the same ~~.

## Slide 41: Issues in Meshing (2 Cont.)
✗ 10-node tetrahedral (T10) mesh with kink causes severe accuracy loss.
T4 T10 with kink
T10 mesh with kink does not increase DOF but induces severe accuracy loss.
Kinked T10
Carbody
hole
Carbody
hole
Notes: This slide explains the issues about T10 mesh with kink.
10-node tetrahedral ~~.
The meshes using T4 and T10 with kink respectively would be like this.
T10 mesh with kink ~~.

## Slide 42: Motivation
Hexahedral elements: ✗ It is difficult to discretize complex shapes.
T10 elements without kink: ✗ It leads to massive increase in DOF.
T10 elements with kink: ✗ It causes severe accuracy loss.
→ We want to realize high accuracy analysis with T4 mesh.
ES-FEM-T4 could be a solution to these issues.
Notes: We cannot use these elements in ED simulation as I explained.
So we want to realize high accuracy analysis with T4 mesh.
ES-FEM-T4 could be a solution to these issues.

## Slide 43: Formulation of ES-FEM for ED Simulation
Notes: Next, I would like to explain about the formulation of ES-FEM for ED Simulation.

## Slide 44: Fundamental Equations
Governing equation
The electrostatic Laplace equation, , in the paint pool domain.
Boundary conditions (BCs)
Insulation BC
Anodic (Electrode surface) BC
Cathodic (Carbody surface) BC
ED boundary models are identified with lab experiments.
The role of ES-FEM is to solve the Laplace equation for each timestep with the iterative solver (MINRES).
+
-
Cathode
Anode
Paint
＋
＋
Notes: This is the fundamental equations.
The governing equation is the electrostatic Laplace equation.
ES-FEM solves this equation.
There are three boundary conditions.
Insulation boundary condition, Anodic boundary condition and cathodic ~~.
Anode means the electrode surface and cathode means the carbody surface.
These are identified ~~.
In our ED Simulation, current density is determined using ~~.

## Slide 45: Outline of ES-FEM
What is ES-FEM-T4?
A kind of strain smoothing method.
Using element edges as Gauss points.
Robust against element skew.
Super-linear mesh convergence rate with T4 mesh.
Standard FEM ES-FEM
Integration domain
Element
Node
assembles each element’s value.
assembles each edge’s value.
Integration domain is different !!
Notes: This is the outline of ES-FEM.
ES-FEM is a kind of strain ~~.
It uses element ~~.
It is robust ~~.
And it has super-linear convergence rate with T4 mesh.
The difference between conventional fem and ES-FEM is the integration domain.
FEM sums up ~~, while ES-FEM ~~.

## Slide 46: Analysis Results

## Slide 47: 4-Plate BOX Simulation
Outline
Imitating a bag-like structure such as side sill in a carbody.
Accuracy on the innermost surface (leftmost plate surface) is the most important; i.e., “maximize the minimum”.
Film thickness is calculated with 4 different mesh seed sizes and compared between FEM-T4 and ES-FEM-T4.
Film Thickness
(http://plaza.rakuten.co.jp/heroc)
Side Sill
4-P BOX

## Slide 48: 4-Plate BOX Simulation
Overview of Meshes
3.2 mm Mesh Seed Size (31k T4 elem.)
0.8 mm Mesh Seed Size (169k T4 elem.)
1.6 mm Mesh Seed Size (65k T4 elem.)
0.4 mm Mesh Seed Size (716k T4 elem.)
Only the surface meshes are shown.

## Slide 49: 4-Plate BOX Simulation
Film Thickness of G-Plate (innermost surface)
FEM results (dashed lines) have large errors due to mesh coarseness. Meanwhile, ES-FEM (solid lines) results have no such errors.
Mesh seed size

## Slide 50: 4-Plate BOX Simulation
Error of Final Film Thickness on G-Plate
ES-FEM-T4 has far better mesh convergence rate than FEM-T4 !!
The result of ES-FEM with the minimum mesh seed size (0.4 mm) is used as the reference.

## Slide 51: Carbody Simulation
Outline
A half carbody fixed in a box pool.
The side wall is treated as an anode surface.
Compare the time-developed film thickness between FEM-T4 and ES-FEM-T4 with a same mesh.
270 V
0 30 180 (s)

## Slide 52: Carbody Simulation
Overview of Surface Mesh
13M T4 elements (3M nodes & 18M edges) in total in the pool.
Provided by SUZUKI MOTOR Co.

## Slide 53: Carbody Simulation
Animation of Film Thickness (Clipped View on Side Sill)
Big difference appears on the inner surfaces.
As the 4-P BOX case, ES-FEM-T4 presents thinner dist. on the side sill.
FEM-T4
ES-FEM-T4

## Slide 54: Comparison of Computational Costs
Calculation Time
on a PC with Intel i9-9960X using 10 cores
 | FEM-T4 | ES-FEM-T4
4-P BOX with 3.2 mm mesh | 0.02 h | 0.02 h
4-P BOX with 1.6 mm mesh | 0.04 h | 0.05 h
4-P BOX with 0.8 mm mesh | 0.45 h | 0.45 h
4-P BOX with 0.4 mm mesh | 9.5 h | 9.0 h
Carbody | 67 h | 125 h
In case iterative solvers can be used, there is no big difference in calculation time although the accuracy of ES-FEM-T4 is much better.
Same Accuracy

## Slide 55
Summary

## Slide 56: Benefits and Drawbacks of S-FEMs
Benefits
  No increase in DOF.
  Purely displacement-based formulation.
  Locking- & checkerboarding-free with T4 mesh.
  No difficulty in severe strain or contact analysis.
  Super-linear mesh convergence rate. Suitable to for industrial problems with complex shape.
Drawbacks
✗ Larger memory consumption. Wider matrix bandwidth as T10 element with T4 mesh.

## Slide 57: Take-Home Messages
ES-FEM-T4 is already in practice as an accurate solver using T4 meshes to overcome the slow mesh convergence rate of the standard FEM-T4.
F-barES-FEM-T4 is the current best T4 FE formulation especially for the large deformation of rubber-like materials, viscoelastic materials, and elastoplastic materials.
Therefore, its practical use will be start shortly.
Details of SelectiveCS-FEM-T10 will be presented soon (10:40~) in the S-FEM MS at Room D today!!
Thank you for your kind attention!

## Slide 58
Appendix

## Slide 59: Natural Modes of ¼ Cylinder
Outline
Iron part: , Elastic, No cyclic smoothing.
Rubber part: , Elastic, 2 cycles of smoothing.
Compared to ABAQUS C3D4, C3D4H, and C3D8.
Eigen Mode
Fixed
In Plane Slide
In Plane Slide
Rubber Part
Iron Part

## Slide 60: Natural Modes of ¼ Cylinder
Eigen frequencies
C3D4 and C3D4H show higher frequencies (stiffer results).
F-barES-FEM-T4 and C3D8 are in good agreement.
1
Eigen Mode

## Slide 61: Natural Modes of ¼ Cylinder
ABAQUS C3D8
(reference)
F-barES-FEM-T4
The 1st modes are all the same as the reference solution.
Selective ES/NS-FEM-T4
NS-FEM-T4
1st eigen mode
Eigen Mode

## Slide 62: Natural Modes of ¼ Cylinder
ABAQUS C3D8
(reference)
F-barES-FEM-T4
NS-FEM-T4 shows strange results due to low-energy mode.
Selective ES/NS-FEM-T4 & F-barES-FEM-T4 are valid.
Selective ES/NS-FEM-T4
NS-FEM-T4
11th eigen mode
Eigen Mode