## Slide 1: SelectiveCS-FEM-T10 with Radial-type Mesh Subdivision
Yuki ONISHI Tokyo Institute of Technology, Japan
You can download this slide at http://nas.a.sc.e.titech.ac.jp/yonishi/slide/iccm2020-sfem-t10.pptx
This is DAY2, Room B, Session 2B-2: “S-FEM”.

## Slide 2: What is S-FEM?
Smoothed finite element method (S-FEM) is a relatively new FE formulation proposed by Prof. G. R. Liu in 2006.
S-FEM is one of the strain smoothing techniques.
There are several types of classical S-FEMs depending on the domains of strain smoothing.
For example in a 2D triangular mesh:
Standard FEM
Edge-based S-FEM (ES-FEM)
Node-based S-FEM (NS-FEM)

## Slide 3: What are the major pros of S-FEM?
Even when we use 4-node tetrahedral mesh:
Super-linear mesh convergence rate. (Almost same rate as the 2nd-order element.)
Shear locking free with ES-FEM. (Excellent with tetrahedral mesh.)
Little accuracy loss in skewed meshes. (No problem with complex geometry.)
S-FEM is a powerful method suitable for practical industrial applications.

## Slide 4: How popular is S-FEM?
Number of journal papers whose title contains “smoothed finite element”:
(inquired at Google Scholar)
The attraction of S-FEM is expanding continuously.

## Slide 5: Applications of S-FEMs in Our Lab
Solid mechanics (still in lab stage)
Static Implicit Dynamic Explicit Viscous Implicit
Electrostatic
(already in practice)
Electro Deposition

## Slide 6: Motivation
What we want to do in actuality:
Solve hyper large deformation analyses accurately and robustly.
Treat complex geometries with tetrahedral meshes.
Consider nearly incompressible materials .
Support contact problems.
Handle auto re-meshing.
Rubber
Plastic/Glass
Metal

## Slide 7: Issues
2nd or higher order elements: ✗ Volumetric locking. Accuracy loss in large strain.
B-bar/F-bar method, Selective reduced integration (SRI): ✗ Not applicable to tetrahedral element directly.
F-bar-Patch method: ✗ Difficulty in building good-quality patches.
u/p mixed (hybrid) method (ABAQUS C3D10MH etc.): ✗ Early convergence failure. Accuracy loss in large strain.
F-bar aided ES-FEM-T4 [Y.Onishi, IJNME, 109 (2017)] :  Accurate & robust ✗ Hard to implement in FEM codes.
SelectiveCS-FEM-T10 [Y.Onishi, IJCM, 17 (2020)] :  Accurate, robust & easy to implement. ✗ Not yet optimal.
Conventional tetrahedral (T4/T10) FE formulations still have issues in accuracy and/or robustness especially in nearly incompressible cases.

## Slide 8: Objective
To find an optimal formulation of SelectiveCS-FEM-T10 for severe large deformation analyses.
Table of Body Contents
Quick Review of Issues in Conventional Methods
Formulation of New SelectiveCS-FEM-T10
Demonstrations of New SelectiveCS-FEM-T10
Summary

## Slide 9: Quick Review of Issues in Conventional Methods

## Slide 10: Issues in Barreling Analysis of Rubber Cylinder
Neo-Hookean hyperelastic body with
1st order hybrid T4 (C3D4H)
 No volumetric locking
✗ Pressure checkerboarding
✗ Shear & corner locking
2nd order modified hybrid T10 (C3D10MH)
 No shear/volumetric locking ✗ Early convergence failure
✗ Low interpolation accuracy
# of Nodes is almost the same.
Pressure
Pressure

## Slide 11: Issues in Barreling Analysis of Rubber Cylinder
Neo-Hookean hyperelastic body with
Same mesh as C3D4H case.
Pressure
Although F-barES-FEM-T4 is accurate and robust,
it cosumes larger memory & CPU costs.
it cannot be implemented in general-purpose FE software due to the adoption of ES-FEM.
Another approach adopting CS-FEM with T10 element would be effective.
F-barES-FEM-T4  No shear/volumetric locking
 No corner locking  No pressure checkerboarding
 No increase in DOF
Y. Onishi, IJMNE, Vol. 109 (2017).

## Slide 12: Issues in Barreling Analysis of Rubber Cylinder
Neo-Hookean hyperelastic body with
SelectiveCS-FEM-T10 (Conventional Ver.)
 No shar/voluemetric locking
 Little corner locking  Little pressure checkerboarding  Same cost & userbility as T10 elements.
Same mesh as C3D10MH case.
As other S-FEMs, SelectiveCS-FEM-T10 has many varieties in the formulation.
The conventional method was not an optimal formulation yet.
Y. Onishi, IJCM, Vol. 17 (2020).
This study proposes New Selective CS-FEM-T10.

## Slide 13: Formulation of New SelectiveCS-FEM-T10

## Slide 14: Concepts of SelectiveCS-FEM-T10
Using T10 element and subdivide it into T4 sub-elements. Overcomes the weak points of intermediate nodes.
Adopting CS-FEM having no strain smoothing across multiple elements. Becomes an independent element of existing FE codes.
Applying selective reduced integration (SRI). Overcomes volumetric locking.

## Slide 15: Brief of Cell-based S-FEM (CS-FEM)
Subdivide each element into some sub-element.
Calculate at each sub-element.
Calculate etc. in each sub-element.
The biggest advantage of CS-FEM is its portability to existing FE codes.
As if putting an integration point on each sub-element

## Slide 16: Flowchart of New SelectiveCS-FEM-T10
Explanation in 2D (6-node triangular element) for simplicity
ES-FEM
SRI
(1) Subdivision into sub-elements with a dummy node
(3) Vol. strain smoothing with all sub-elements
(2) Dev. strain smoothing at edges
(4)
Overall mean
In case of 3D, there are varieties in mesh subdivision.

## Slide 17: Mesh Subdivision Types in 3D
Conventional subdivision (30% shrunk mesh)
Each frame edge is owned by only one sub-element.
Strain on frame edges are NOT smoothed by ES-FEM.
There are 12 sub-elements in total.

## Slide 18: Mesh Subdivision Types in 3D
New Radial-type subdivision (30% shrunk mesh)
Each frame edge is owned by two sub-elements.
Strain on all edges are smoothed by ES-FEM.
There are 16 sub-elements in total.
Sub-elements have a little larger skewness.

## Slide 19: Mesh Subdivision Types in 3D
Future extension: Radial-type for polyhedral mesh
It should be useful for mixture meshing such as ANSYS Mosaic Meshing.
Each frame edge is owned by two sub-elements.
There are 60 sub-elements in total.

## Slide 20: Demonstration of New SelectiveCS-FEM-T10

## Slide 21: Bending of Hyperelastic Cantilever
Outline
Neo-Hookean hyperelastic material
Initial Poisson’s ratio:
Compared to ABAQUS C3D10MH (modified hybrid T10 element) with the same mesh.
Dead Load
Static Implicit

## Slide 22: Bending of Hyperelastic Cantilever
Comparison of the pressure dist. at the final state
Almost the same pressure distributions with no checkerboarding. (No locking of course.)
ABAQUS C3D10MH
Static Implicit
New Selective CS-FEM-T10

## Slide 23: Bending of Hyperelastic Cantilever
Comparison of the Mises stress dist. at the final state
ABAQUS C3D10MH
Almost the same Mises stress distributions.
Static Implicit
ABAQUS C3D10MH
New Selective CS-FEM-T10

## Slide 24: Barreling of Hyperelastic Cylinder
Outline
Enforce axial displacement on the top face.
Neo-Hookean body with ．
Compare results with ABAQUS T10 hybrid elements (C3D10H, C3D10MH, C3D10HS) using the same mesh.
Static Implicit

## Slide 25: Barreling of Hyperelastic Cylinder
Animation of Mises stress (ABAQUS C3D10MH)
Convergence failure at 24% compression
Unnaturally oscillating distributions are obtained around the rim.
Static Implicit

## Slide 26: Barreling of Hyperelastic Cylinder
Animation of Mises stress (New Selective CS-FEM-T10)
Convergence failure at 47% compression
Smooth distributions
are obtained except around the rim.
The present element is more long-lasting (robust) than ABAQUS C3D10MH
Static Implicit

## Slide 27: Barreling of Hyperelastic Cylinder
Comparison of Mises stress at 24% comp.
New Selective CS-FEM-T10
ABAQUS C3D10MH
ABAQUS C3D10HS
ABAQUS C3D10H
All results are similar to each other except around the rim having stress singularity.
Static Implicit

## Slide 28: Barreling of Hyperelastic Cylinder
Comparison of pressure at 24% comp.
New Selective CS-FEM-T10
ABAQUS C3D10MH
ABAQUS C3D10HS
ABAQUS C3D10H
All results are similar to each other except around the rim having stress singularity.
Static Implicit

## Slide 29: Barreling of Hyperelastic Cylinder
Comparison of nodal reaction force at 24% comp.
New Selective CS-FEM-T10
ABAQUS C3D10MH
ABAQUS C3D10HS
ABAQUS C3D10H
ABAQUS C3D10H and C3D10HS suffer from nodal force oscillation.
Static Implicit

## Slide 30: Compression of Hyperelastic Block
Outline
Arruda-Boyce hyperelastic material ().
Applying pressure on ¼ of the top face.
Compared to ABAQUS C3D10MH with the same unstructured T10 mesh.
Load
Static Implicit

## Slide 31: Compression of Hyperelastic Block
Animation of pressure dist. (ABAQUS C3D10MH)
Convergence failure at 0.7 GPa pressure
Static Implicit

## Slide 32: Compression of Hyperelastic Block
Animation of Mises stress dist. (ABAQUS C3D10MH)
Convergence failure at 0.7 GPa pressure
Static Implicit

## Slide 33: Compression of Hyperelastic Block
Animation of pressure dist. (New Selective CS-FEM-T10)
Convergence failure at 3.3GPa pressure
Static Implicit
The present element is more long-lasting (robust) than ABAQUS C3D10MH

## Slide 34: Compression of Hyperelastic Block
Animation of Mises stress dist. (New Selective CS-FEM-T10)
The present element presents Mises stress oscillation.
Static Implicit

## Slide 35: Compression of Hyperelastic Block
Misess stress dist. at 0.7 GPa pressre
ABAQUS C3D10MH New SelectiveCS-FEM-T10
Less smooth Mises stress is observed in SelectiveCS-FEM-T10 compared to C3D10MH. Further improvement is still required.
Static Implicit

## Slide 36: Summary

## Slide 37: Characteristics of SelectiveCS-FEM-T10
Benefits
  Accurate (no locking, no checkerboarding, no force oscillation).
  Robust (long-lasting in large deformation).
  No increase in DOF (No static condensation).
  Same memory & CPU costs as the other T10 elements.
  Implementable to commercial FE codes (e.g., ABAQUS UEL).
Drawbacks
✗ Mises stress oscillation in some extreme analyses.
✗ No longer a T4 formulation.
SelectiveCS-FEM-T10 is competitive with the best ABAQUS T10 element, C3D10MH.

## Slide 38: Summary
Summary
The present method (New SelectiveCS-FEM-T10) is more robust than the conventional one.
The present method is already very good enough for practical use as compared to ABAQUS Tet elements.
Take-home message
Please consider implementing New SelectiveCS-FEM-T10 to your in-house code. It’s supremely useful & easy to code!!
FYI
You can download my slides at http://www.a.sc.e.titech.ac.jp/~yonishi/
Please contact me on yonishi@a.sc.e.titech.ac.jp.
Thank you for your kind attention!

## Slide 39: Appendix

## Slide 40: Flowchart of Old SelectiveCS-FEM-T10
Explanation in 2D (6-node triangular element) for simplicity
(1) Subdivision with a dummy node
(2) Dev. strain smoothing with edges and sub-elements
(3) Vol. strain smoothing with all sub-elements
(4)
ES-FEM
(ES-FEM)-1
Overall mean
SRI

## Slide 41: Differences between Old and New
The new formulation adopts radial-type mesh subdivision.
  Strain smoothing on all edges including frame edges.
  Larger skewness of sub-elements .
The new formulation has No ES-FEM-1 after ES-FEM.
  Strain & stress evaluation at edges (NOT at sub-elements).
Discussions
The old formulation is shorter-lasting than the new one probably because of the low-energy modes induced by the multiple smoothing (too much smoothing).
The new formulation does not need multiple smoothing because any edge is owned by multiple sub-elements.