## Slide 1: Explicit Dynamic Analysis using SelectiveCS-FEM-T10 with Radial Element Subdivision
Yuki ONISHI (Tokyo Institute of Technology)

## Slide 2: Applications of S-FEMs in Our Lab
Large deformation solid mechanics (still in academic)
Static Implicit Dynamic Explicit Viscous Implicit
Electrostatic (already in practice)
Carbody Electro Deposition
64 CPUs (512 cores)
MPI/OpenMP hybrid
140M elements
2000 timesteps
18.5 h wall time

## Slide 3: Motivation
What we want to do:
Solve severe large deformation analyses accurately and robustly.
Treat complex geometries with tetrahedral meshes.
Consider nearly incompressible materials .
Support contact problems.
Handle auto re-meshing.
Rubber
Plastic/Glass
Metal

## Slide 4: Issues (e.g., barreling analysis of rubber cylinder)
Neo-Hookean hyperelastic body with
2nd order modified hybrid T10 (ABAQUS C3D10MH)
 No shear/volumetric locking ✗ Short lasting (weak to severe deformation)
✗ Low interpolation accuracy
Pressure
With the best tetrahedral element in ABAQUS
T10: 10-node Tetrahedra

## Slide 5: Our Approach (e.g., barreling analysis of rubber cylinder)
Neo-Hookean hyperelastic body with
Latest S-FEM T10 (SelectiveCS-FEM-T10)
 No shear/volumetric locking  Less pressure checkerboarding  Long lasting (robust to severe deformation)  Same CPU time as T10 elements.
Same mesh & contour range as C3D10MH case.
Selective CS-FEM-T10 is much better than conventional tetrahedral elements in static analyses.
Y. Onishi, IJCM, (2021).
Further evaluation is necessary in dynamic analyses.
With the our latest S-FEM tetrahedral element

## Slide 6: Objective
Development of a dynamic version of SelectiveCS-FEM-T10
Evaluation of its accuracy and robustness in dynamic severe large deformation analyses.
Table of Body Contents
Methods: Formulation of SelectiveCS-FEM-T10
Results: Demonstrations of SelectiveCS-FEM-T10
Summary

## Slide 7: Methods: Formulation of SelectiveCS-FEM-T10

## Slide 8: Concepts of SelectiveCS-FEM-T10
Using T10 element and subdivide it into T4 sub-elements. Overcomes the drawbacks of intermediate nodes.
Adopting intra-element ES-FEM (a kind of CS-FEM) having no strain smoothing across multiple elements. Becomes an independent element of existing FE codes.
Applying selective reduced integration (SRI). Overcomes volumetric locking.

## Slide 9: Brief Formulation of ES-FEM
Let us consider two 3-node triangular elements in 2D for simplicity.
Calculate at each element as usual.
Distribute each to the connecting edge with an area weight and build .
Calculate deformation gradient , Cauchy stress () and nodal internal force in each edge smoothing domain.
As if putting a Gauss point on each edge center
etc.

## Slide 10: Flowchart of SelectiveCS-FEM-T10
Explanation in 2D (6-node triangular element) for simplicity
ES-FEM
SRI
(1) Radial type element subdivision into sub-elements with a dummy node
(3) Vol. strain smoothing with all sub-elements
(2) Iso-vol. strain smoothing at edges
(4)
Overall mean

## Slide 11: T10 Element Subdivision in 3D
Radial subdivision (30% shrunk mesh)
Strain on all 34 edges are smoothed by ES-FEM.
There are 16 T4 sub-elements in total.
Sub-elements have a little larger skewness.
but skewness is not a big issue for ES-FEM.

## Slide 12: Building Lumped Mass Matrix
Calculate the mass of each sub-element.
Distribute it to composing 4 nodes. (3 nodes in 2D.)
The mass of the dummy node is distributed to the connecting 6 mid-nodes. (3 mid-nodes in 2D.)
Schematics in 2D
Each color denotes the corresponding area for mass.

## Slide 13: Results: Demonstration of SelectiveCS-FEM-T10

## Slide 14: Tensioning of Rubber-Filler Composite
Outline
Soft material: Neo-hookean,
Hard material: Neo-hookean,
Discretized into T10 mesh. (about 11,000 nodes and 7,000 elements)
Compared to ABAQUS C3D10MH, the best T10 element of ABAQUS, with the same mesh.
Static Implicit

## Slide 15: Tensioning of Rubber-Filler Composite
Result of ABAQUS C3D10MH with pressure contour
Static Implicit
Convergence failure at 69% nominal stretch (short lasting)

## Slide 16: Tensioning of Rubber-Filler Composite
Result of Selective CS-FEM-T10 with pressure contour
Static Implicit
Convergence failure at 166% nominal stretch (long lasting)

## Slide 17: Tensioning of Rubber-Filler Composite
Comparison of pressure dist. at 60% nominal stretch
Static Implicit
SelectiveCS-FEM-T10 ABAQUS C3D10MH
SelectiveCS-FEM-T10 has good pressure accuracy.

## Slide 18: Tensioning of Rubber-Filler Composite
Comparison of Mises stress dist. at 60% nominal stretch
Static Implicit
SelectiveCS-FEM-T10 ABAQUS C3D10MH
SelectiveCS-FEM-T10 has an issue of Mises stress oscillation, which should be resolved in the future.

## Slide 19: Tensioning of Rubber-Filler Composite
Comparison of history of at the bottom corner
Static Implicit
SelectiveCS-FEM-T10 has enough accuracy in displacement (and force, also) in addition to large deformation robustness.
ABAQUS C3D10MH died here.
Selective CS-FEM-T10 died here.

## Slide 20: Deformation Modes of Armadillo
Outline
Rubber body. (Young’s modulus: 5MPa, Poisson’s ratio: 0.49)
Discretized in T10 mesh. (about 80,000 nodes and 52,000 elements)
Both soles of the feet are perfectly constrained.
Modal analysis up to 40 eigen modes. (This is not a large deformation analysis.)
Compared to ABAQUS C3D10MH with the same mesh.
Eigen Mode

## Slide 21: Deformation Modes of Armadillo
Eigen modes up to Mode 40 with SelectiveCS-FEM-T10
Eigen Mode
SelectiveCS-FEM-T10 has no spurious low-energy modes like hour-glass modes.
There are no unnatural modes.

## Slide 22: Deformation Modes of Armadillo
Comparison of eigen frequencies
Eigen Mode
SelectiveCS-FEM-T10 has practical accuracy in modal analyses as ABAQUS C3D10MH; therefore, SelectiveCS-FEM-T10 would be stable in dynamic analyses.

## Slide 23: Dynamic Bending of Cantilever
Neo-Hookean, , ,
Initial velocity: for all nodes of cantilever
Discretized into T10 mesh. (about 4,000 nodes and 2,000 elements)
Compared to ABAQUS/Explicit C3D10M (NOT C3D10MH) with the same mesh and .
Dynamic Explicit
Initial Condition: (uniform)

## Slide 24: Dynamic Bending of Cantilever
Comparison of animation of Mises stress
Dynamic Explicit
SelectiveCS-FEM-T10 has similar accuracy in displacement and Mises stress to ABAQUS C3D10M.
SelectiveCS-FEM-T10/Explicit ABAQUS/Explicit C3D10M

## Slide 25: Dynamic Bending of Cantilever
Comparison of animation of pressure
Dynamic Explicit
SelectiveCS-FEM-T10 has similar accuracy in displacement and pressure to ABAQUS C3D10M.
SelectiveCS-FEM-T10/Explicit ABAQUS/Explicit C3D10M

## Slide 26: Dynamic Bending of Cantilever
Comparison of time-history of at the tip node
Dynamic Explicit
SelectiveCS-FEM-T10 has similar accuracy in displacement to ABAQUS C3D10M.

## Slide 27: Swing of Bunny Ears
Outline
Iron ears: Neo-Hookean, .
Rubber body: Neo-Hookean, .
Discretized into T10 mesh. (about 61,000 nodes and 41,000 elements)
Compared to ABAQUS/Explicit C3D10M (NOT C3D10MH) with the same mesh and .
Contact is not considered.
Iron Ears
Rubber Body
Fixed Soles
25 m/s Initial Velocity of Iron Ears
Dynamic Explicit
, which is recommended for C3D10M

## Slide 28: Swing of Bunny Ears
Comparison of Mises stress animation
Dynamic Explicit
SelectiveCS-FEM-T10/Explicit ABAQUS/Explicit C3D10M
SelectiveCS-FEM-T10 has similar accuracy in displacement and Mises stress to ABAQUS C3D10M.

## Slide 29: Swing of Bunny Ears
Comparison of pressure sign at ms (right after the stat)
Dynamic Explicit
SelectiveCS-FEM-T10 seems to calculate the initial pressure wave propagation more correctly than ABAQUS C3D10M.
Red: positive pressure Blue: negative pressure
Clear stripe pattern
Unclear stripe pattern
SelectiveCS-FEM-T10/Explicit ABAQUS/Explicit C3D10M

## Slide 30: Swing of Bunny Ears
Timestep-history of total energy (= kinetic + strain)
Dynamic Explicit
SelectiveCS-FEM-T10 has enough energetic stability in dynamic analysis.
( 0.1 s)

## Slide 31: Summary

## Slide 32: Summary
Summary
A new SelectiveCS-FEM-T10 was proposed, which is:
  More robust to severe large deformation than the conventional T10s.
  Enough accuracy for practical use as compared to ABAQUS’s best T10.
  Slower than conventional T10s only in dynamic explicit analysis.
More severe large deformation dynamic analyses should be performed for evaluation.
Take-home message
If you are interested in large deformation analysis,
please consider implementing SelectiveCS-FEM-T10 to your FE code. It’s supremely useful & easy to code!!
Thank you for your kind attention!

## Slide 33: Appendix

## Slide 34: Characteristics of SelectiveCS-FEM-T10
Benefits
  Accurate (no locking, no checkerboarding, no force oscillation).
  Robust (long-lasting in large deformation).
  No increase in DOF (No static condensation).
  Same CPU costs as the other T10 elements (except explicit analyses).
  Implementable to commercial FE codes (e.g., ABAQUS UEL).
Drawbacks
✗ Mises stress oscillation in some extreme analyses.
✗ Several times larger memory size than other T10 elements.
✗ No longer a T4 formulation.
SelectiveCS-FEM-T10 is competitive with the best ABAQUS T10 element, C3D10MH.

## Slide 35: T10 Element Subdivision in 3D
Natural subdivision (30% shrunk mesh)
Each frame edge is owned by only one sub-element.
Strain on frame edges are NOT smoothed by ES-FEM.
There are 12 sub-elements in total.

## Slide 36: Brief of Cell-based S-FEM (CS-FEM)
Subdivide each element into some sub-element.
Calculate at each sub-element.
Calculate etc. in each sub-element.
The biggest advantage of CS-FEM is its portability to existing FE codes.
As if putting an integration point on each sub-element

## Slide 37: Issues
2nd or higher order elements: ✗ Volumetric locking. Accuracy loss in large strain.
B-bar/F-bar method, Selective reduced integration (SRI): ✗ Not applicable to tetrahedral element directly.
F-bar-Patch method: ✗ Difficulty in building good-quality patches.
u/p mixed (hybrid) method (ABAQUS C3D10MH etc.): ✗ Early convergence failure. Accuracy loss in large strain.
F-bar aided ES-FEM-T4 [Y.Onishi, IJNME, 109 (2017)] :  Accurate & robust ✗ Hard to implement in FEM codes.
SelectiveCS-FEM-T10 [Y.Onishi, IJCM, 17 (2020)] :  Accurate, robust & easy to implement. ✗ Not yet optimal.
Conventional tetrahedral (T4/T10) FE formulations still have issues in accuracy and/or robustness especially in nearly incompressible cases.

## Slide 38: Issues in Barreling Analysis of Rubber Cylinder
Neo-Hookean hyperelastic body with
Same mesh as C3D4H case.
Pressure
Although F-barES-FEM-T4 is accurate and robust,
it cosumes larger memory & CPU costs.
it cannot be implemented in general-purpose FE software due to the adoption of ES-FEM.
Another approach adopting CS-FEM with T10 element would be effective.
F-barES-FEM-T4  No shear/volumetric locking
 No corner locking  No pressure checkerboarding
 No increase in DOF
Y. Onishi, IJMNE, Vol. 109 (2017).