## Slide 1: A large deformation tetrahedral smoothed finite element formulation for nearly incompressible solids based on the strain smoothed element (SSE) technique
Yuki ONISHI (Tokyo Institute of Technology)

## Slide 2: What is S-FEM?
Smoothed finite element method (S-FEM) is a relatively new FE formulation proposed by Prof. G. R. Liu in 2006.
S-FEM is one of the strain smoothing techniques.
There are several types of classical S-FEMs depending on the domains of strain smoothing.
For example, in a 2D triangular mesh:
Standard FEM
Edge-based S-FEM (ES-FEM)
Node-based S-FEM (NS-FEM)

## Slide 3: What are the major benefits of S-FEM?
Super-linear mesh convergence rate. (Almost same rate as 2nd-order elements with T4 mesh.)
Shear locking free with ES-FEM. (Excellent accuracy with T4 mesh.)
Little accuracy loss with skewed meshes. (No problem with complex geometry or severe deformation.)
S-FEM is a powerful method suitable for practical industrial applications.
T4: 4-node Tetrahedra

## Slide 4: How popular is S-FEM?
Number of journal papers whose title contains “smoothed finite element”:
(inquired at Google Scholar)
The attraction of S-FEM is expanding continuously.

## Slide 5: Applications of S-FEM in Our Lab
Large deformation solid mechanics (still in academic)
Static Implicit Dynamic Explicit Viscous Implicit
Electrostatic (already in practice)
Carbody Electro-Deposition

## Slide 6: Motivation
What we want to do:
Solve severe large deformation analyses accurately and robustly.
Treat complex geometries with tetrahedral meshes.
Consider nearly incompressible materials .
Support contact problems.
Handle auto re-meshing.
Rubber
Plastic/Glass
Metal

## Slide 7: Issues in Conventional FE (ABAQUS）
Neo-Hookean hyperelastic body with
ABQUS C3D4H  No volumetric locking.
✗ Pressure checkerboarding.
✗ Shear locking & Corner locking.
ABAQUS C3D10MH
 No shear/volumetric locking.
✗ Short lasting (weak to severe deformation). ✗ Low interpolation accuracy.
Almost the same # of nodes.
Pressure
Pressure
4 node tet (T4)
10 node tet (T10)

## Slide 8: Our Approach using S-FEM
Neo-Hookean hyperelastic body with
F-barES-FEM-T4 (2017)
 No shear/volumetric locking.
 Less pressure checkerboarding.  Less corner locking. Long lasting. ✗ Long CPU time. Incompatible w/ FE.
SelectiveCS-FEM-T10 (2021)
 No shear/volumetric locking.
 Less pressure checkerboarding.  Less corner locking. Long lasting.  Same CPU time. Compatible w/ FE.
4 node tet (T4)
10 node tet (T10)

## Slide 9: Issue in SelectiveCS-FEM-T10
Deviatoric stress oscillation is observed in some cases…
e.g.) Tension of filler-rubber composite:
  A hard iron filler (1/8 sphere)
  Poisson’s ratio of rubber (soft) is 0.49.
 Excellent in robustness. Up to 200% stretch!!
 Excellent in nodal displacement/ force and pressure accuracy.
✗ Poor in deviatoric stress accuracy. Due to the lack of deviatoric strain smoothing?
Can we resolve this issue by using the approach of Strain Smoothed Element (SSE), which adopts multi-smoothing?
SSE is explained later.

## Slide 10: Objective
Development of a new T10 element formulation “SelectiveCSSE-T10” introducing the concept of SSE to reduce the deviatoric stress oscillation.
Table of contents:
Method: brief of ES-FEM, SSE, SelectiveCS-FEM-T10, and SelectiveCSSE-T10
Results: an example of analysis
Summary

## Slide 11: Method

## Slide 12: Brief of ES-FEM-T3
Let us consider two 3-node triangular elements in 2D, for simplicity.
Calculate at each element as usual.
Distribute each to the connecting edge with an area weight and build .
Calculate deformation gradient , Cauchy stress () and nodal internal force in each edge smoothing domain with .
As if putting a Gauss point on each edge center
etc.
Constant stress/strain in a smoothing domain.
No shear locking.

## Slide 13: Brief of SSE-T3
Let us consider four 3-node triangular elements in 2D, for simplicity.
Calculate at each element as usual.
Calculate at each edge in the same way as ES-FEM-T3.
Distribute each to the three Gauss points with an equal weight and build .
Calculate , , etc. with s in the same way as FEM-T6.
Strain smoothing is performed twice before evaluating the stress/strain.
Linear stress/strain in an element.
No shear locking.
Faster rate of mesh convergence.

## Slide 14: Performance of SSE-T3
Comparison of Mises stress dist. in cantilever bending analysis
But,
SSE has volumetric locking.
SSE cannot be implemented as an element of standard FE codes.
T. Jinsong et al., Euro. J. Mech. /A, v95, 2022.
Step-like stress dist. (poor).
Shear locking.
Linear stress dist. (good).
No shear locking.
Linear stress dist. (fine).
No shear locking.

## Slide 15: Brief of SelectiveCS-FEM-T10 (Old)
Explanation in 2D (6-node triangular element), for simplicity
ES-FEM
SRI
(1) Radial type element subdivision into sub-elements with a dummy node
(3) Vol. strain smoothing with all sub-elements
(2) Iso-vol. strain smoothing at edges
(4)
Overall mean
Dummy node
Dev. stress integration at edges

## Slide 16: Brief of SelectiveCSSE-T10 (New)
Explanation in 2D (6-node triangular element), for simplicity
ES-FEM
(1) Radial type element subdivision into sub-elements with a dummy node
(3) Vol. strain smoothing with all sub-elements
(2) Iso-vol. strain smoothing at Gauss points
Overall mean
Dummy node
SRI
Re-smoothing at Gauss points
Dev. stress integration at Gauss points.
(4)

## Slide 17: Brief of SelectiveCSSE-T10 in 3D
Radial subdivision of a T10 element (30% shrunk mesh)
1st strain smoothing on 34 edges (ES-FEM).
There are 16 T4 sub-elements in total.
2nd strain smoothing on 64 Gauss points (SSE).

## Slide 18: Results

## Slide 19: Tension of Filler-Rubber Composite
Outline
Filler: Neo-Hookean hyperelastic ()
Rubber: Neo-Hookean hyperelastic ()
T10 mesh (about 11,000 nodes & 7,000 elements)
Compared to ABAQUS C3D10MH (the best T10 element in ABAQUS) with the same mesh.
Static Implicit

## Slide 20: Tension of Filler-Rubber Composite
Result of ABAQUS C3D10MH (Pressure Dist.)
Convergence failure at ~70% stretch.
Static Implicit

## Slide 21: Tension of Filler-Rubber Composite
Result of Selective CSSE-T10 (Pressure Dist.)
Convergence failure at ~100% stretch. Less robust compared to Selective CS-FEM-T10 (up tp 200% stretch.)
Static Implicit

## Slide 22: Tension of Filler-Rubber Composite
Result of Selective CSSE-T10 (Mises Stress Dist.)
The issue of deviatoric stress oscillation was hardly solved…
Static Implicit

## Slide 23: Tension of Filler-Rubber Composite
Comparison of pressure dist. at 60% stretch.
SelectiveCSSE-T10 has sufficient accuracy in displacement/force and pressure.
ABAQUS C3D10MH SelectiveCS-FEM-T10 SelectiveCSSE-T10
Static Implicit

## Slide 24: Tension of Filler-Rubber Composite
Comparison of Mises stress dist. at 60% stretch
SelectiveCSSE-T10 resolves the oscillation issue only a little bit. Unfortunately, there is no fundamental improvement...
Static Implicit
ABAQUS C3D10MH SelectiveCS-FEM-T10 SelectiveCSSE-T10

## Slide 25: Tension of Filler-Rubber Composite
Mises stress Dist. of SelectiveCSSE-T10 at 60% stretch
Mises stress dist. is severely discontinuous at the element interfaces.
This issue may be unavoidable as long as CS-FEM is adopted... (Strain smoothing across elements would be essential?)
Static Implicit

## Slide 26: Summary

## Slide 27: Summary
A new CS-FEM formulation, SelectiveCSSE-T10, was developed.
SelectiveCSSE-T10 introduces the idea of the strain smoothing element (SSE) to our conventional method (SelectiveCS-FEM-T10) to resolve the issue of deviatoric stress oscillation.
Unfortunately, SelectiveCSSE-T10 cannot resolve the oscillation issue fundamentally...
Another approach should be taken to achieve a volumetric locking-free SSE formulation, which is our future work.
Thank you for your kind attention!

## Slide 28: Appendix

## Slide 29: Tension of Filler-Rubber Composite
Result of Selective CS-FEM-T10 (Pressure Dist.)
Static Implicit
Convergence failure at ~200% stretch.