## Slide 1: Pressure checkerboarding suppression in the next-gen smoothed finite element method: EC-SSE-SRI-T4
Yuki ONISHI (Institute of Science Tokyo)

## Slide 2: Motivation
What we want to do:
Solve severe large deformation analyses with finite elements.
Treat complex geometries with tetrahedral (tet) meshes.
Consider nearly incompressible materials .
Support contact problems.
Handle auto re-meshing.
Current situation:
There is no tet FE formulation that satisfies the 3 points: i) Accuracy, ii) Robustness in large deformation, and iii) Compute time.
Rubber
Hot Plastic/Glass
Ductile Metal

## Slide 3: Issues in Accuracy and Their Solutions
Issues in Accuracy | Solutions
Shear Locking | 2nd-order, ES-FEM, NS-FEM, etc.
Volumetric Locking | SRI, B-bar, F-bar, NS-FEM, etc.
Reaction Force Oscillation | 1st-order, Modified 2nd-order, etc.
Pressure Checkerboarding | None! (No absolute solution)
Typical reaction force oscillation (ABAQUS C3D10)
Related to Nodal Force/Disp.
Related to Stress/Strain
Typical pressure checkerboarding (ABAQUS C3D4)
Pressure checkerboarding is quite difficult to resolve.

## Slide 4: Birth of a Next-gen S-FEM, EC-SSE, in 2022
Comparison of Mises stress dist. in cantilever bending analyses in 2D
T. Jinsong et al., Euro. J. Mech. /A, v95, 2022.
Step-like stress dist. (poor).
Shear locking.
Edge Center-based Strain Smoothing Element
Detailed Later
Linear stress dist. (very good) using the same T3 mesh. Very close to analytical solution.
No shear locking.
EC-SSE is an excellent formulation for compressible solids; but when , EC-SSE has volumetric locking and pressure checkerboarding. Therefore, EC-SSE is NOT directly applicable to nearly incompressible solids.
T3
Poisson’s Ratio:
This breakthrough should be called
“S-FEM 2.0”.

## Slide 5: Development of EC-SSE-SRI-T4 in 2024
3D Rubber Cantilever Bending Analysis
Points | Results
Accuracy | Excellent in Mises stress. No shear/volumetric locking. Pressure checkerboarding still remains.
Robustness in Large Deformation | No problem.
Compute Time | Same as EC-SSE-T4.
When the pressure checkerboarding is present……
We cannot trust on as well as pressure.
Contact instability occurs especially in finite sliding cases.
Hence, EC-SSE-SRI-T4(2024) is not bad, but it is not an ultimate formulation, yet.
T4

## Slide 6: Objective and Strategy
Objective
Strategy Adopting the following two techniques (detailed later):
Double strain smoothing in the volumetric part,
Inconsistent hydrostatic stress integration.
Develop a new low-cost improvement method of EC-SSE-SRI to suppress the pressure checkerboarding in nearly incompressible large deformation analysis.
New EC-SSE-SRI

## Slide 7: Method Introduction to ES-FEM, NS-FEM, EC-SSE, and Old/New EC-SSE-SRI

## Slide 8: Brief of ES-FEM
Let us consider a mesh with only two 3-node triangular cells.
Make at each cell as usual.
At each edge, gather s of the connecting cells and average them with area weights to build .
Calculate strain , stress () and nodal internal force in each edge smoothing domain with .
As if putting a Gauss point on each edge center
Strain distribution is piecewise constant in each smoothing domain.
No shear locking.
Cannot avoid volumetric locking & pressure checkerboarding.
Let me explain in 2D for simplicity
etc.

## Slide 9: Brief of NS-FEM
Let us consider a mesh with only four 3-node triangular cells.
Make at each cell as usual.
At each node, gather s of the connecting cells and average them with area weights to build .
Calculate strain , stress () and nodal internal force in each nodal smoothing domain with .
As if putting a Gauss point on each node center
etc.
No shear/volumetric locking. Less pressure checkerboarding.
Cannot avoid spurious low-energy modes.
Let me explain in 2D for simplicity
Strain distribution is piecewise constant in each smoothing domain.

## Slide 10: Brief of EC-SSE
Make s in the same procedure as ES-FEM.
Consider each is the value at the center point of each edge, and assume is linearly distributed in each cell.
Make three s in each cell as the extrapolation of the three s.
Calculate , and using each in the same manner as the 2nd -order element.
No shear locking with T3/T4 mesh.
Fast mesh convergence rate in strain/stress as an 2nd –order element.
Strain distribution is piecewise-linear in each cell and is continuing at every edge center.
Strain/stress are evaluated at the Gauss points in each cell.
Let me explain in 2D for simplicity
Cannot avoid volumetric locking and pressure checkerboarding

## Slide 11: Brief of Old EC-SSE-SRI (2024)
Apply the selective reduced integration (SRI) to EC-SSE to handle rubber-like solids
(1) Calculate at each Gauss point with EC-SSE
(3) Calculate at each node with NS-FEM
(5) Assemble
(2) Calculate at each Gauss point and its contribution to
(4) Calculate at each node and its contribution to
Selective Reduced Integration (SRI)
Let me explain in 2D for simplicity
No volumetric locking.
Deviatoric Part
Volumetric Part
Pressure checkerboarding remains.
No shear locking.
Excellent accuracy in deviatoric stress.
Similar idea as Selective ES/NS-FEM

## Slide 12: Brief of New EC-SSE-SRI (2025)
Apply the selective reduced integration (SRI) to EC-SSE to handle rubber-like solids
(1) Calculate at each Gauss point with EC-SSE
(3) Calculate at each cell with double strain smoothing
(5) Assemble
(2) Calculate at each Gauss point and its contribution to
(4) Calculate at each cell and its contribution to
Selective Reduced Integration (SRI)
Let me explain in 2D for simplicity
No volumetric locking.
Less pressure checkerboarding.
Deviatoric Part
Volumetric Part
No shear locking.
Excellent accuracy in deviatoric stress.
Double strain smoothing: Strain smoothing at nodes (NS-FEM) followed by strain smoothing at cells (NS-FEM-1)

## Slide 13: Inconsistent Hydrostatic Stress Integration in New EC-SSE-SRI
One-point integration for hydrostatic stress integration at Cell :
By using , the distribution range of the internal force becomes narrower. ( It distributes nodal force only to the 4 nodes of Cell .)
On the other hand, is derived from the influence of many cells around Cell .
In short, this hydrostatic stress integration is “collecting widely & distributing narrowly”, which is effective to suppress pressure checkerboarding.
This inconsistent stress integration leads to energy divergence in dynamic analyses ( is no longer in the form of ); but, it is OK in static cases.
Contribution of to nodal internal force
B-matrix of the standard FEM-T4
Hydrostatic stress derived with double smoothed volumetric strain,
Cell volume of the standard FEM-T4

## Slide 14: Result & Discussion Performance evaluation of New EC-SSE-SRI-T4 and Discussion on CPU Cost

## Slide 15: Bending of Rubber Cantilever
Outline
10 x 1 x 1 m cantilever.
Neo-Hookean hyperelastic material, .
Dead load applied to the tip node.
A large deflection analysis with m at the final state.
Compared the results of Old/New EC-SSE-SRI-T4 and ABAQUS C3D4.
Dead Load
Static Implicit

## Slide 16: Bending of Rubber Cantilever
Mises Stress Distribution at the Finial State
Static Implicit
(Ref.) ABAQUS C3D4: Standard FEM-T4
Both results are excellent and have no much difference.
No issues in nodal displacement & force (details omitted).
New EC-SSE-SRI-T4
Old EC-SSE-SRI-T4

## Slide 17: Bending of Rubber Cantilever
Pressure Distribution at the Finial State
Static Implicit
(Ref.) ABAQUS C3D4: Standard FEM-T4
In the old formulation, checkerboarding remains.
In the new formulation, checkerboarding is almost suppressed!!
New EC-SSE-SRI-T4
Old EC-SSE-SRI-T4

## Slide 18: Pressuring of Rubber Block
Outline
1 x 1 x 1 m block.
Arruda-Boyce hyperelastic material, GPa, .
Applying pressure on ¼ of the top face with lateral confinement.
Evaluated the result of New EC-SSE-SRI-T4.
Load
Static Implicit

## Slide 19: Pressuring of Rubber Block
Mises Stress Animation of New EC-SSE-SRI-T4
Static Implicit
No major issue found:
Smooth distribution of Mises stress.
Sufficient robustness in large deformation

## Slide 20: Pressuring of Rubber Block
Pressure Animation of New EC-SSE-SRI-T4
Static Implicit
Noticeable checkerboarding at the final state.
But, in the middle stage, checkerboarding is limited and sufficiently practical.

## Slide 21: Tensioning of Rubber-Filler Composite
Outline
0.5 x 0.5 x 0.5 m cube (1/8 model)
Rubber: Neo-Hookean hyperelastic material
Iron Filler: Neo-Hookean hyperelastic material
Applying enforced tensioning displacement on the top face with lateral confinement.
Evaluated the result of New EC-SSE-SRI-T4.
Static Implicit

## Slide 22: Tensioning of Rubber-Filler Composite
Mises Stress Animation of New EC-SSE-SRI-T4
Static Implicit
Convergence failure at 188% nominal streatch
No major issue is found:
Smooth distribution of Mises stress.
Sufficient robustness in large deformation.

## Slide 23: Tensioning of Rubber-Filler Composite
Pressure Animation of New EC-SSE-SRI-T4
Static Implicit
Practical result is obtained:
No checkerboarding in the steel part.
Only little checkerboarding in the rubber part.

## Slide 24: Discussion on CPU Time of New EC-SSE-SRI-T4
Since the most of CPU time for implicit analyses is spent solving the stiffness equation (i.e., ), the size of matrix () directly affects the CPU time.
S-FEMs including the EC-SSE-T4 family are purely displacement-based FE formulations; thus, the matrix size () is exactly identical to that of FEM-T4.
The EC-SSE-T4 family has all the same bandwidth of , which is x6.7 wider than that of FEM-T4.
Formulation | Bandwidth of | v.s. FEM-T4 Ratio
FEM-T4 | 14 nodes x 3 DOF | 1
FEM-T10 | 28 nodes x 3 DOF | 2.0
ES-FEM-T4 | 45 nodes x 3 DOF | 3.2
NS-FEM-T4, SelectiveES/NS-FEM | 60 nodes x 3 DOF | 4.3
EC-SSE-T4, Old EC-SSE-SRI-T4, New EC-SSE-SRI-T4 | 94 nodes x 3 DOF | 6.7
Formulation |  | v.s. FEM-T4 Ratio
FEM-T4 | 14 nodes x 3 DOF | 1
FEM-T10 | 28 nodes x 3 DOF | 2.0
ES-FEM-T4 | 45 nodes x 3 DOF | 3.2
NS-FEM-T4, SelectiveES/NS-FEM | 60 nodes x 3 DOF | 4.3
EC-SSE-T4, Old EC-SSE-SRI-T4, New EC-SSE-SRI-T4 | 94 nodes x 3 DOF | 6.7
No increase in CPU time compared to EC-SSE-T4 or Old EC-SSE-SRI-T4.

## Slide 25: Summary

## Slide 26: Summary
New EC-SSE-SRI-T4 introduces double smoothing and inconsistent stress integration in the volumetric/hydrostatic part.
Its specs in nearly incompressible large deformation analyses are:
New EC-SSE-SRI-T4 is a method very close to our goal.
Points | Results
Accuracy | Excellent in Mises stress. No shear/volumetric locking. Sufficiently small pressure checkerboarding.
Robustness in Large Deformation | No problem.
Compute Time | Same as EC-SSE-T4.
Thank you for your kind attention!

## Slide 27: Appendix

## Slide 28: Brief of Old EC-SSE-SRI-T4 (in 3D)
[Deviatoric Part]
Make s in the same procedure as ES-FEM.
Make s by re-smoothing three s per face.
Consider each is the value at the center of each face, and assume is linearly distributed in each cell.
Make four s in each cell as the extrapolation of the four s.
Calculate , and using each , like the 2nd -order element.
[Volumetric Part]
Make s in the same procedure as NS-FEM.
Calculate , and using each .
[SRI]
Make .
Let me explain with text only
T4