## Slide 1: A Low-cost and Pressure-checker-free Smoothed Finite Element Formulation using 4-node Tetrahedral Meshes for Nearly Incompressible Large Deformation Analyses
Yuki ONISHI (Institute of Science Tokyo, Japan)

## Slide 2: Motivation
What we want to do:
Solve severe large deformation analyses with finite elements.
Treat complex geometries with tetrahedral (TET) meshes.
Consider nearly incompressible materials .
Support contact problems.
Handle auto re-meshing.
Current situation:
There is no triple-threat TET element that satisfies
Good accuracy,
Fast compute time, and
Enough robustness in large deformation.
Rubber
Hot Plastic/Glass
Ductile Metal

## Slide 3: Issues of TET Elems in Accuracy and Their Solutions
Issues in Accuracy | Solutions
Shear Locking | 2nd-order, ES-FEM, NS-FEM, etc.
Volumetric Locking | , SRI, B-bar, F-bar, NS-FEM, etc.
Reaction Force Oscillation | 1st-order, Modified 2nd-order, etc.
Pressure Checkerboarding | None! (No absolute solution)
Issues in Accuracy | Solutions
Shear Locking | 2nd-order, ES-FEM, NS-FEM, etc.
Volumetric Locking | 
Reaction Force Oscillation | 1st-order, Modified 2nd-order, etc.
Pressure Checkerboarding | None! (No absolute solution)
Typical reaction force oscillation (ABAQUS C3D10)
Related to Nodal Force/Disp.
Related to Stress/Strain
Typical pressure checkerboarding (ABAQUS C3D4)
Pressure checkerboarding is quite difficult to resolve.
S-FEMs will be detailed later.

## Slide 4: Objective
Develop a new smoothed finite element method
with 4-node tetrahedral meshes (ES-FEM-SRI-T4) to suppress pressure checkerboarding in nearly incompressible large deformation analysis.
Table of Contents
Quick Introduction to S-FEM
Method: Brief of ES-FEM-SRI-T4
Result & Discussion 1: Performance of ES-FEM-SRI-T4
Result & Discussion 2: Performance of Conventional S-FEM with Post-Smoothing in Pressure
Summary

## Slide 5: Quick Introduction to S-FEM

## Slide 6: What is S-FEM?
Smoothed finite element method is an FE formulation proposed by Prof. G.R. Liu in 2006.
After 20 years of active research, practical applications are now underway in various fields.
S-FEM is one of the gradient (strain) smoothing techniques.
There are many kinds of S-FEMs depending on the scheme of smoothing.
There are a few classical S-FEMs depending on the smoothing domain.
For example, in a 2D triangular mesh:
Standard FEM
Edge-based S-FEM (ES-FEM)
Node-based S-FEM (NS-FEM)
Each colored area shows the domain for gradient smoothing.

## Slide 7: Brief of ES-FEM
Let us consider a mesh with only two 3-node triangular (T3) cells.
Calculate at each cell as usual.
Distribute each to the connecting edge with an area weight and build .
Calculate strain , Cauchy stress () and nodal internal force in each edge smoothing domain with .
As if putting a Gauss point on each edge center
etc.
Let me explain in 2D for simplicity

## Slide 8: Performance of ES-FEM
Cantilever Bending Analysis with Dead Load at the Tip Plane-Strain, Size:10x1 m,
Mises stress
Pressure
ABAQUS CPE3 (Standard FEM-T3)
ES-FEM-T3
ES-FEM-T3 gives more accurate stress/strain distributions than the standard FEM-T3 using the same mesh.

## Slide 9: Performance of ES-FEM
Cantilever Bending Analysis with Dead Load at the Tip Plane-Strain, Size:10x1 m,
Mesh Seed Size (m) | The Number of Cells
1 | 22
1/2 | 84
1/4 | 342
1/8 | 1,442
1/16 | 5,766
1/32 | 23,034
1/64 | 92,146
Converged
Converged
ES-FEM-T3 is shear locking free and thus the mesh convergence rate of displacement/force is much faster than the Standard FEM-T3.

## Slide 10: What are the benefits of S-FEM?
Super-linear mesh convergence rate with T4 mesh. (Almost same rate as 2nd-order T10 elements.)
Shear locking free with ES-FEM-T4. (Good accuracy with T4 mesh in solid mechanics.)
Volumetric locking free with NS-FEM-T4. (Key technique for rubber-like nearly incompressible solid.)
Little accuracy loss with skewed meshes. (No problem with complex geometry or severe deformation.)
No increase in DOF. (Purely displacement-based formulation. )
Easy to code. (keeping away from mixed variational formulations.)
T4: 4-node Tetrahedra
T4
Search
S-FEM wiki
G.R. Liu et al., CRC Press
S-FEM is a powerful method suitable for practical industrial applications.

## Slide 11: Two Major Issues in ES-FEM
In nearly incompressible solid, ES-FEM-T3 causes
Volumetric locking
Pressure checkerboarding
Same Cantilever Bending Analysis with Pressure
A brand-new code with a novel S-FEM formulation for nearly incompressible solids is still awaited.
ABAQUS CPE3 (Standard FEM-T3)
ES-FEM-T3

## Slide 12: Method Brief of ES-FEM-SRI-T4

## Slide 13: Brief of ES-FEM
Let us consider a mesh with only two 3-node triangular (T3) cells.
Make at each cell as usual.
At each edge, gather s of the connecting cells and average them with area weights to build .
Calculate strain , stress () and nodal internal force in each edge smoothing domain with .
As if putting a Gauss point on each edge center
Strain distribution is piecewise constant in each smoothing domain.
No shear locking.
Cannot avoid volumetric locking & pressure checkerboarding.
Let me explain in 2D for simplicity
etc.

## Slide 14: Brief of NS-FEM
Let us consider a mesh with only four 3-node triangular (T3) cells.
Make at each cell as usual.
At each node, gather s of the connecting cells and average them with area weights to build .
Calculate strain , stress () and nodal internal force in each nodal smoothing domain with .
As if putting a Gauss point on each node center
etc.
No shear/volumetric locking. Minor pressure checkerboarding.
Cannot avoid spurious low-energy modes.
Let me explain in 2D for simplicity
Strain distribution is piecewise constant in each smoothing domain.

## Slide 15: Brief of SelectiveES/NS-FEM (Conventional Method)
(1) Calculate at each edge with ES-FEM
(3) Calculate at each node with NS-FEM
(5) Assemble
(2) Calculate at each edge and its contribution to
(4) Calculate at each node and its contribution to
Selective Reduced Integration (SRI)
Let me explain in 2D for simplicity
No volumetric locking.
Deviatoric Part
Volumetric Part
Apply the selective reduced integration (SRI) to ES-FEM to handle rubber-like solids
Unacceptable pressure checkerboarding.
No shear locking.
Good accuracy in deviatoric stress.

## Slide 16: Brief of ES-FEM-SRI (New Method)
(1) Calculate at each edge with ES-FEM
(3) Calculate at each cell with double strain smoothing
(5) Assemble
(2) Calculate at each edge and its contribution to
(4) Calculate at each cell and its contribution to
Selective Reduced Integration (SRI)
Let me explain in 2D for simplicity
No volumetric locking.
Less pressure checkerboarding.
Deviatoric Part
Volumetric Part
No shear locking.
Good accuracy in deviatoric stress.
Double strain smoothing: Strain smoothing at nodes (NS-FEM) followed by another smoothing at cells (NS-FEM-1)
Apply the selective reduced integration (SRI) to ES-FEM to handle rubber-like solids

## Slide 17: CPU Time of S-FEM-T4s
Since the most of CPU time for implicit analyses is spent solving the stiffness equation (i.e., ), the size of matrix () directly affects the CPU time.
S-FEMs are purely displacement-based FE formulations; thus, the matrix size () is exactly identical to that of FEM-T4.
Both the SelectiveES/NS-FEM-T4 and ES-FEM-SRI-T4 have the same bandwidth of , which is x4.3 wider than that of FEM-T4, meaning about x4 slower than FEM-T4 w/ the same mesh.
Formulation | Bandwidth of | v.s. FEM-T4 Ratio
FEM-T4 | 14 nodes x 3 DOF | 1
FEM-T10 | 28 nodes x 3 DOF | 2.0
ES-FEM-T4 | 45 nodes x 3 DOF | 3.2
NS-FEM-T4, SelectiveES/NS-FEM-T4, ES-FEM-SRI-T4 | 60 nodes x 3 DOF | 4.3
Formulation |  | v.s. FEM-T4 Ratio
FEM-T4 | 14 nodes x 3 DOF | 1
FEM-T10 | 28 nodes x 3 DOF | 2.0
ES-FEM-T4 | 45 nodes x 3 DOF | 3.2
NS-FEM-T4, SelectiveES/NS-FEM-T4, ES-FEM-SRI-T4 | 60 nodes x 3 DOF | 4.3
ES-FEM-SRI-T4 costs the same as SelectiveES/NS-FEM-T4 and is relatively low-cost.
Remind that S-FEM-T4s have much faster mesh convergence rate than FEM-T4.
Therefore, S-FEM-T4s are faster than FEM-T4 to obtain a solution with a certain level of accuracy.

## Slide 18: Result & Discussion 1 Performance of ES-FEM-SRI-T4

## Slide 19: Bending of Rubber Cantilever
Outline
10 x 1 x 1 m cantilever.
Neo-Hookean hyperelastic material, .
Dead load applied to the tip node.
A large deflection analysis with m at the final state.
Compared the results of ABAQUS C3D4, ABAQUS C3D4H, SelectiveES/NS-FEM-T4, and ES-FEM-SRI-T4.
Dead Load
Static Implicit

## Slide 20: Bending of Rubber Cantilever
Mises Stress Distribution at the Finial State
Static Implicit
C3D4 suffers from severe volumetric locking, whereas C3D4H has slight shear locking.
SelectiveES/NS-FEM-T4 and ES-FEM-SRI-T4 are locking-free and present smoother stress distributions.
ES-FEM-SRI-T4
ABAQUS C3D4H (Hybrid)
ABAQUS C3D4 (Standard FEM-T4)
Selective ES/NS-FEM-T4

## Slide 21: Bending of Rubber Cantilever
Pressure Distribution at the Finial State
Static Implicit
Only ES-FEM-SRI-T4 shows an acceptable pressure-checker-free result.
Inaccurate pressure leads to accuracy loss in , direction and magnitude of principal stresses, etc..
ES-FEM-SRI-T4
ABAQUS C3D4H (Hybrid)
ABAQUS C3D4 (Standard FEM-T4)
SelectiveES/NS -FEM-T4

## Slide 22: Bending of Rubber Cantilever
Pressure Distribution at the Finial State of ES-FEM-SRI-T4 with Various Poisson’s Ratios
Static Implicit
ES-FEM-SRI-T4 is pressure-checker-free up to , but not beyond that.

## Slide 23: Pressuring of Rubber Block
Outline
1 x 1 x 1 m block.
Arruda-Boyce hyperelastic material, GPa, .
Applying pressure on ¼ of the top face with lateral confinement.
Evaluated the result of ES-FEM-SRI-T4.
Load
Static Implicit

## Slide 24: Pressuring of Rubber Block
Mises Stress Animation of ES-FEM-SRI-T4
Static Implicit
Smooth distribution of Mises stress.
Sufficient robustness in large deformation
No major issue is found.

## Slide 25: Pressuring of Rubber Block
Pressure Animation of ES-FEM-SRI-T4
Static Implicit
No major checkerboarding.
Practical result is obtained.

## Slide 26: Tensioning of Rubber-Filler Composite
Outline
0.5 x 0.5 x 0.5 m cube (1/8 model)
Rubber: Neo-Hookean hyperelastic material
Iron Filler: Neo-Hookean hyperelastic material
Applying enforced tensioning displacement on the top face with lateral confinement.
Evaluated the result of ES-FEM-SRI-T4.
Static Implicit

## Slide 27: Tensioning of Rubber-Filler Composite
Mises Stress Animation of ES-FEM-SRI-T4
Static Implicit
Smooth distribution of Mises stress.
Sufficient robustness in large deformation
No major issue is found.

## Slide 28: Tensioning of Rubber-Filler Composite
Pressure Animation of ES-FEM-SRI-T4
Static Implicit
No checkerboarding in the steel part.
No major checkerboarding in the rubber part.
Practical result is obtained.

## Slide 29: Result & Discussion 2 Performance of SelectiveES/NS-FEM-T4 with Post-Smoothing in Pressure

## Slide 30: Quick Introduction to Post-Smoothing in Pressure
The conventional S-FEM (SelectiveES/NS-FEM-T4) has the pressure checkerboarding issue in nearly incompressible analyses.
But, in most practical analyses, we can accept results smoothed in post-processing.
SelectiveES/NS-FEM-T4
Post-Smoothing in Pressure
?
Can we accept it, or not?

## Slide 31: Bending of Rubber Cantilever
Step-by-Step Smoothed Pressure Distributions of SelectiveES/NS-FEM-T4 with
Static Implicit
SelectiveES/NS-FEM-T4 with post-smoothing in pressure works so well to obtain a smooth pressure distribution.
Node-to-Cell Post-Smoothing
Cell-to-Node Post-Smoothing
Node-to-Edge Post-Smoothing
Original Result

## Slide 32: Bending of Rubber Cantilever
Comparison to the Reference Solution (ABAQUS C3D8) with
Static Implicit
SelectiveES/NS-FEM-T4 with post-smoothing in pressure gives acceptable solutions for all stress components.
ABAQUS C3D8
ABAQUS C3D8
Selective ES/NS-FEM-T4
Selective ES/NS-FEM-T4
Pressre
Mises Stress

## Slide 33: Bending of Rubber Cantilever
Post-Smoothed Pressure Distribution of SelectiveES/NS-FEM-T4 with Various s
Static Implicit
SelectiveES/NS-FEM-T4 with post-smoothing in pressure works so well even for the almost incompressible cases.
Original Result
3-Step Post-Smoothing
Original Result
3-Step Post-Smoothing

## Slide 34: Overview of the Differences Between the Two Methods
ES-FEM-SRI-T4: Pre-smoothing of volumetric strain () before stress calculation.
  Pressure-dependent constitutive models (e.g., Gurson, Drucker-Prager, Cam-Clay, etc.) can be treated appropriately.
Selective-ES/NS-FEM-T4 with Post-Smoothing in Pressure: Post-smoothing of pressure (, ) after stress calculation.
  Pressure-dependent constitutive models cannot be treated appropriately.
However, since handling pressure-dependent materials is relatively rare in practice, the post-smoothing method is sufficient in most cases.

## Slide 35: Pressuring of Rubber Block
Pressure Animation of Selective ES/NS-FEM-T4 with Post-Smoothing
Static Implicit
No checkerboarding although .
An excellent result is obtained.

## Slide 36: Pressuring of Rubber Block
Comparison of Pressure Distributions at 1.8 GPa Loading State
Static Implicit
Selective ES/NS-FEM-T4 with Post-Smoothing
ABAQUS C3D8
SelectiveES/NS-FEM-T4 with post-smoothing in pressure works so well in nearly incompressible severe large deformation analyses.

## Slide 37: Tensioning of Rubber-Filler Composite
Pressure Animation of Selective ES/NS-FEM-T4 with Post-Smoothing
Static Implicit
No checkerboarding in both the rubber part () and the steel part ().
An excellent result is obtained.

## Slide 38: Summary

## Slide 39: Summary
A new smoothed finite element method (ES-FEM-SRI-T4) was proposed.
Despite using 4-node tetrahedral (T4) meshes, ES-FEM-SRI-T4 is not only locking-free but also pressure-checker-free for solids with Poisson’s ratio up to 0.49.
The pressure-checker-free property is especially important in the implicit analyses with pressure-dependent constitutive models (e.g., Gurson, Drucker-Prager, Cam-Clay, etc.), in which cosmetic post-smoothing in pressure does not work.
For the analyses only with pressure-independent constitutive models, the conventional SelectiveES/NS-FEM-T4 with post-smoothing in pressure works well.
Take Home Message:
By using SelectiveES/NS-FEM-T4 with post-smoothing or ES-FEM-SRI-T4 appropriately, most practical problems, including nearly incompressible large deformation analyses with complex geometries, are accurately solved.

## Slide 40: Applications of S-FEM-T4s in Our Lab
Large deformation solid mechanics (still in academic research)
Dynamic Explicit Static Implicit Viscous Implicit
Electrostatic (already in commercial use)
Carbody Electro Deposition
Thank you for your kind attention!

## Slide 41: Appendix

## Slide 42: Proper Usage of S-FEM-T4s
Post-smoothing is a technique for cosmetic improvement and is not welcomed; however, it is an extremely useful technique for materials without pressure dependency in engineering applications.
Material Properties | Recommended Method
A) Compressible | ES-FEM-T4 or SelectiveES/NS-FEM-T4
B) Incompressible & Pressure-independent | SelectiveES/NS-FEM-T4 with Post-Smoothing
C) Incompressible & Pressure-dependent | ES-FEM-SRI-T4 with Poisson’s Ratio up to 0.49 or SelectiveES/NS-FEM-T4 with Post-Smoothing and Explicit parameterization for Pressure