## Slide 1: A Stable Rezoning Method for Large Deformation Finite Element Analysis using Incremental Equilibrium Equation
Yuki ONISHI, Kenji AMAYA
Tokyo Institute of Technology (Japan)
This talk indirectly relates to Particle/Meshfree methods.
I beg your patience till the end.
yonishi@a.mei.titech.ac.jp

## Slide 2: Motivation and Background
Motivation
  We want to solve severely large deformation problems accurately and stably! (Final target: thermal nanoimprinting)
Background
  Finite elements are distorted in a short time, thereby resulting in convergence failure.
FE rezoning method (h-adaptive mesh-to-mesh solution mapping) is indispensable.

## Slide 3: Methods for Forming Simulation
 | Software | Accuracy | Stability
One Step Method | HyperForm FASTFORM | * | *****
Dynamic-Explicit FE Rezoning | LS-DYNA PAM-STAMP | ** | ***
Static-Explicit FE Rezoning | ASU/P-form | *** | **
Static-Implicit FE Rezoning | ABAQUS MARC | ***** | *
Most of the
rezoning researches
try to improve this.
Our approach
tries to improve
this with
a new idea.

## Slide 4: Objective
Develop an accurate and stable implicit FE rezoning method
for large deformation problems with a new idea.
Table of Body Contents
Derivation of the IEE for static-implicit analysis
Formulation of our implicit FE rezoning method based on the IEE
Verification analysis in 2D
Demonstration analysis in 3D
New Idea: adopting implicit FE formulation based on
the incremental equilibrium equation (IEE)

## Slide 5
Derivation of the incremental equilibrium equation (IEE)
for static-implicit analysis

## Slide 6: Virtual Work Equation in Rate Form
Work Conjugate
The static-explicit FE formulation uses
the same Eq.

## Slide 7: Linearization and Discretization
Fully Implicit Time Advancing
Linearization
in Time
Galerkin
Discretization
:Trial Variable,
E : Set of Elements,
S : Set of Element Faces
Work Conjugate

## Slide 8: Incremental Equilibrium Equation (IEE)
Let the left-hand side be , the right-hand side be .
Avoid error accumulation through timesteps.
The implicit IEE:
The implicit IEE (secondary form):
We use the secondary form in the actual implementation.
:Trial Variable,
E : Set of Elements,
S : Set of Element Faces

## Slide 9: Comparison of IEE to Standard EE
[Standard
Static-Implicit EE]
[Implicit
IEE]
Cauchy Stress
1st P-K Stress
increment

## Slide 10
Formulation of
our implicit FE rezoning method based on the IEE

## Slide 11: Conventional Implicit FE Rezoning
Time: tn-1
Time:
tn
Time:
tn+1
Solve
Standard EE
Remesh
&
Map States
Resolve
Standard EE
Solve
Standard EE
Force
Induce
Large Deformation
and
Convergence Failure

## Slide 12: Proposed Implicit FE Rezoning
Time: tn-1
Time:
tn
Time:
tn+1
Solve
IEE
Remesh
&
Map
and States
Assign
to
Solve
IEE
Force
Never Induce
Any Deformation
nor
Convergence Failure
Unique Operations

## Slide 13: Flowchart of the Proposed Method
Start of timestep loop
  Assume initial
  Start of (implicit) Newton-Raphson loop
    Calculate trial states
    Calculate
    Convergence check
    Solve
    Substitute for
  Substitute for
  Substitute for
  Update States
  Rezone if necessary
Almost the same as the
conventional implicit method
except the green parts

## Slide 14: Proposed vs. Conventional
 | Proposed Implicit FE Rezoning | Conventional Implicit FE Rezoning
Equation to be Solved | IEE | Standard EE
Mapping of | Required... | Unnecessary!
Equilibrium after Mapping | YES! | NO...
Unique Deformed Shape at a Time | YES! | NO...
Convergence Failure in Rezoning Process | NO! | YES...
 | Proposed Implicit FE Rezoning | Conventional Implicit FE Rezoning
Equation to be Solved | IEE | Standard EE
 | Required... | Unnecessary!
Equilibrium after Mapping | YES! | NO...
Unique Deformed Shape at a Time | YES! | NO...
Convergence Failure in Rezoning Process | NO! | YES...

## Slide 15
Verification Analysis
in 2D

## Slide 16: Shearing of 2D Bar
Static, 2D Plane-strain condition
All 1st order triangular elements
Global rezoning every 10 timesteps (much more frequent than necessary)
remeshing with ANSYS GAMBIT

## Slide 17: Shearing of 2D Bar
Material: Hencky's elastic body
  constitutive equation in total strain form:
  Cauchy Stress Hencky Strain
  constitutive equation in rate form:
  Jaumann Rate of Cauchy Stress Stretching
  Young's modulus: 1 GPa; Poisson's Ratio: 0.3

## Slide 18: Shearing of 2D Bar

## Slide 19: Shearing of 2D Bar
Proposed Method
Standard Implicit FEM without Rezoning
1 m Disp.
9 Times Rezoning
2.5 m Disp.
24 Times Rezoning
1 m Disp.
2.5 m Disp.
Shear
Locking

## Slide 20: Tension of 2D Brick
Static, 2D Plane-strain condition
All 1st order triangular elements
Global rezoning every 5 timesteps
Up to 400%
Nominal Strain

## Slide 21: Tension of 2D Brick
Material: Neo-Hookean hyperelastic body
  Strain energy density function:
  Constitutive equation in total strain form:
  Constitutive equation in strain rate form:
where CL(F) is obtained through a long hand calculation.
  C10=0.172 GPa; D1=0.6 GPa-1

## Slide 22: Tension of 2D Brick

## Slide 23: Tension of 2D Brick
0.5 m Disp.
(100% Nominal
Strain)
Proposed Method (19 Times Rezoning)
Standard Implicit FEM without Rezoning

## Slide 24: Tension of 2D Brick
1.0 m Disp.
(200% Nominal
Strain)
Proposed Method (39 Times Rezoning)
Standard Implicit FEM without Rezoning

## Slide 25: Tension of 2D Brick
1.5 m Disp.
(300% Nominal
Strain)
Proposed Method (59 Times Rezoning)
Standard Implicit FEM without Rezoning

## Slide 26: Tension of 2D Brick
2.0 m Disp.
(400% Nominal
Strain)
Proposed Method (79 Times Rezoning)
Standard Implicit FEM without Rezoning

## Slide 27
Demonstration Analysis
in 3D

## Slide 28: Tension of 3D Cube
Static, 3D
1/8 model of a cube
Neo-Hookean hyperelastic body
All 1st order tetrahedral elements
Global rezoning every 10 timesteps
Up to 300% nominal strain

## Slide 29: Twist of 3D Cuboid
Static, 3D
1 x 2 x 4 m size
Henkey's elastic body of
All 1st order tetrahedral elements
Global rezoning every 30 degree
Up to 360 degree rotation

## Slide 30: Punching of 3D Cuboid
Static, 3D
1/4 model
2 x 3 x 4 m size
Henkey's elastic body of
All 1st order tetrahedral elements
Global rezoning every 10 timesteps
radius of punch m
punch up to 1/3 height

## Slide 31: Take-Home Messages
Our method is as stable as the explicit method and as accurate as the implicit method.
The Implicit IEE is useful not only for FE rezoning
but also Meshfree/Particle methods.
See the e-book of PARTICLES2011 or our full-paper in Int. J. Numer. Meth. Engng (2012) in detail.

## Slide 32: Summary and Future Work
Summary
  A new implicit FE rezoning method for severely large deformation analysis is proposed.
  It solves the IEE instead of the standard EE.
  It maps in addition to the other states.
  Its accuracy and stability are verified.
Future Work
  More V&V
  SFEM implementation
  Apply to contact forming, crack propagation, etc.
Thank you for your kind attention!

## Slide 33
Appendix

## Slide 34: Tension of 3D Cube
0% Nominal Strain
(Initial State)
100%
Strain
200%
Strain
300%
Strain

## Slide 35: Twist of 3D Cuboid

## Slide 36: Punching of 3D Cuboid

## Slide 37: Mapping of
Boil down to the following minimization problem:
Unknown
nodal on the new mesh surface
Cost Function
|| {surface traction on the new mesh face}
{surface traction on the old mesh face} ||2
Constraints
  {new nodal } {old nodal }
  {new nodal } {old nodal }
Solve it with Lagrange multiplier method

## Slide 38: Derivation of Stiffness Matrix (1/2)
Relation between and :
Relation between and Jaumann rate:
Erasing :
Constitutive equation (e.g. Hencky's):
Erasing :

## Slide 39: Derivation of Stiffness Matrix (2/2)
Rewrite in matrix form:
where
Stiffness Matrix

## Slide 40: Characteristics of Meshfree Method
Advantage
  Locking free
  Easy to add/remove nodes
Disadvantage
  High cost to construct a stable shape function
  High cost to correct [B] to satisfy the divergence-free condition
  High cost to treat multiple materials, concave boundaries, contact, etc.

## Slide 41: Characteristics of Static-Explicit Method
Advantage
  No convergence calculation
  Solution can stably be obtained (even if there exist no static solution)
Disadvantage
  Equilibrium is not guaranteed due to error accumulation
  Necessitates small with r-min method in plasticity

## Slide 42: Comparison of IEE to Stiffness Eq.
[Standard
Static-Explicit EE]
[Implicit
IEE]
NOT equilibrium equation
BUT stiffness equation
without trial values