## Slide 1: F-barES-FEM-T4: a new finite element formulation of nearly incompressible solids with tetrahedral elements
Yuki ONISHI, Ryoya IIDA Tokyo Institute of Technology, Japan
In this presentation, there are no structural elements and no collapse...
But there are a few dynamic analyses of continuum elements. I hope they interest you.

## Slide 2: Motivation & Background
Motivation
  We want to analyze severe large deformation of nearly incompressible solids accurately and stably! (Target: automobile tire, thermal nanoimprint, etc.)
Background
  Finite elements are distorted in a short time, thereby resulting in convergence failure.
Mesh rezoning (aka., remeshing) is indispensable.
Mold
Polymer
1m

## Slide 3: Our First Result in Advance
What we want to do:
Large deformation
Mesh rezoning
Various kinds of analyses:
  Static implicit
  Dynamic explicit
  Eigen Mode

## Slide 4: Issues
The biggest issue in large deformation mesh rezoning
It is impossible to remesh arbitrary deformed 3D shapes with hexahedral 8-node (H8) elements.
However, the standard (constant strain) T4 elements easily induce shear and volumetric locking, which leads to inaccurate results.
We have to use tetrahedral 4-node (T4) elements...

✗

## Slide 5: Conventional Methods
Higher order elements: ✗ Not volumetric locking free; Unstable in contact analysis; No good in large deformation due to intermediate nodes.
EAS method: ✗ Unstable due to spurious zero-energy modes.
B-bar, F-bar and selective integration method: ✗ Not applicable to T4 mesh directly.
F-bar patch method: ✗ Difficult to construct good patches. Not shear locking free.
u/p hybrid elements based on the mixed variational principle: ✗ No sufficient formulation for T4 mesh so far. (There are almost acceptable hybrid elements such as C3D4H of ABAQUS.)
Smoothed finite element method (S-FEM): ? Unknown potential (since 2007~). It’s worth trying!!

## Slide 6: Various Types of S-FEMs
Basic type
  Node-based S-FEM (NS-FEM)
  Face-based S-FEM (FS-FEM)
  Edge-based S-FEM (ES-FEM)
Selective type
  Selective FS/NS-FEM
  Selective ES/NS-FEM
Bubble-enhanced or Hat-enhanced type
  bFS-FEM, hFS-FEM
  bES-FEM, hES-FEM
F-bar type
  F-barES-FEM
NEW
✗ Volumetric Locking
✗ Spurious zero-energy
✗ Restriction of constitutive model, Pressure oscillation, Corner locking (detailed later)
? Unknown potential
✗ Pressure oscillation, Short-lasting

## Slide 7: Objective
Develop a new S-FEM, F-barES-FEM-T4, by combining F-bar method and ES-FEM-T4 for large deformation problems of rubber-like materials
Table of Body Contents
Methods: Formulation of F-barES-FEM-T4
Results: Some verification analyses
Summary

## Slide 8
Methods
Formulations of F-barES-FEM-T4 (F-barES-FEM-T3 in 2D is explained for simplicity.)

## Slide 9: Quick Review of F-bar Method
Algorithm
Calculate deformation gradient at the element center, and then make the relative volume change .
Calculate deformation gradient at each gauss point as usual, and then make ) .
Modify at each gauss point to obtain as
.
Use to calculate the stress, nodal force and so on.
F-bar method is used to avoid volumetric locking in Q4 or H8 elements. Yet, it cannot avoid shear locking.
For quadrilateral (Q4) or hexahedral (H8) elements
A kind of low-pass filter for

## Slide 10: Quick Review of ES-FEM
Algorithm:
Calculate the deformation gradient at each element as usual.
Distribute the deformation gradient to the connecting edges with area weights to make at each edge.
Use to calculate the stress, nodal force and so on.
ES-FEM is used to avoid shear locking in T3 or T4 elements. Yet, it cannot avoid volumetric locking.
For triangular (T3) or tetrahedral (T4) elements.

## Slide 11: Outline of F-barES-FEM
Concept
is given by ES-FEM.
is given by Cyclic Smoothing (detailed later).
is calculated in the manner of F-bar method:
.
Combination of F-bar method and ES-FEM

## Slide 12: Outline of F-barES-FEM
Brief Formulation
Calculateas usual.
Smooth at nodes and get.
Smooth at elements and get.
Repeat 2. and 3. as necessary ( times).
Smooth at edges to make .
Combine and of ES-FEM as
.
Cyclic Smoothing of
Hereafter, F-barES-FEM-T4 with cycles of smoothing is called “F-barES-FEM-T4()”.
( layers of ~)
A kind of low-pass filter for

## Slide 13: Equations to Satisfy
Implicit static
  Balance equation: .
  In Newton-Raphson loop, there is a need for solving the matrix equation:
  .
Dynamic explicit
  Motion equation: .
  Using the lumped mass matrix for , there is no need for solving any matrix equations.
  Velocity Verlet method is applied for time integration.

## Slide 14
Results
Some verification analyses (Analyses for hyperelastic materials without mesh rezoning are presented for pure verification.)

## Slide 15: Bending of a Cantilever
Outline
Neo-Hookean hyperelastic material
Initial Poisson’s ratio: 0.49 or 0.499.
Two types of T4 meshes: a structured mesh and an unstructured mesh.
Compared to ABAQUS C3D4H (1st-order hybrid tetrahedral element).
Dead Load
Static Implicit

## Slide 16: Bending of a Cantilever
Pressure Distributions
ABAQUS C3D4H
F-bar ES-FEM- T4(1)
Structured Mesh
Static Implicit

## Slide 17: Bending of a Cantilever
Pressure Distributions
F-bar ES-FEM-
T4(2)
F-bar ES-FEM- T4(3)
Increase in the number of cyclic smoothing () makes stronger suppression of pressure oscillation.
Structured Mesh
Static Implicit

## Slide 18: Bending of a Cantilever
Pressure Distributions
ABAQUS C3D4H
F-bar ES-FEM- T4(1)
Unstructured Mesh
Static Implicit

## Slide 19: Bending of a Cantilever
Pressure Distributions
F-bar ES-FEM-
T4(3)
F-bar ES-FEM-
T4(2)
No mesh dependency is observed.
Unstructured Mesh
Static Implicit

## Slide 20: Compression of a Block
Outline
Arruda-Boyce hyperelastic material ().
Applying pressure on ¼ of the top face.
Compared to ABAQUS C3D4H with the same unstructured T4 mesh.
Load
Static Implicit

## Slide 21: Compression of a Block
Pressure Distribution
ABAQUS C3D4H
F-bar ES-FEM-
T4(2)
Early stage Middle stage Later stage
Static Implicit

## Slide 22: Compression of a Block
Pressure Distribution
Early stage Middle stage Later stage
F-bar ES-FEM- T4(3)
F-bar ES-FEM- T4(4)
In case the Poisson’s ratio is 0.499, F-barES-FEM-T4(2) or later resolves the pressure oscillation issue.
Static Implicit

## Slide 23: Barreling of 1/8 Cylinder
Outline
Neo-Hookean hyperelastic material ().
Enforced displacement is applied to the top surface.
Compared to ABAQUS C3D4H with the same unstructured T4 mesh.
Static Implicit

## Slide 24: Barreling of 1/8 Cylinder
Result of F-bar ES-FEM(2) (Pressure)
50% nominal compression
Almost smooth
pressure
distribution is obtained
except just around the rim.
Static Implicit

## Slide 25: Barreling of 1/8 Cylinder
Result of F-bar ES-FEM(2) (Mises Stress)
Smooth
Mises stress
distribution is obtained
except just around the rim.
50% nominal compression
Static Implicit

## Slide 26: Barreling of 1/8 Cylinder
Pressure Distribution
ABAQUS C3D4H
F-bar ES-FEM-
T4(3)
F-bar ES-FEM-
T4(4)
F-bar ES-FEM- T4(2)
F-barES-FEM-T4 with a sufficient cyclic smoothing can resolve the corner locking issue.
Static Implicit
Strange deformation (corner locking) around the rim

## Slide 27: Bending of a Cantilever
Outline
Neo-Hookean hyperelastic material: .
Uniform initial velocity: .
Compared to ABAQUS/Explicit C3D4 (NOT C3D4H) & C3D8 (hexahedral selective reduced integration).
Dynamic Explicit

## Slide 28: Bending of a Cantilever
Pressure sign distributions
Dynamic Explicit
ABAQUS/Explicit C3D4 (✗Locking & Pressure oscillation)
ABAQUS/Explicit C3D8
F-barES-FEM-T4(2)
F-barES-FEM has no locking & less pressure oscillation in dynamic explicit analysis.

## Slide 29: Bending of a Cantilever
Pressure at
Dynamic Explicit
F-barES-FEM-T4 has good accuracy in pressure.
ABAQUS/Explicit C3D8
F-barES-FEM-T4(2)
ABAQUS/Explicit C3D4

## Slide 30: Bending of a Cantilever
Deflection
Dynamic Explicit
Displacement accuracy of F-barES-FEM is independent of the number of cyclic smoothing.

## Slide 31: Swinging of Bunny Ears
Outline
Iron ears: , Neo-Hookean, No cyclic smoothing.
Rubber body: , Neo-Hookean, 1 cycle of smoothing.
Compared to ABAQUS/Explicit C3D4.
Dynamic Explicit
Iron Ears
Rubber Body
Fixed
Initial Velocity of Iron Ears

## Slide 32: Swinging of Bunny Ears
Pressure sign distributions
F-barES-FEM is apparently softer than C3D4.
F-barES-FEM shows patchy pressure patterns due to complex reflections of pressure waves.
C3D4 shows typical checkerboard patterns.
Dynamic Explicit
ABAQUS/
Explicit C3D4
F-barES- FEM-T4

## Slide 33: Swinging of Bunny Ears
Pressure distributions (back shot)
C3D4 shows checkerboard patterns even on the iron ears. (Because of the negative influence from rubber body???)
F-barES-FEM-T4 shows smooth pressure distribution except the connection interfaces (corners).
Dynamic Explicit
F-barES-FEM-T4
ABAQUS/Explicit C3D4

## Slide 34: Natural Modes of ¼ Cylinder
Outline
Iron part: , Elastic, No cyclic smoothing.
Rubber part: , Elastic, 2 cycles of smoothing.
Compared to ABAQUS C3D4, C3D4H, and C3D8.
Eigen Mode
Fixed
In Plane Slide
In Plane Slide
Rubber Part
Iron Part

## Slide 35: Natural Modes of ¼ Cylinder
Eigen frequencies
C3D4 and C3D4H show higher frequencies (stiffer results).
F-barES-FEM-T4 and C3D8 are in good agreement.
1
Eigen Mode

## Slide 36: Natural Modes of ¼ Cylinder
Eigen modes
 | 1st Mode | 11th Mode
ABAQUS C3D8 |  | 
F-barES-FEM-T4 |  | 
F-barES-FEM-T4 has good accuracy in eigen mode analysis.
Eigen Mode

## Slide 37
Summary

## Slide 38: Benefits and Drawbacks of F-barES-FEM-T4
Benefits
  Locking-free with 1st -order tetra meshes. No difficulty in severe strain or contact analysis.
  No increase in DOF. No need of static condensation.
  No restriction of material constitutive model.
  Less pressure oscillation in rubber-like materials.
  Less corner locking.
  Applicable to static/dynamic, implicit/explicit, and modal analyses.

## Slide 39: Benefits and Drawbacks of F-barES-FEM-T4
Drawbacks
✗ Slow speed of calculation.
In implicit analyses, CPU Time is roughly linear with respect to the band width of [K].
Chart: # of Cyclic Smoothings
| 0 | 1 | 2 | 3
列3 | 40 | 390 | 860 | 1580
(x1)
(x9.8)
(x21.5)
(x39.5)

## Slide 40: Benefits and Drawbacks of F-barES-FEM-T4
Drawbacks
✗ Slow speed of calculation.
In explicit analyses, [K] is unnecessary; yet, CPU Time increases gradually with the # of cyclic smoothings.
Chart: In case of 6864 DOF & 10000 timesteps
| 0 | 1 | 2 | 3
列3 | 108 | 292 | 684 | 1402
(x1)
(x2.7)
(x6.3)
(x13.1)

## Slide 41: Conclusion
F-barES-FEM-T4 has excellent accuracy, but needs some effort for speed-up.
Thank you for your kind attention!