## Slide 1: Recent Advancement in Smoothed Finite Element Methods for Locking-free Analysis with Tetrahedral Elements
Yuki ONISHI Tokyo Institute of Technology (Japan)

## Slide 2: Motivation & Background
Motivation
  We want to analyze severely large deformation problems in solids accurately and stably! (Target: automobile tire, thermal nanoimprint, etc.)
Background
  Finite elements are distorted in a short time, thereby resulting in convergence failure.
Mesh rezoning method (h-adaptive mesh-to-mesh solution mapping) is indispensable.
Mold
Polymer

## Slide 3: Our First Result in Advance
What we want to do:
Static
Implicit
Large deformation
Mesh rezoning

## Slide 4: Issues
The biggest issue in large deformation mesh rezoning
It is impossible to remesh arbitrary deformed 2D or 3D domains with quadrilateral or hexahedral elements.
However, the standard (constant strain) triangular or tetrahedral elements induce shear and volumetric locking easily, which leads to inaccurate results.
We have to use triangular or tetrahedral elements...
YES
NO

## Slide 5: Conventional Methods
Higher order elements: ✗ Not volumetric locking free; Not effective in large deformation due to intermediate nodes.
EAS elements: ✗ Unstable.
B-bar, F-bar and selective integration elements: ✗ Not applicable to triangular/tetrahedral mesh.
F-bar patch elements: ✗ Difficult to construct good patches
u/p hybrid (mixed) elements ✗ No sufficient formulation for triangular/tetrahedral mesh is presented so far. (There are almost acceptable hybrid elements such as C3D4H or C3D10H of ABAQUS.)
Smoothed finite elements: ? Unknown potential (since 2009~). Let’s try!

## Slide 6: Objective
Develop a locking-free, accurate and stable smoothed finite element method (S-FEM)
with 4-node tetrahedral elements (T4) for large deformation problems
Table of Body Contents
Quick survey of 3 classical S-FEMs
Introduction to a recent S-FEM: hES-FEM
Introduction to our new S-FEM: F-barES-FEM
Summary

## Slide 7
Quick survey of
3 Classical S-FEMs

## Slide 8: (i) Edge-based S-FEM (ES-FEM)
Calculate at element as usual.
Distribute to the connecting edges and make .
F, T etc and {f int} are calculated on smoothed edge domains.
Generally accurate but induces volumetric locking.
Substituting "face" for "edge"
gives FS-FEM for 3D

## Slide 9: (ii) Node-based S-FEM (NS-FEM)
Calculate at element as usual.
Distribute to the connecting nodes and make
F, T etc and {f int} are calculated on smoothed node domains.
Generally not accurate but volumetric locking free.
(due to zero-energy modes, which are arisen in
reduced integration
finite elements as hour-glass modes)
close to FVM with
vertex-based control volume

## Slide 10: (iii) Selective ES/NS-FEM
Separate stress into "deviatoric part" and "hydrostatic part“ and combine them .
F, T etc and {f int} are calculated on both smoothed domains.
No locking & No zero-energy modes!! thus, the best choice.
Substituting "face"
for
"edge"
gives
FS/NS-FEM
for 3D

## Slide 11: Characters of 3 Classical S-FEMs
All the classical S-FEMs have an unique benefit: no increase in DOF.
  The nodal displacement vectors are only the unknown. (No pressure or volumetric strain unknowns.)
  Static condensation is unnecessary.
All S-FEMs have a drawback: increase in the bandwidth of stiffness matrix [K].
  [Bandwidth of ES-FEM-T4] [Bandwidth of standard FEM-T4])
  [Bandwidth of NS-FEM-T4] = [Bandwidth of selective S-FEM-T4] [Bandwidth of standard FEM-T4])

## Slide 12: Example: Compression of Hyperelastic Block
Outline
Arruda-Boyce hyperelastic material ()
Applying pressure on ¼ of the top face

## Slide 13: Example: Compression of Hyperelastic Block
Result of Selective ES/NS- FEM-T4

## Slide 14: Example: Compression of Hyperelastic Block
Vertical Displacements vs. Applied Pressure
Constant strain element (C3D4) locks quickly.
Other elements including selective S-FEMs do not lock.
Selective S-FEMs are locking-free in large strain analysis!!

## Slide 15: Example: Compression of Hyperelastic Block
Sign of Pressure
Pressure oscillation is present…
Selective FS/NS-FEM-T4
Selective ES/NS-FEM-T4
Checkerboard
patterns are observed.

## Slide 16: Characteristics of Classical S-FEMs
 | Shear Locking | Volumetric Locking | Zero- Energy Mode | Pressure Oscillation
Standard FEM-T4 | ✗ | ✗ |  | ✗
NS-FEM-T4 |  |  | ✗ | ✗
ES-FEM-T4 & FS-FEM-T4 |  | ✗ |  | ✗
Selective S-FEM-T4 |  |  |  | ✗
There still remain
issues to be resolved.

## Slide 17
Introduction to a Recent S-FEM:
hES-FEM

## Slide 18: Hat-enhanced ES-FEM (hES-FEM)
Concept
An additional internal node (hat node or bubble node) is put at each standard triangular element.
Each hat node has its own displacement DOFs.
The shape function of hat nodes is the hat function.
Namely in hES-FEM, 3 sub-elements (, , ) have the same shape functions as the standard triangular elements.
3 sub-elements
In an element
1
0
0
0
Hat Function

## Slide 19: Hat-enhanced ES-FEM (hES-FEM)
Brief formulation
Calculate at sub-element as usual.
Distribute to the connecting edges and make .
F, T etc and {f int} are calculated on smoothed edge domains.
hES-FEM
Segments
between nodes and
hat nodes are not
regarded
as edges.

## Slide 20: Example: Compression of Hyperelastic Block
Result of hES-FEM
Mises stress distribution is smooth. But, it got convergence failure at a relatively earlier stage
due to pop out of hat nodes…

## Slide 21: Example: Compression of Hyperelastic Block
Vertical Displacements vs. Applied Pressure
Locking-free and accurate.
hES-FEM stopped at 82% nominal compression, where as other locking-free methods stopped around 95% of that.
hES-FEM is loking-free but cannot bear with severe strain.
Standard (constant strain) T4

## Slide 22: Example: Compression of Hyperelastic Block
Pressure distribution
Pressure oscillation is almost suppressed.

## Slide 23: Characteristics of hES-FEM
Benefits
  Locking-free.
  Only displacement DOF.
  Suppress pressure oscillation to some extent.
Drawbacks
  ✗ Early convergence failure due to pop out of internal nodes.
  ✗ Significant increase in total DOF. In general unstructured T4 mesh, [the num. of elements] [the num. of nodes]. i.e., total DOF of hES-FEM is 6 times larger…

## Slide 24
Introduction to our new S-FEM:
F-barES-FEM

## Slide 25: F-bar aided ES-FEM (F-barES-FEM)
Concept
Use classical ES-FEM to calculate .
Use “cyclic smoothing” to calculate .
Apply F-bar method to obtain .
Combination of F-bar method and ES-FEM

## Slide 26: F-bar aided ES-FEM (F-barES-FEM)
Brief Formulation
Calculate at elements as usual.
Smooth of elements at nodes.
Smooth of nodes at elements.
Repeat 2. and 3. as necessary.
Smooth of elements at edges.
Combine the cyclically smoothed and of ES-FEM as .
Cyclic
Smoothing
of J
(Currently we employ
2 cycles.)

## Slide 27: Example: Compression of Hyperelastic Block
Pressure distribution
F-barES-FEM(2) suppresses pressure oscillation!!
No checkerboard patterns are observed.

## Slide 28: Example: Compression of 1/8 Cylinder
Outline
Neo-Hookean hyperelastic material ().
Enforced displacement is applied to the top surface.
Stress singularity is present around the rim.

## Slide 29: Example: Compression of 1/8 Cylinder
Result of F-bar ES-FEM(2)
50% nominal compression
Almost smooth
pressure
distribution is obtained
except just around the rim.

## Slide 30: Example: Compression of 1/8 Cylinder
Result of F-bar ES-FEM(2)
Smooth
Mises stress
distribution is obtained
except just around the rim.
50% nominal compression

## Slide 31: Characteristics of F-barES-FEM
Benefits
  Locking-free.
  No increase in DOF.
  Suppress pressure oscillation as increasing the number of cyclic smoothing.
Drawbacks
  ✗ Increase in bandwidth of stiffness matrix [K]. In general unstructured T4 mesh, F-barES-FEM(1): 10 times wider than FEM-T4, F-barES-FEM(2): 20 times wider than FEM-T4. But, exactly consistent [K] is not necessary and thus speed up can be expected.

## Slide 32
Summary

## Slide 33: Characteristics of S-FEMs
 | Shear & Volumetric Locking | Zero- Energy Mode | Dev/Vol Coupled Material | Pressure Oscillation | Severe Strain
Standard FEM-T4 | ✗ |  |  | ✗ | 
Selective S-FEM-T4 |  |  | ✗ | ✗ | 
hES-FEM-T4 |  |  |  |  | ✗
F-bar ES-FEM-T4 |  |  |  |  | 
This is  when the num. of cyclic smoothing is large enough; but, speed-up is necessary.

## Slide 34: Take-Home Messages
Recent S-FEMs are about to realize locking-free, accurate and stable large deformation analysis of nearly incompressible solids with T4 elements.
Recent S-FEMs have no increase in DOF (or no increase in non-displacement DOF); thus, they have potential to be applied to various types of analysis such as eigen mode, harmonic response, explicit dynamic, etc..
Thank you for your kind attention!