## Slide 1: A Novel Meshfree Method for Large Deformation Analysis of Elastic and Viscoelastic Bodies without using Background Cells
Yuki ONISHI and Kenji AMAYA
Tokyo Institute of Technology

## Slide 2: Background
After the advent of nanoimprinting, micro hot embossing and thermal nanoimprinting have been in area of active research.
  Pressing patterned mold onto polymer or glass to transcribe the pattern.
  Better precision than photo lithography
  A mechanical process
  Experiments cost high!
Goal
Establishment of numerical technique for thermal nanoimprint process optimization.
J.W.Lee et al., EIPBN (2007)‏

## Slide 3: Our Previous Work
Finite element Analysis
  Geometric nonlinear (Large deformation)
  Material nonlinear （rigid mold and viscoelastic polymer)
  Contact nonlinear
  Quasi-static analysis
Mold
（rigid）
Polymer
(viscoelastic)
Onishi et al.,
JVST B (2008) etc.‏
FE analyses agreed
with experiments
in case of
line-and-space
up to AR=1

## Slide 4: Our Previous Work

## Slide 5: Objective
Our previous work was incomplete…
In practical applications, AR over 1 is not uncommon. (even AR>3 is usual.)
FEM cannot treat the extremely large deformation without adaptive meshing. (Adaptive meshing is difficult to implement.)
Objective
Development of a meshfree method for viscoelastic large deformation analysis
(utilize it for thermal nanoimprint process optimization in the future)

## Slide 6: Proposing Meshfree Formulation
[4 Points]
1. Quasi-static analysis for viscoelastic body
2. Modified stress-point integration
3. Robust moving least squares (Robust MLS) with integration correction
4. Quasi-implicit time advancing

## Slide 7: 1. Viscoelastic Model
Standard solid model in shear (the simplest generalized Maxwell model)
T:Cauchy stress, Evol：logarithmic volumetric strain，
E’：logarithmic deviatoric strain, Ev’：logarithmic viscous strain
G∞：long-term shear modulus
G0：instantaneous shear modulus
g：dimensionless shear modulus
t：relaxation time
●Constitutive equation
●Schematic diagram
On the other hand, bulk modulus, K, is a constant.

## Slide 8: 1. Viscoelastic Model
material constants used in example analysis
instantaneous Young’s modulus（E0）： 9 GPa
instantaneous Poisson’s ratio（n0）： 0.333・・・
instantaneous shear modulus（G0）： 3.375 GPa
bulk modulus（K）： 9 GPa
dimensionless shear modulus（g）： 0.9
relaxation time（t）： 5 s
long-term Young’s modulus（E∞）： 1 GPa
long-term Poission’s ratio（n∞）： 0.481
long-term shear modulus(G∞): 0.3375 GPa

## Slide 9: 2. Modified SP Integration
Meshfree domain integration with BG cells is not suitable for large deformation.
There are 2 ways of domain integration without BG cells.
[1] Nodal integration (J. S. Chen)
merit) very simple. generation of stress-points is not necessary.
demerit) zero-energy mode arise without artificial stabilization. (similar to hour-glass modes in FEM)
[2] Stress-point (SP) integration (T. Belytschko)
merit) artificial stabilization is not essential.
demerit) generation and translation of stress-points are required.
No practical SP integration scheme for large deformation analysis was developed so far.
We introduce a SP integration
modified for large deformation
analysis.

## Slide 10: 2. Modified SP Integration (initialization)
(currently) SPs are generated from FE meshes [Note] meshes are only for initialization!!!
Locate every SP in the middle edges
(Belytschko’s SP integration has master and slave SPs.)
Corresponding SP volume is calculated with meshes
：node
(has only x and u)
：stress point (SP)
(has x, T, E, E v, etc.)

## Slide 11: 2. Modified SP Integration (updates)
Location
Volume
Vinitial：initial volume，F：deformation gradient
x: current location, S: set of nodes in the support,
f: shape function

## Slide 12: 3. Robust MLS (approximation)
IR
Weight function
Support radius
IR
IR
not bell shape but mountain shape
(small)

## Slide 13: 3. Robust MLS (integration correction)
Integration constraint
Integration correction (IC)
n: outward normal unit vector, A: correspoiding nodal area
JS: set of SPs that include node J in the support
determine g s so that modified y s satisfy reproducing constraints
including integration constraint

## Slide 14: 4. Quasi-implicit Time Advancing
Start of time increment loop
  Start of Newton-Raphson loop
    update support, w, f, etc.
    calc f int. and K
    calc r = f int. -f ext.
    solve K du = r
    update node locations
    update SP locations
  End of Newton-Raphson loop
End of time increment loop
Typical fully-implicit time advancing

## Slide 15: 4. Quasi-implicit Time Advancing
Start of time increment loop
  update support, w, f, etc.
  renew f virtual
  Start of Newton-Raphson loop
    update support, w, f, etc.
    calc f int. and K
    calc r = f int. -f ext. -f virtual
    solve K du = r
    update node locations
    update SP locations
  End of Newton-Raphson loop
End of time increment loop
Enforcement of temporal continuity of the mechanical equilibrium
Constant shape function in each Newton-Raphson loop

## Slide 16: Patch Test
Elastic body, Static, Plane-strain
Irregularly-arranged nodes and SPs
Displacement BC for every external nodes
：node
：stress point (SP)

## Slide 17: Patch Test (animation)

## Slide 18: Patch Test (result)
within 1% error of Mises stress
Proposed method passes the patch test

## Slide 19: Bending of Cantilever
Static/Quasi-static, Plane strain
50x5 structured grid nodes
Concentrated force at right-top node
Compared to FEM(ABAQUS/Standard) with same node arrangements and selective reduced integration quadrangle elements
Elastic/Viscoelastic body
1m
0.1m
200 kN
Force
Time
1s
100s

## Slide 20: Bending of Cantilever (elastic)
Less than 1% error of displacement
No problem in elastic large deflection analysis
E=1GPa, n=0.481
ABAQUS/Standard Proposed Method

## Slide 21: Bending of Cantilever (viscoelastic)
ABAQUS/Standard Proposed Method

## Slide 22: Bending of Cantilever (viscoelastic)
2.5% error of displacement
Error decreases as dt decreases
Further improvement of time-advancing scheme is necessary

## Slide 23: Imprinting-like Analysis
Quasi-static, plane strain
Horizontal bounding for left and right side
Vertical bounding for bottom side
Enforced displacement for right half of top side toward downward with horizontal bounding
Unstructured grid with fineness and coarseness
0.5m disp.
in 100s
1m
1m

## Slide 24: Imprinting-like Analysis (FEM)
Inappropriate deformation because of the locking under the corner

## Slide 25: Imprinting-like Analysis (FEM)

## Slide 26: Imprinting-like Analysis (animation)
An appropriate result was obtained.

## Slide 27: Summary & Future Work
Summary
  A Meshfree formulation of large deformation of viscoelastic body without BG cells was proposed.
  It passes the patch test.
  It has fair accuracy in large deflation analysis.
  Appropriate result is obtained in imprinting-like analysis.
  Further modification is required to apply it to thermal nanoimprint simulation.
Future work
  Improvement of time advancing scheme
  Verification with experiments or FEM with adaptive meshing
  Insertion of additional nodes and SPs during analysis
  Contact analysis