## Slide 1: Meshfree Large Deformation Analysis with Modified Formulation of Floating Stress-point Integration (FSPI)
Yuki ONISHI, Kenji AMAYA,
Tokyo Institute of Technology, JAPAN
Ryuta IMAI
Mizuho Information & Research Institute, Inc., JAPAN

## Slide 2: Table of Contents
Introduction and Objective
Formulation of Floating Stress-Point Integration (FSPI) Meshfree Method
Examples of Analysis
Conclusion

## Slide 3: Table of Contents
Introduction and Objective
Formulation of Floating Stress-Point Integration (FSPI) Meshfree Method
Examples of Analysis
Conclusion

## Slide 4: Backuground and Motivation
We want to solve extremely large deformation problems easily!! Final target: thermal imprinting
Using FEM, finite elements are easily distorted and bring analysis failure.
Adaptive FEM is not convenient so far.
Challenge meshfree!!

## Slide 5: 3 Types of Domain Integration
Background Cell Integration (EFGM)
  Numerical diffusion arises through physical state interpolation.
Nodal Integration (SCNI)
  Doesn't get along with updated Lagrangian.
  Zero-energy mode arises without artificial stabilization.
Stress-Point Integration
  Move of SPs is required with deformation goes on.
We adopted this, and
developed a new one named FSPI.
There are only few researches especially for large deformation. (There is no standard formulation.)

## Slide 6: Objective
In this presentation,
effectiveness of FSPI in cases of
elastic and elastoplastic materials
are presented.
Develop a new type of
stress-point integration meshfree method,
floating stress-point integration (FSPI),
for large deformation problems

## Slide 7: Table of Contents
Introduction and Objective
Formulation of Floating Stress Point Integration (FSPI) Meshfree Method
Examples of Analysis
Conclusion

## Slide 8: Outline of FSPI
Concept of FSPI
  Fully meshfree method for large deformation
  Use stress-points for domain integration
  Use updated Lagrangian procedure
  Use implicit time advancing sheme
Introduced Unique Techniques
  Shape function construction with Robust MLS
  Incremental equilibrium equation for quasi-implicit time advancing scheme
Combination of these two is difficult to be realized
in meshfree.

## Slide 9: Spacial Discretization & Initialization
Generate nodes and stress-points in the initial analysis domain
Any generation methods will do.

## Slide 10: Spacial Discretization & Initialization
Currently, nodes and stress-points are generated with unstructured triangular meshes.
Assign initial corresponding volume of stress-points, , as .

## Slide 11: Spacial Discretization & Initialization
After the generation and the assignment, meshes are never referred any more.
This way of node and stress-point generation is not an optimal one.

## Slide 12: Mathematical Notation Rules
: variable of a stress-point I superscript I to the left of a variable e.g.) : location of stress-point I
: variable of a node J subscript J to the left of a variable e.g.) : location of node J
: trial variable in time increments superscript + to the right of a variable e.g.) : trial internal force vector

## Slide 13: Shape Function
IR
Robust Moving Least Squares (Robust MLS)
Support radius for each stress-point I, IR, is set dynamically and varies over time.
<Algorithm to set IR >
IR
IR
(small)

## Slide 14: Shape Function
Weight function w (at a stress-point I to a node J )
Shape function N and its derivatives N '
(at a stress-point I )
same as the original MLS except IR

## Slide 15: Integration Correction
Integration constraint (Divergence-free cond.)
Necessary and sufficient condition to pass patch tests.
Unfortunately, s don't satisfy this condition.
Making corrected ( ) is necessary.
n : outward normal unit vector
JA : correspoiding nodal area
JI : set of SPs that include node J in the support

## Slide 16: Integration Correction
Scaling type integration correction
Ig : correction coefficient
Currently, we simply took minimum norm solution as {g} to minimize the magnitude of the correction.
Assigning this into the equations of integration constraint,
a matrix equation is obtained.
This is an
Under-determined
system
The num. of SPs > The num. of nodes

## Slide 17: Time Advancing Scheme
Fully-implicit Time Advancing
Start of a time increment
  Start of the Newton-Raphson loop
    Update support, w, N, and N' of SPs
    Calculate strain, stress, etc. of SPs
    Calculate {f int.}, {f ext.}, and [K ]
    If || {f ext.} - {f int.}|| is small, break
    Solve [K ] {du } = {f ext.} - {f int.}
    Update {Du } ={Du } + {du }
    Update disp. of Nodes and SPs
  Update all physical variables
Support, shape function, etc. are changed every time in Newton-Raphson loop.
Unstable
A node can get in-and-out of the support repetitively

## Slide 18: Time Advancing Scheme
Quasi-implicit Time Advancing
Start of a time increment
  Update support, w, N, and N' of SPs
  Start of the Newton-Raphson loop
    Update support, w, N, and N' of SPs
    Calculate strain, stress, etc. of SPs
    Calculate {f int.}, {f ext.}, and [K ]
    If || {f ext.} - {f int.}|| is small, break
    Solve [K ] {du } = {f ext.} - {f int.}
    Update {Du } ={Du } + {du }
    Update disp. of Nodes and SPs
  Update all physical variables
B matrix changed suddenly.
Unstable
also changed suddenly.

## Slide 19: Time Advancing Scheme
Quasi-implicit Time Advancing + Incremental
Start of a time increment
  Update support, w, N, and N' of SPs
  Start of the Newton-Raphson loop
    Update support, w, N, and N' of SPs
    Calculate strain, stress, etc. of SPs
    Calculate {Df int.}, {Df ext.}, and [K ]
    If || {Df ext.} - {Df int.}|| is small, break
    Solve [K ] {du } = {Df ext.} - {Df int.}
    Update {Du } ={Du } + {du }
    Update disp. of Nodes and SPs
  Update all physical variables
Equalibrium
Equation
Stable!!

## Slide 20: Incremental Equilibrium Equation
Virtual Work Equation in Rate Form without body force term

## Slide 21: Incremental Equilibrium Equation
Linearize
time derivative
Galerkin
discretization

## Slide 22: Table of Contents
Introduction and Objective
Formulation of Floating Stress-Point Integration (FSPI) Meshfree Method
Examples of Analysis
Conclusion

## Slide 23: Elastic Constitutive Equation
Common isotropic elastic model
Exactly the same as the default elastic model of ABAQUS/Standard.

## Slide 24: Patch Test
Quasi-static, Plane strain
Young's modulus: 1GPa, Poisson's ratio: 0.3
Displacement BC for every external nodes
：node
：stress point (SP)
Irregularly
-arranged

## Slide 25: Patch Test
Distribution of Misess Stress

## Slide 26: Patch Test
Mises stress at the final state is between 177.187 and 177.189 MPa.
Error of Mises stress is less than 0.2%.

## Slide 27: Elastic Cantilever Bending
Quasi-static, Plane strain
Young's modulus: 1GPa, Poisson's ratio: 0.3
The num. of nodes: 335, The num of SPs: 1450
400kN concentrated force to downward dir.
Compared to ABAQUS/Standard with 8-node 2nd-order quadrilateral elements (CPE8)

## Slide 28: Elastic Cantilever Bending
Distributions of Mises Stress
FSPI Meshfree ABAQUS/Standard

## Slide 29: Elastic Cantilever Bending
Displacement error is less than 0.3%.
Proposing method is shear locking free.

## Slide 30: Elastic Uniaxial Compression
Quasi-static, Plane strain
Young's modulus: 1GPa, Poisson's ratio: 0.45
The num. of nodes: 528, The num. of SPs: 2455
0.4m displacement to downward dir.
Compared to ABAQUS/ Standard with 3-node 1st-order triangular elements (CPE3)

## Slide 31: Elastic Uniaxial Compression
FSPI Meshfree ABAQUS/Standard
ABAQUS stopped at 0.28m displacement.

## Slide 32: Elastic Uniaxial Compression
3% displacement difference at 0.28m disp.
Treatments at the concave corner is necessary.

## Slide 33: Elasto-plastic Constitutive Equation
Classical elasto-plastic model with
  von Mises yield criterion
  associated flow rule
  isotropic hardening rule
Exactly the same as the default elasto-plastic model of ABAQUS/Standard.
Young's Modulus: 1GPa
Poisson's Ratio: 0.3

## Slide 34: Elasto-plastic Cantilever Bending
Quasi-static, Plane strain
Num. of Nodes: 335, Num of SPs: 1450
Oscillating vertical disp. enforced
Compared to ABAQUS/Standard with 8-node 2nd-order quadrilateral elements (CPE8)

## Slide 35: Elasto-plastic Cantilever Bending
FSPI Meshfree ABAQUS/Standard
Distributions of Equivalent Plastic Strain

## Slide 36: Elasto-plastic Cantilever Bending
Time-history of Vertical Reaction Force at the Bounding Node
Error of reaction force is less than 0.3%
No shear locking in elasto-plastic case too

## Slide 37: Elasto-plastic Uniaxial Tensioning
Quasi-static, Plane strain
1m disp. of upper side
The num. of nodes: 1800, The num of SPs: 5400
Compared to ABAQUS /Standard with 3-node 1st-order triangular elements (CPE3)

## Slide 38: Elasto-plastic Uniaxial Tensioning
FSPI Meshfree ABAQUS/Standard
Distributions of
Equivalent Plastic Stain

## Slide 39: Elasto-plastic Uniaxial Tensioning
Progress of Horizontal Displacement at the Lower-right Node
Error of displacement is less than 0.2%.
Enough accuracy in plastic large deformation

## Slide 40: Elasto-plastic Bar Shearing
Quasi-static, Plane strain
Shearing with 1.5m vertical displacement
The num. of nodes: 1052, The num. of SPs: 3156
Compared to ABAQUS/Standard with 3-node 1st-order triangular elements (CPE3)

## Slide 41: Elasto-plastic Bar Shearing
FSPI
Meshfree
ABAQUS /Standard
Distributions of
Equivalent Plastic Strain

## Slide 42: Table of Contents
Introduction and Objective
Formulation of Floating Stress-Point Integration (FSPI) Meshfree Method
Examples of Analysis
Conclusion

## Slide 43: Summary and Future Work
Summary
  A new meshfree method for large deformation analysis, FSPI meshfree method, was proposed.
  Its formulation based on robust MLS and incremental equilibrium equation was presented.
  A patch test and a few examples of elasto-plastic large deformation analysis were performed to verify that the method had enough accuracy.
Future Work
  solve contact problems
  feature of adding node and stress-point
  adaptive FEM based on the incremental equilibrium equation

## Slide 44
Appendix

## Slide 45: List of Specifications
 | Standard FEM | FSPI Meshfree
Node | Yes | Yes
Element | Yes | No (only for initialization)
Evaluation Point | Integration Point | Stress-Point
Shape Func. | in Element | with MLS
Integration Correction | Unnecessary | Scaling Type Correction
Time-advancing | Fully implicit | Quasi-implicit (shape func. etc. are explicit)
Reference Configuration | Updated/Total Lagrange | Updated Lagrange
Equilibrium Eq. | Standard Form | Incremental Form

## Slide 46: Update Equations for SP variables
Location Ix
Corresponding volume IV
Vinitial: Initial Corresponding Volume F: Deformation Gradient
x: Current Posiotion, S: Set of Nodes in Support, f: Shape Function

## Slide 47: MLS with Total/Updated Lagrange
In case of wide horizontal stretch:
Before
After (Total- Lagrange)
After (Updated-
Lagrange)
Support is widened
↓
Unsuitable for very large deformation and rezoning
Support is dynamic circles
↓
Having nodes to start/stop relation
(Same as adaptive FEM)