## Slide 1: Application of Preconditioned Iterative Methods in Selective Smoothed Finite Element Methods with Tetrahedral Elements for Nearly Incompressible Materials
Yuki ONISHI Tokyo Institute of Technology, Japan
----------------------------------------------------------- ----------------------------------------------------------- F-bar

## Slide 2: Motivation & Background
Motivation
  We want to analyze severe large deformation of nearly incompressible solids accurately and stably! (Target: automobile tire, thermal nanoimprint, etc.)
Background
  Finite elements are distorted in a short time, thereby resulting in convergence failure.
Mesh rezoning method is indispensable.
Mold
Polymer
1m

## Slide 3: Our First Result in Advance
What we want to do:
Static
Implicit
Large deformation
Mesh rezoning with locking-free T4 elements

## Slide 4: Conventional Methods
Higher order elements: ✗ Not volumetric locking free; Unstable in contact analysis; No good in large deformation due to intermediate nodes.
EAS method: ✗ Unstable due to spurious zero-energy modes.
B-bar, F-bar and selective integration method: ✗ Not applicable to T4 mesh directly.
F-bar patch method: ✗ Difficult to construct good patches. Not shear locking free.
u/p hybrid (mixed) elements: ✗ No sufficient formulation for T4 mesh so far. (There are almost acceptable hybrid elements such as C3D4H of ABAQUS.)
Smoothed finite element method (S-FEM): ? Unknown potential (since 2009~). It’s worth trying!!

## Slide 5: Various Types of S-FEMs
Basic type
  Node-based S-FEM (NS-FEM)
  Face-based S-FEM (FS-FEM)
  Edge-based S-FEM (ES-FEM)
Selective type
  Selective FS/NS-FEM
  Selective ES/NS-FEM
Bubble-enhanced or Hat-enhanced type
  bFS-FEM, hFS-FEM
  bES-FEM, hES-FEM
F-bar type
  F-barES-FEM
NEW
✗ Volumetric Locking
✗ Spurious zero-energy
✗ Limitation of constitutive model, Pressure oscillation, Corner locking
? Unknown potential
✗ Pressure oscillation, Short-lasting

## Slide 6: Objective
Develop a new S-FEM, F-barES-FEM-T4, by combining F-bar method and ES-FEM-T4 for large deformation problems of nearly incompressible solids
Table of Body Contents
Method: Formulation of F-barES-FEM-T4 & Introduction of AMG-GMRES
Result: Verification of F-barES-FEM-T4
Discussion: Application of AMG-GMRES to F-barES-FEM-T4
Summary

## Slide 7
Method
Formulation of F-barES-FEM-T4 & Introduction of AMG-GMRES
(F-barES-FEM-T3 in 2D is explained for simplicity.)

## Slide 8: Quick Review of F-bar Method
Algorithm
Calculate deformation gradient at the element center, and then make the relative volume change .
Calculate deformation gradient at each gauss point as usual, and then make ) .
Modify at each gauss point as
.
Use to calculate the stress, nodal force and so on.
F-bar method is used to avoid volumetric locking in Q4 or H8 elements. Yet, it cannot avoid shear locking.
For quadrilateral (Q4) or hexahedral (H8) elements

## Slide 9: Quick Review of ES-FEM
Algorithm:
Calculate the deformation gradient at each element as usual.
Distribute the deformation gradient to the connecting edges with area weights to make at each edge.
Use to calculate the stress, nodal force and so on.
ES-FEM is used to avoid shear locking in T3 or T4 elements. Yet, it cannot avoid volumetric locking.
For triangular (T3) or tetrahedral (T4) elements.

## Slide 10: Outline of F-barES-FEM
Concept
is given by ES-FEM.
is given by Cyclic Smoothing (detailed later).
is calculated in the manner of F-bar method:
.
Combination of F-bar method and ES-FEM

## Slide 11: Outline of F-barES-FEM
Brief Formulation
Calculateas usual.
Smooth at nodes and get.
Smooth at elements and get.
Repeat 2. and 3. as necessary ( times).
Smooth at edges to make .
Combine and of ES-FEM as
.
Cyclic Smoothing of
Hereafter, F-barES-FEM-T4 with -time cyclic smoothing is called “F-barES-FEM-T4()”.
( layers of ~)

## Slide 12: Quick Introduction of AMG-GMRES
Preconditioner: AMG
  Algebraic Multi-Grid.
  A framework of stationary iterative methods.
  Mainly comprised of 3 parts: Smoothing, Restriction, and Prolongation.
  Can be used as a preconditioner.
Solver: GMRES
  Generalized Minimal RESidual.
  One of the non-stationary iterative methods.
  Usually used with a restart parameter r as GMRES(r).

## Slide 13
Result
Verification of F-barES-FEM-T4
(Analyses without mesh rezoning are presented for pure verification.)

## Slide 14: #1: Compression of a Block
Outline
Arruda-Boyce hyperelastic material ().
Applying pressure on ¼ of the top face.
Compared to ABAQUS C3D4H with the same unstructured tetra mesh.
Load

## Slide 15: #1: Compression of a Block
Pressure Distribution
ABAQUS C3D4H
F-bar ES-FEM-
T4(2)
Early stage Middle stage Later stage

## Slide 16: #1: Compression of a Block
Pressure Distribution
Early stage Middle stage Later stage
F-bar ES-FEM- T4(3)
F-bar ES-FEM- T4(4)
In case the Poisson’s ratio is 0.499, F-barES-FEM-T4(2) or later resolves the pressure oscillation issue.

## Slide 17: #2: Compression of 1/8 Cylinder
Outline
Neo-Hookean hyperelastic material ().
Enforced displacement is applied to the top surface.
Compared to ABAQUS C3D4H with the same unstructured tetra mesh.

## Slide 18: #2: Compression of 1/8 Cylinder
Result of F-bar ES-FEM(2)
50% nominal compression
Almost smooth
pressure
distribution is obtained
except just around the rim.

## Slide 19: #2: Compression of 1/8 Cylinder
Pressure Distribution
ABAQUS C3D4H
F-bar ES-FEM-
T4(3)
F-bar ES-FEM-
T4(4)
F-bar ES-FEM- T4(2)
F-barES-FEM-T4 with a sufficient cyclic smoothing also resolves the corner locking issue.

## Slide 20
Discussion
Application of AMG-GMRES to F-barES-FEM-T4

## Slide 21: Characteristics of [K] in F-barES-FEM-T4
 No increase in DOF. (No Lagrange multiplier. No static condensation.)
 Positive definite.
✗ Wide in bandwidth… In case of standard unstructured T4 meshes, ✗ Ill-posed… (Relatively large condition number.)
Method | Approx. Bandwidth | Approx. Ratio
Standard FEM-T4 | 40 | 1
F-barES-FEM(1) | 390 | x10
F-barES-FEM(2) | 860 | x20
F-barES-FEM(3) | 1580 | x40
F-barES-FEM(4) | 2600 | x65

## Slide 22: Condition Number of [K]
Condition number vs. Initial Poisson’s ratio
Increase in c does not improve the ill-posedness of [K] much… Application of iterative solver for [K] is difficult.
In one case of cantilever bending with neo Hookean model

## Slide 23: Capability of AMG-GMRES
AMG-GMRES with
  5th order Chebyshev polynomial smoother
  Jacobi smoothed aggregation
  Restart number is fixed at
  # of V-cycle is varied between 10 and 30.
# of V-cycle = 10 |  | ✗ | ✗
# of V-cycle = 20 |  |  | ✗
# of V-cycle = 30 |  |  | 
# of V-cycle = 10 |  | ✗ | ✗
# of V-cycle = 20 |  |  | ✗
# of V-cycle = 30 |  |  | 
Increase in the # of V-cycles improves the condition number of [K] for GMRES and helps the convergence of AMG-GMRES.

## Slide 24: CPU Time of AMG-GMRES
CPU time is compared between
  Direct solver: MKL PARDISO of Intel
  Iterative solver: AMG-GMRES(150) (Note that it is not tuned yet...)
Currently,
  AMG-GMRES is faster only when .
  MKL PARDISO is faster when .
This is due to the increase of cost for many V-cycles and also the lack of tuning of AMG-GMRES.
  In point of speed, F-barES-FEM-T4 needs some improvements. e.g.) finding a good sparse approximation of , generalization of , and so on.

## Slide 25
Summary

## Slide 26: Benefits and Drawbacks of F-barES-FEM-T4
Benefits
  Locking-free with 1st -order tetra meshes. No difficulty in severe strain or contact analysis.
  No increase in DOF. No need of static condensation; Easy extension to dynamic explicit analysis.
  Suppression of pressure oscillation in nearly incompressible materials.
  Suppression of corner locking.
Drawbacks
  ✗ Increase in bandwidth of the exact tangent stiffness . ✗ Relatively large condition number of .
  F-barES-FEM-T4 has excellent accuracy but needs some effort for speed-up.

## Slide 27: Conclusion
A new FE formulation named “F-barES-FEM-T4” is proposed.
F-barES-FEM-T4 combines the F-bar method and ES-FEM-T4.
Owing to the cyclic smoothing, F-barES-FEM-T4 is locking-free and also pressure oscillation-free with no increase in DOF.
Only one drawback of F-barES-FEM-T4 is the decrease of calculation speed due to the increase in bandwidth of , which is our future work to solve.
Thank you for your kind attention! I appreciate your questions and comments in easy and slow English!

## Slide 28
Appendix

## Slide 29: Characteristics of FEM-T4s
 | Shear & Volumetric Locking | Zero- Energy Mode | Dev/Vol Coupled Material | Pressure Oscillation | Corner Locking | Severe Strain
Standard FEM-T4 | ✗ |  |  | ✗ | ✗ | 
ABAQUS C3D4H |  |  |  | ✗ | ✗ | 
Selective S-FEM-T4 |  |  | ✗ | ✗ | ✗ | 
bES-FEM-T4 hES-FEM-T4 |  |  |  | ✗ | ✗ | ✗
F-bar ES-FEM-T4 |  |  |  | * | * | 
) when the num. of cyclic smoothings is sufficiently large.
*

## Slide 30: #2: Compression of 1/8 Cylinder
Result of F-bar ES-FEM(2)
Smooth
Mises stress
distribution is obtained
except just around the rim.
50% nominal compression

## Slide 31: #0: Bending of a Cantilever
Outline
Neo-Hookean hyperelastic material with a constant (=1 GPa) and various s so that the initial Poisson’s ratios are 0.49 and 0.499.
Two types of tetra meshes: structured and unstructured.
Compared to ABAQUS C3D4H (1st-order hybrid tetrahedral element).
Dead Load

## Slide 32: #0: Bending of a Cantilever
Pressure Distributions
ABAQUS C3D4H
F-bar ES-FEM- T4(1)
Structured Mesh

## Slide 33: #0: Bending of a Cantilever
Pressure Distributions
F-bar ES-FEM-
T4(2)
F-bar ES-FEM- T4(3)
Increase in the number of cyclic smoothing () makes stronger suppression of pressure oscillation.
Structured Mesh

## Slide 34: #0: Bending of a Cantilever
Pressure Distributions
ABAQUS C3D4H
F-bar ES-FEM- T4(1)
Unstructured Mesh

## Slide 35: #0: Bending of a Cantilever
Pressure Distributions
F-bar ES-FEM-
T4(3)
F-bar ES-FEM-
T4(2)
No mesh dependency is observed.
Unstructured Mesh