## Slide 1: A Locking-free and Pressure-checker-free Smoothed Finite Element Method for Nearly Incompressible Solids using Tetrahedral Meshing
Yuki ONISHI (Institute of Science Tokyo, Japan)

## Slide 2: Motivation
What we want to do:
Solve severe large deformation analyses with finite elements.
Treat complex geometries with tetrahedral (TET) meshes.
Consider nearly incompressible materials .
Support contact problems.
Handle auto re-meshing.
Current situation:
There is no triple-threat TET element that satisfies
Accuracy,
Compute time, and
Robustness in large deformation.
Rubber
Hot Plastic/Glass
Ductile Metal

## Slide 3: Issues in Accuracy and Their Solutions
Issues in Accuracy | Solutions
Shear Locking | 2nd-order, ES-FEM, NS-FEM, etc.
Volumetric Locking | , SRI, B-bar, F-bar, NS-FEM, etc.
Reaction Force Oscillation | 1st-order, Modified 2nd-order, etc.
Pressure Checkerboarding | None! (No absolute solution)
Issues in Accuracy | Solutions
Shear Locking | 2nd-order, ES-FEM, NS-FEM, etc.
Volumetric Locking | 
Reaction Force Oscillation | 1st-order, Modified 2nd-order, etc.
Pressure Checkerboarding | None! (No absolute solution)
Typical reaction force oscillation (ABAQUS C3D10)
Related to Nodal Force/Disp.
Related to Stress/Strain
Typical pressure checkerboarding (ABAQUS C3D4)
Pressure checkerboarding is quite difficult to resolve.
S-FEMs will be detailed later.

## Slide 4: Objective
Develop a new smoothed finite element method
with 4-node tetrahedral meshes (ES-FEM-SRI-T4) to suppress pressure checkerboarding in nearly incompressible large deformation analysis.
Table of Contents
Quick Introduction to S-FEM
Method: Brief of ES-FEM-SRI-T4
Result & Discussion: Performance of ES-FEM-SRI-T4
Summary

## Slide 5: Quick Introduction to S-FEM

## Slide 6: What is S-FEM?
Smoothed finite element method (S-FEM) is an FE formulation proposed in 2006.
After 20 years of active research, practical applications are now underway in various fields.
S-FEM is one of the gradient (strain) smoothing techniques.
There are many kinds of S-FEMs depending on the scheme of smoothing.
There are a few classical S-FEMs depending on the smoothing domain.
For example, in a 2D triangular mesh:
Standard FEM
Edge-based S-FEM (ES-FEM)
Node-based S-FEM (NS-FEM)
Each colored area shows the domain for gradient smoothing.

## Slide 7: Brief of ES-FEM
Let us consider a mesh with only two 3-node triangular (T3) cells.
Calculate at each cell as usual.
Distribute each to the connecting edge with an area weight and build .
Calculate strain , Cauchy stress () and nodal internal force in each edge smoothing domain with .
As if putting a Gauss point on each edge center
etc.
Let me explain in 2D for simplicity

## Slide 8: Performance of ES-FEM
Cantilever Bending Analysis with Dead Load at the Tip Plane-Strain, Size:10x1 m,
Mises stress
Pressure
ABAQUS CPE3 (Standard FEM-T3)
ES-FEM-T3
ES-FEM-T3 gives more accurate stress/strain distributions than the standard FEM-T3 using the same mesh.

## Slide 9: Performance of ES-FEM
Cantilever Bending Analysis with Dead Load at the Tip Plane-Strain, Size:10x1 m,
Mesh Seed Size (m) | The Number of Cells
1 | 22
1/2 | 84
1/4 | 342
1/8 | 1,442
1/16 | 5,766
1/32 | 23,034
1/64 | 92,146
Converged
Converged
ES-FEM-T3 is shear locking free and thus the mesh convergence rate of displacement/force is much faster than the Standard FEM-T3.

## Slide 10: Major Issues in ES-FEM
In nearly incompressible solid, ES-FEM-T3 causes
Volumetric locking
Pressure checkerboarding
Same Cantilever Bending Analysis with Pressure
A brand-new code with a novel S-FEM formulation for nearly incompressible solids is still awaited.
ABAQUS CPE3 (Standard FEM-T3)
ES-FEM-T3

## Slide 11: Method Brief of ES-FEM-SRI-T4

## Slide 12: Brief of ES-FEM
Let us consider a mesh with only two 3-node triangular (T3) cells.
Make at each cell as usual.
At each edge, gather s of the connecting cells and average them with area weights to build .
Calculate strain , stress () and nodal internal force in each edge smoothing domain with .
As if putting a Gauss point on each edge center
Strain distribution is piecewise constant in each smoothing domain.
No shear locking.
Cannot avoid volumetric locking & pressure checkerboarding.
Let me explain in 2D for simplicity
etc.

## Slide 13: Brief of NS-FEM
Let us consider a mesh with only four 3-node triangular (T3) cells.
Make at each cell as usual.
At each node, gather s of the connecting cells and average them with area weights to build .
Calculate strain , stress () and nodal internal force in each nodal smoothing domain with .
As if putting a Gauss point on each node center
etc.
No shear/volumetric locking. Minor pressure checkerboarding.
Cannot avoid spurious low-energy modes.
Let me explain in 2D for simplicity
Strain distribution is piecewise constant in each smoothing domain.

## Slide 14: Brief of ES-FEM-SRI
(1) Calculate at each edge with ES-FEM
(3) Calculate at each cell with double strain smoothing
(5) Assemble
(2) Calculate at each edge and its contribution to
(4) Calculate at each cell and its contribution to
Selective Reduced Integration (SRI)
Let me explain in 2D for simplicity
No volumetric locking.
Less pressure checkerboarding.
Deviatoric Part
Volumetric Part
No shear locking.
Excellent accuracy in deviatoric stress.
Double strain smoothing: Strain smoothing at nodes (NS-FEM) followed by another smoothing at cells (NS-FEM-1)
Apply the selective reduced integration (SRI) to ES-FEM to handle rubber-like solids

## Slide 15: Result & Discussion Performance of ES-FEM-SRI-T4

## Slide 16: Bending of Rubber Cantilever
Outline
10 x 1 x 1 m cantilever.
Neo-Hookean hyperelastic material, .
Dead load applied to the tip node.
A large deflection analysis with m at the final state.
Compared the results of ABAQUS C3D4, ABAQUS C3D4H, and ES-FEM-SRI-T4.
Dead Load
Static Implicit

## Slide 17: Bending of Rubber Cantilever
Mises Stress Distribution at the Finial State
Static Implicit
C3D4 suffers from severe volumetric locking, whereas C3D4H has slight shear locking.
ES-FEM-SRI-T4 is locking-free and present smoother stress distributions.
ES-FEM-SRI-T4
ABAQUS C3D4H (Hybrid)
ABAQUS C3D4 (Standard FEM-T4)

## Slide 18: Bending of Rubber Cantilever
Pressure Distribution at the Finial State
Static Implicit
Only ES-FEM-SRI-T4 shows a practical pressure-checker-free result.
Inaccurate pressure leads to accuracy loss in , direction and magnitude of principal stresses, etc..
ES-FEM-SRI-T4
ABAQUS C3D4H (Hybrid)
ABAQUS C3D4 (Standard FEM-T4)

## Slide 19: Pressuring of Rubber Block
Outline
1 x 1 x 1 m block.
Arruda-Boyce hyperelastic material, GPa, .
Applying pressure on ¼ of the top face with lateral confinement.
Evaluated the result of ES-FEM-SRI-T4.
Load
Static Implicit

## Slide 20: Pressuring of Rubber Block
Mises Stress Animation of ES-FEM-SRI-T4
Static Implicit
Smooth distribution of Mises stress.
Sufficient robustness in large deformation
No major issue is found.

## Slide 21: Pressuring of Rubber Block
Pressure Animation of ES-FEM-SRI-T4
Static Implicit
No major checkerboarding.
Practical result is obtained.

## Slide 22: Tensioning of Rubber-Filler Composite
Outline
0.5 x 0.5 x 0.5 m cube (1/8 model)
Rubber: Neo-Hookean hyperelastic material
Iron Filler: Neo-Hookean hyperelastic material
Applying enforced tensioning displacement on the top face with lateral confinement.
Evaluated the result of ES-FEM-SRI-T4.
Static Implicit

## Slide 23: Tensioning of Rubber-Filler Composite
Mises Stress Animation of ES-FEM-SRI-T4
Static Implicit
Smooth distribution of Mises stress.
Sufficient robustness in large deformation
No major issue is found.

## Slide 24: Tensioning of Rubber-Filler Composite
Pressure Animation of ES-FEM-SRI-T4
Static Implicit
No checkerboarding in the steel part.
No major checkerboarding in the rubber part.
Practical result is obtained.

## Slide 25: Summary

## Slide 26: Summary
A new smoothed finite element method (ES-FEM-SRI-T4) was proposed.
Despite using 4-node tetrahedral (T4) meshes, ES-FEM-SRI-T4 is not only locking-free but also pressure-checker-free for solids with Poisson’s ratio up to 0.49.
The pressure-checker-free property is especially important in the implicit analyses with pressure-dependent constitutive models (e.g., Gurson, Drucker-Prager, Cam-Clay, etc.), in which cosmetic post-smoothing in pressure does not work.
ES-FEM-SRI-T4 is ready for practical use!

## Slide 27: Applications of S-FEM-T4 in Our Lab
Large deformation solid mechanics (still in academic research)
Dynamic Explicit Static Implicit Viscous Implicit
Electrostatic (already in commercial use)
Carbody Electro Deposition
Thank you for your kind attention!

## Slide 28: Appendix

## Slide 29: Discussion on CPU Time of ES-FEM-SRI-T4
Since the most of CPU time for implicit analyses is spent solving the stiffness equation (i.e., ), the size of matrix () directly affects the CPU time.
S-FEMs are purely displacement-based FE formulations; thus, the matrix size () is exactly identical to that of FEM-T4.
The bandwidth of of ES-FEM-SRI-T4 is x4.3 wider than that of FEM-T4.
Formulation | Bandwidth of | v.s. FEM-T4 Ratio
FEM-T4 | 14 nodes x 3 DOF | 1
FEM-T10 | 28 nodes x 3 DOF | 2.0
ES-FEM-T4 | 45 nodes x 3 DOF | 3.2
NS-FEM-T4, SelectiveES/NS-FEM, ES-FEM-SRI-T4 | 60 nodes x 3 DOF | 4.3
Formulation |  | v.s. FEM-T4 Ratio
FEM-T4 | 14 nodes x 3 DOF | 1
FEM-T10 | 28 nodes x 3 DOF | 2.0
ES-FEM-T4 | 45 nodes x 3 DOF | 3.2
NS-FEM-T4, SelectiveES/NS-FEM, ES-FEM-SRI-T4 | 60 nodes x 3 DOF | 4.3
For the same mesh, S-FEM-T4s are slower than FEM-T4. But, for the same accuracy, S-FEM-T4s are faster than FEM-T4.

## Slide 30: What are the benefits of S-FEM?
Super-linear mesh convergence rate with T4 mesh. (Almost same rate as 2nd-order elements with T4 mesh.)
Shear locking free with ES-FEM-T4. (Good accuracy with T4 mesh in solid mechanics.)
Volumetric locking free with NS-FEM-T4. (Key technique for rubber-like nearly incompressible solid.)
Little accuracy loss with skewed meshes. (No problem with complex geometry or severe deformation.)
No increase in DOF. (Purely displacement-based formulation. )
Easy to code. (keeping away from mixed variational formulations.)
T4: 4-node Tetrahedra
T4
Search
S-FEM wiki
G.R. Liu et al., CRC Press
S-FEM is a powerful method suitable for practical industrial applications.