## Slide 1: Performance Evaluation of F-barES-FEM-T4 in Dynamic Analysis
Ryoya IIDA, Yuki ONISHI, Kenji AMAYA
Tokyo Institute of Technology, Japan

## Slide 2: Background
In the previous talk, F-bar aided edge-based smoothed finite element method with tetrahedral elements (F-barES-FEM-T4) is presented.
Characteristics of F-barES-FEM-T4 in static analysis are as follows.
✔ Excellent accuracy,
✔ No increase in DOF,
✗ Increase in bandwidth of stiffness matrix.

## Slide 3: Characteristics (1 of 2)
Our method shows excellent accuracy in static problems!
ABAQUS C3D4H
✗ pressure oscillation
✔ Excellent accuracy
F-barES-FEM-T4(3)
# of cyclic smoothings

## Slide 4: Characteristics (2 of 2)
✔ No increase in DOF
F-barES-FEM-T4 is a purely displacement-based formulation.
In contrast to the u/p hybrid formulations, F-barES-FEM-T4 can be directly applied to explicit dynamics.
✗ Increase in bandwidth of stiffness matrix
F-barES-FEM-T4 takes longer time to solve the equilibrium equations…
In explicit dynamics, however, we don’t need to solve them!
F-barES-FEM-T4 would be suitable
for explicit dynamics of rubber-like materials!

## Slide 5: Objective
Objective
Evaluate the performance of F-barES-FEM-T4
in explicit dynamics for rubber-like materials.
Table of Body Contents
Methods: Quick introduction of F-barES-FEM-T4
Results & Discussion: A few verification analyses
Summary

## Slide 6: Methods
Notes: Then we will explain our proposed method

## Slide 7: Procedure of F-barES-FEM (1 of 2)
ES-FEM
Deformation gradient of each edge, is derived as

## Slide 8: Procedure of F-barES-FEM (2 of 2)
Each part of is calculated as
(1)
Isovolumetric part
Smoothing the value of adjacent elements.
↓
The same manner as
ES-FEM
(1)Calculating node’s value by smoothing
the value of adjacent elements
(2)Calculating elements’ value by smoothing
the value of adjacent nodes
(3)Repeating (1) and (2) a few times
(2)
Volumetric part

## Slide 9: Advantages of F-barES-FEM
Like a ES-FEM
1. Shear locking free
Like a NS-FEM
2. Little pressure oscillation
3. Volumetric locking free with the aid of F-bar method
Isovolumetric part
Volumetric part
This formulation is designed to have 3 advantages.

## Slide 10: Equation to solve
Equation of Motion
,
where
Time integration
Velocity Verlet method (2nd order simplectic integrator)
-matrix of ES-FEM
Stress derived from
Defenition of in the same fashion as F-bar method

## Slide 11: Result & Discussion

## Slide 12: #1 Bending of a cantilever
Dynamic explicit analysis.
Neo-Hookean material Initial Young’s modulus: 6.0 MPa, Initial Poisson’s ratio: 0.499, Density: 10000 kg/m3.
Compare the results of F-barES-FEM-T4, Standard T4 (ABAQUS/Explicit C3D4) and Selective H8 (ABAQUS/Explicit C3D8) elements.

## Slide 13: Time history of deformed shapes
F-barES-FEM-T4(2)
(Proposed method)
✔ No pressure oscillation
✔ No locking
ABAQUS/Explicit C3D4
(Standard T4 element)
✗ Pressure oscillation
✗ Locking
ABAQUS/Explicit C3D8
(Selective H8 element)
Reference
Proposed method suppresses pressure oscillation and locking!

## Slide 14: Deformed shapes and pressure distributions
ABAQUS/Explicit C3D8
(Selective H8 element)
Reference
F-barES-FEM-T4(2)
(Proposed method)
at s
Proposed method is comparable to Selective H8 element!

## Slide 15: Deformed shapes and pressure distributions
ABAQUS/Explicit C3D4
Standard T4 element
✗Pressure oscillation and locking
Proposed method shows far better solutions than Standard T4!
at s
F-barES-FEM-T4(2)
(Proposed method)

## Slide 16: Time history of displacement
Proposed method shows good result without locking.
The accuracy of displacement does not depend on the number of cyclic smoothings.
Standard T4
Proposed &
Reference

## Slide 17: Time history of total energy
Energy divergences arise in earlier stage…
Increasing the number of smoothings suppresses the speed of divergence.

## Slide 18: #2 Natural mode of a cantilever
Modal analysis.
Linear elastic material Young’s modulus: 6.0 MPa, Poisson’s ratio: 0.499, Density: 10000 kg/m3.
Compare the results of F-barES-FEM-T4, Standard T4 (ABAQUS/Explicit C3D4) and Selective H8 (ABAQUS/Explicit C3D8) elements.
Same initial elasticity as the previous example

## Slide 19: Natural frequencies of each mode
Natural frequencies of our method agree with those of reference !
Standard T4
Proposed &
Reference

## Slide 20: Natural mode shapes
5th
30th
ABAQUS C3D8
(Reference)
F-barES-FEM(2)
(Proposed method)
Mode shapes also agree with the reference solutions.

## Slide 21: Distributions of natural frequencies
Some natural frequencies have small imaginary part…
Imag.
Part
Increasing the number of smoothings makes
the frequencies close to real numbers.

## Slide 22: Cause of energy divergence
Due to the adoption of F-bar method, the stiffness matrix becomes asymmetric.
Equation of Motion:
Asymmetric stiffness matrix gives rise to imaginary part of natural frequencies and instability in dynamic problem.
As shown before, increasing the number of smoothings suppress the energy divergence speed.
asymmetric
Our method is restricted to short-term analysis (such as impact analysis) with a sufficient number of smoothings.

## Slide 23: #3 Swinging of Bunny Ears
Outline
Iron ears: , Neo-Hookean, No cyclic smoothing.
Rubber body: , Neo-Hookean, 1 cycle of smoothing.
Compared to ABAQUS/Explicit C3D4. No Hex mesh available!
Iron Ears
Rubber Body
Fixed
Initial Velocity of Iron Ears

## Slide 24: Time histories of deformed shapes
F-barES-FEM-T4
(Proposed method)
ABAQUS/Explicit C3D4
(Standard T4 element)
✗ Pressure oscillation ✗ Locking
✔ No pressure oscillation ✔ No locking
Proposed method seems be representing not pressure oscillations but pressure waves.

## Slide 25: Deformed shapes and sign of pressure
Our method represents pressure waves correctly!
F-barES-FEM-T4
(Proposed method)
✔ Pressure waves
ABAQUS/Explicit C3D4
(Standard T4 element)
In an early stage
✗ Pressure oscillations

## Slide 26: Deformed shapes and sign of pressure
ABAQUS/Explicit C3D4
(Standard T4 element)
✗ Pressure oscillation in iron ears
A rubber parts is a “bad apple” when Standard T4 elements are used.
In a later stage
F-barES-FEM-T4
(Proposed method)
✔ No pressure oscillation in iron ears
It should be noted that a presence of rubber spoils over all accuracy of the analysis with Standard T4 elements.

## Slide 27: Summary

## Slide 28: Summary
F-barES-FEM-T4 was applied to dynamic explicit analysis.
A few examples of analysis revealed that our method has excellent accuracy on relatively short-term problems.
On long-term problems, however, our method is unstable because of complex natural frequencies.
Improvement for the long-term stability is our future work.
Thank you for your kind attention.
Notes: まとめです
今後は接触を考慮した問題への拡張を中心に、研究を進めていくつもりです。

## Slide 29
Appendix

## Slide 30: Propagation of 1D pressure wave
Outline
Small deformation analysis.
Linear elastic material, Young’s modulus: 200 GPa, Poisson’s ratio: 0.0, Density: 8000 kg/m3.
Results of F-barES-FEM(0), (1), (2), and (3) are compared to the analysical solution.

## Slide 31: Propagation of 1D pressure wave
Results

## Slide 32: Velocity Verlet Method
Algorithm
Calculate the next displacement as
.
Calculate the next acceleration as
.
Calculate the next velocity as
Characteristics
2nd order symplectic scheme in time.
Less energy divergence.

## Slide 33: Cause of energy divergence
Due to the adoption of F-bar method, the stiffness matrix becomes asymmetric and thus the dynamic system turns to unstable.
Equation of natural vibration, , derives an eigen equation, , which has asymmetric left-hand side matrix.
Some of eigen frequencies could be complex numbers.
When an angular frequency （）, the time variation of the th mode is
Divergent term!