## Slide 1: A Locking-free and Pressure Oscillation-free Elasto-plastic Large Deformation Analysis using F-barES-FEM-T4
Yuki ONISHI, Ryoya IIDA, Kenji AMAYA Tokyo Institute of Technology, Japan

## Slide 2: Motivation
Motivation
  We want to accurately and stably analyze severe large deformation of solids in any shape with finite elements.
Issues
  Only tetra mesh is available for arbitrary body shape.
  The standard 1st / 2nd order tetrahedral element are poor especially when incompressibility is present. Also, all the other advanced tetrahedral elements (e.g., C3D4H, C3D10H, C3D10MH in ABAQUS) have some issues:
    shear/volumetric locking,
    pressure oscillation, etc.
  Researches on FE formulations for 1st order tetra (T4) are still active especially for rubber-like or elasto-plastic materials.

## Slide 3: An Example for Rubber-like Material
Material: neo-Hookean hyperelastic,
1st order hybrid T4 (C3D4H)  No shear/volumetric locking
✗ Pressure oscillation
✗ Corner locking
2nd order modified hybrid T10 (C3D10MH)
 No shear/volumetric locking
✗ Low interpolation accuracy ✗ Early convergence failure
# of Nodes is almost the same.
Pressure
Pressure

## Slide 4: An Example for Rubber-like Material
Material: neo-Hookean hyperelastic,
F-barES-FEM-T4 (a new type of smoothed finite element method (S-FEM))  No shear/volumetric locking
 Less pressure oscillation  Less corner locking
F-barES-FEM-T4 has excellent accuracy on rubber-like materials.
How about it on elasto-plastic materials?
# of Nodes is exactly the same as the C3D4H case.
Note: F-barES-FEM-T4 is a pure displacement-based formulation.

## Slide 5: Objective
Apply the new type of S-FEM, F-barES-FEM-T4, to large deformation problems of elasto-plastic materials.
Table of Body Contents
Methods: Quick introduction of F-barES-FEM-T4
Results: A few example analyses
Summary
Note: Elasto-plastic materials may have near incompressibility after yielding.

## Slide 6
Methods
Quick introduction of F-barES-FEM-T4 (F-barES-FEM-T3 in 2D is explained for simplicity.)

## Slide 7: Quick Review of Node-based S-FEM (NS-FEM)
Algorithm:
Calculate the deformation gradient at each element, , as usual.
Distribute s to the connecting nodes with area weights to make at each node.
Use s to calculate the stress, nodal force and so on.
NS-FEM avoids shear & volumetric locking in T3/T4 elements and also alleviates pressure oscillation. Yet, it suffers from spurious low-energy modes, corner locking and minor pressure oscillation….
For triangular (T3) or tetrahedral (T4) elements.

## Slide 8: Quick Review of Edge-based S-FEM (ES-FEM)
Algorithm:
Calculate the deformation gradient at each element, , as usual.
Distribute s to the connecting edges with area weights to make at each edge.
Use s to calculate the stress, nodal force and so on.
ES-FEM avoids shear locking in T3/T4 elements. Yet, it suffers from volumetric locking, corner locking, and major pressure oscillation…
For triangular (T3) or tetrahedral (T4) elements.

## Slide 9: Quick Introduction of F-barES-FEM
Concept: combine ES-FEM and NS-FEM using F-bar method
Outlline
is given by ES-FEM.
is given by cyclically applied NS-FEM.
is calculated in the manner of F-bar method:
.

## Slide 10: Outline of F-barES-FEM
Brief Formulation
Calculateas usual.
Smooth at nodes and get.
Smooth at elements and get.
Repeat 2. and 3. as necessary ( times).
Smooth at edges to make .
Combine and of ES-FEM as
.
Cyclic Smoothing of
Hereafter, F-barES-FEM-T4 with cycles of smoothing is called “F-barES-FEM-T4()”.
( layers of ~)
A kind of low-pass filter for

## Slide 11
Results
A few example analyses

## Slide 12: Bending of Elasto-Plastic Spanner
P. 12
Outline
2 faces are perfectly constrained.
Pressure is applied to a side part of the spanner.
Compared to ABAQUS C3D4H with the same unstructured T4 mesh.
Fixed
Pressure
Elasto-plastic material:
Hencky elasticity with and .
Isotropic von Mises yield criterion with and (constant).
8.5 k nodes & 33 k elems.

## Slide 13: Bending of Elasto-Plastic Spanner
Equivalent Plastic Strain
Distributions of
equivalent plastic strain
are about the same.
ABAQUS C3D4H
F-barES-FEM-T4

## Slide 14: Bending of Elasto-Plastic Spanner
F-barES-FEM-T4
Pressure
ABAQUS C3D4H
ABAQUS C3D4H suffers from pressure oscillation even in a small deformation elasto-plastic case.
Checkerboard patterns here.
Smooth distribution here.

## Slide 15: Shearing & Tensioning of Elasto-Plastic Bar
P. 15
Outline
Blue face is perfectly constrained.
Red face is constrained in plane and pressed down.
Compared to ABAQUS C3D4H with the same unstructured T4 mesh.
Elasto-plastic material:
Hencky elasticity with and .
Isotropic von Mises yield criterion with and (constant).
1.2 k nodes & 4.8 k elems.

## Slide 16: Shearing & Tensioning of Elasto-Plastic Bar
Result of F-bar ES-FEM (Equiv. Plastic Strain)

## Slide 17: Shearing & Tensioning of Elasto-Plastic Bar
P. 17
Equivalent Plastic Strain
F-barES-FEM-T4
ABAQUS C3D4H
There is minor oscillation.
Smooth distribution.

## Slide 18: Shearing & Tensioning of Elasto-Plastic Bar
P. 18
Equivalent Plastic Strain
F-barES-FEM-T4
ABAQUS C3D4H
Accuracy of equivalent plastic strain seems no much different.

## Slide 19: Shearing & Tensioning of Elasto-Plastic Bar
P. 19
Pressure
F-barES-FEM-T4
ABAQUS C3D4H
Smooth distribution.
There is major oscillation.

## Slide 20: Shearing & Tensioning of Elasto-Plastic Bar
P. 20
Pressure
Accuracy of pressure is quite different due to the pressure oscillation of ABAQUS C3D4H.
F-barES-FEM-T4
ABAQUS C3D4H

## Slide 21: Twist of Rubber/Aluminium Composite Plate
Outline
Bottom face is perfectly constrained.
Top face is constrained in the plane and twisted 360 deg. around the vertical axis.
Calculated by F-barES-FEM-T4 only.
Multiple s at edges on the material interface.
3 k nodes & 14 k elems.
[Aluminium]
Hencky elasticity: ， .
Isotropic von Mises plasticity: ， (const.),
[Rubber]
Neo-Hook Hyperelasticity: ,

## Slide 22: Twist of Rubber/Aluminium Composite Plate
Seems valid.
Result of F-bar ES-FEM-T4 Equivalent Plastic Strain

## Slide 23: Twist of Rubber/Aluminium Composite Plate
No pressure oscillation.
Result of F-bar ES-FEM-T4 Pressure

## Slide 24: Twist of Rubber/Aluminium Composite Plate
Discontinuous .
No strain smoothing across material interfaces.
Result of
F-bar ES-FEM-T4 Deformation Gradient

## Slide 25
Summary

## Slide 26: Benefits and Drawbacks of F-barES-FEM-T4
Benefits
  Locking-free with 1st order tetra meshes.
  No difficulty in severe strain or contact analysis.
  No increase in DOF.
  Purely displacement-based formulation.
  No restriction of material constitutive model. Pressure dependent models are acceptable.
  Less corner locking and pressure oscillation.
Drawbacks
✗ The more cyclic smoothing necessitates the more CPU time due to the wider bandwidth.

## Slide 27: FYI
If you are interested in F-barES-FEM-T4, please refer to the following paper:
“F-bar aided edge-based smoothed finite element method using tetrahedral elements for finite deformation analysis of nearly incompressible solids, International Journal for Numerical Methods in Engineering (IJNME), Jul. 2016.
Thank you for your kind attention!