## Slide 1: Performance Evaluation of Stabilized F-bar Aided Edge-based Smoothed Finite Element Method with Four-node Tetrahedral Elements (SymF-barES-FEM-T4) for Contact Problemｓ
Ryoya IIDA, Yuki ONISHI, Kenji AMAYA
Tokyo Institute of Technology, Japan

## Slide 2: Motivation
What we want to do:
Solve hyper large deformation analyses accurately and stably.
Treat complex geometries with tetrahedral meshes.
Consider nearly incompressible materials .
Support contact problems.
Handle auto re-meshing.
Rubber
Plastic/Glass
Metal

## Slide 3: Issue in Ordinary T10 Elements
Issue
When we use 10-node tetrahedral (T10) mesh, the number of nodes gets much larger to express complex shapes without element kink.
 Skewed T4 ✗Kinked T10
Possible Solutions
Robust T10 element (method in the previous talk)
Accurate T4 element (method in THIS talk)

## Slide 4: Our T4 Method for Static Problems
Our group has proposed a new S-FEM-T4 formulation, F-barES-FEM-T4, detailed later.
ABAQUS C3D4H
✗ pressure oscillation
F-barES-FEM-T4(3)
# of cyclic smoothings
F-barES-FEM-T4 shows excellent accuracy in static problems!

## Slide 5: Our T4 Method for Dynamic Problems
Our group has proposed another S-FEM-T4 formulation, SymF-barES-FEM-T4, detailed later.
SymF-barES-FEM-T4 shows good accuracy and stability in dynamic problems!
SymF-barES-FEM-T4(2)
ABAQUS/Explicit C3D8 (H8-SRI element)
F-barES-FEM-T4(2) ✗ Energy divergence

## Slide 6: Objective
FAQ How about the stability in dynamic contact problems?
Objective
To evaluate the stability of SymF-barES-FEM-T4 in explicit dynamics with contact.
Table of Body Contents
Methods: Quick introduction of SymF-barES-FEM-T4
Results & Discussion: A few verification analyses
Summary

## Slide 7: Methods
Notes: Then we will explain our proposed method

## Slide 8: Formulation of F-barES-FEM (1 of 2)
ES-FEM
Deformation gradient of each edge () is derived as

## Slide 9: Formulation of F-barES-FEM (2 of 2)
Each part of is calculated as follows.
(1)
Isovolumetric part
Smoothing Fs of adjacent elements at each edge.
↓
The same manner as
ES-FEM.
(1)Calculating node’s F by smoothing Fs of adjacent elements.
(2)Calculating elements’ F by smoothing Fs of adjacent nodes.
(3)Repeating (1) and (2) a few times. (This is named “cyclic smoothing”.)
(2)
Volumetric part
NS-FEM
NS-FEM-1
ES-FEM

## Slide 10: Advantages of F-barES-FEM
Like ES-FEM
1. Shear locking free
Like NS-FEM
2. Little pressure oscillation
3. Volumetric locking free with the aid of F-bar method
Isovolumetric part
Volumetric part
This formulation is designed to have 3 advantages.

## Slide 11: Issue of F-barES-FEM in Dynamics
Issue: Energy divergence occurs.
Due to the adoption of F-bar method, the stiffness system is no longer symmetric.
In F-barES-FEM, the internal force vector is calculated as
Combination of , and (mixture of and ) causes asymmetry of the dynamic system.
-matrix of ES-FEM
Stress derived from
Defenition of in the same fashion as the original F-bar method
Volume of ES-FEM

## Slide 12: Formulation of SymF-barES-FEM
In SymF-barES-FEM, the derivation of the internal force vector is slightly modified.
F-barES-FEM:
SymF-barES-FEM:
The replacements ( to & to) help to preserve the symmetry of the stiffness system.
-matrix
derived from
Stress
derived from
Volume
derived as

## Slide 13: Result & Discussion

## Slide 14: Twist of Rubber Cantilever
Outline
No contact.
Dynamic explicit analysis.
Twisting initial velocity fields:
Neo-Hookean material: Initial Young’s modulus: 17.0 MPa, Initial Poisson’s ratio: 0.49, Density: 1100 kg/m3.
Compare the results of SymF-barES-FEM-T4, F-barES-FEM-T4, and ABAQUS/Explicit C3D8.

## Slide 15: Twist of Rubber Cantilever
Comparison of Pressure and Shape
F-barES-FEM-T4(2)
✔ No pressure oscillation
✔ No locking
✗ Energy divergence
ABAQUS/Explicit C3D8
(H8-SRI)
SymF-barES-FEM-T4(2)
✔ Less pressure oscillation
✔ No locking
✔ No energy divergence

## Slide 16: Twist of Rubber Cantilever
Comparison of total energy
SymF-barES-FEM-T4 can suppress energy divergence!
F-barES-FEM-T4
SymF-barES-FEM-T4
(60,000 timesteps)
(Kinetic + Strain)

## Slide 17: Time history of displacement
Comparison of axial displacement at a tip node
Standard T4
Proposed
Proposed methods can show good results as H8-SRI.

## Slide 18: Twist of Rubber Cantilever
Effect of the number of cyclic smoothing
F-barES-FEM-T4
SymF-barES-FEM-T4
#cyclic
smoothings
1
2
3
1
2
3
In SymF-barES-FEM-T4, the increase in cyclic smoothings no longer improves the accuracy, unlike F-barES-FEM-T4.

## Slide 19: Impact of Rubber Bullet
Outline
¼ bullet made of nearly incompressible rubber.
Impacting the bullet to a slippery rigid wall with a uniform initial velocity.
Compared to ABAQUS/Explicit C3D4 with a same mesh.

## Slide 20: Impact of Rubber Bullet
Mises stress Anim. of SymF-bar ES-FEM -T4(1)

## Slide 21: Impact of Rubber Bullet
Comparison of pressure dist. in a contact state
SymF-barES-FEM-T4(1)
ABAQUS/Explicit C3D4
F-barES-FEM-T4(1)
Our methods represent far better pressure distributions without major checkerboarding.

## Slide 22: Impact of Rubber Bullet
Comparison of total energy over time
(Kinetic + Strain)
SymF-barES-FEM-T4
F-barES-FEM-T4
SymF-barES-FEM-T4 conserves the total energy even in a contact problem.

## Slide 23: Impact of Rubber Bunny
Outline
A Stanford bunny made of nearly incompressible rubber (neo-Hookean hyperelastic body with.)
Impacting the bunny to a slippery rigid wall with a uniform initial velocity.
Compared to ABAQUS/Explicit C3D4 with a same mesh.
Initial velocity
10 m/s (uniform)
Rigid Wall
contact condition:
free-slip & free-separation
Rubber body

## Slide 24: Impact of Rubber Bunny
Pressure sign anim.
SymF-barES-FEM-T4(1)
✔ Less pressure checker ✔ No locking ✔ No energy divergence
ABAQUS/Explicit C3D4
✗Pressrue checkerboard ✗Locking ✔ No energy divergence
F-barES-FEM-T4(1)
✔ No pressure checker ✔ No locking ✗ Energy divergence

## Slide 25: Impact of Rubber Bunny
Pressure sign dist. right after contact
Our methods can capture the pressure wave propagation in a complex body.
SymF-barES-FEM-T4(1)
ABAQUS/Explicit C3D4
F-barES-FEM-T4(1)
✔ Pressure wave propagation
✗Pressure checkerboard

## Slide 26: Impact of Rubber Bunny
Comparison of total energy over time
SymF-barES-FEM-T4 conserves the total energy in a contact problem even with complex shapes.
SymF-barES-FEM-T4
F-barES-FEM-T4
(150,000 timesteps)
(Kinetil + Strain)

## Slide 27: Summary

## Slide 28: Summary
The accuracy and stability of SymF-barES-FEM-T4 in dynamic explicit contact problems was evaluated.
SymF-barES-FEM-T4 realizes ✔ Less pressure oscillation ✔ No locking ✔ No energy divergence
Further improvement for perfect suppression of pressure oscillation is our future work.
Thank you for your kind attention.
Notes: まとめです
今後は接触を考慮した問題への拡張を中心に、研究を進めていくつもりです。

## Slide 29
Appendix

## Slide 30: Benefits and Drawbacks of F-barES-FEM-T4
Drawbacks
✗ Slow speed of calculation.
In explicit analyses, [K] is unnecessary; yet, CPU Time increases gradually with the # of cyclic smoothings.
Chart: In case of 6864 DOF & 10000 timesteps
| 0 | 1 | 2 | 3
列3 | 108 | 292 | 684 | 1402
(x1)
(x2.7)
(x6.3)
(x13.1)